## Slide 1
ERCOT Load Resource Price and 4CP Response
Carl L Raish
Principal Load Profiling and Modeling
Wholesale Market Working Group – Oct 25, 2021

## Slide 2: Methodology
  Identify Load Resources active 1Jun 2019 – 30 Sep 2020
  Determine unique ESIIDs
    366 Resources
    332 ESIIDs
  Load Resource ESIIDs reported on RT or DA Indexed pricing for 2019 and 2020 ERCOT Surveys
    201 ESIIDs
  Analysis focused day-by-day on Load Resources with no AS Responsibility in 12:30 pm – 8:00 pm window.
  Initial analysis targeted
    Load Resources associated with ESIIDs on Indexed Real Time Pricing.
    Response on high price days (≥$800) and on 4CP/Near CP days.
    ‘Eyeball’ baselines used.
    Load Resource telemetry data

## Slide 3: Days with High Real-Time Prices
  Threshold $800
  Does not include 4CP/NearCP days (EEA1 days also not included)
  7 days in analysis window.
    55 – 85 Load Resources
    16 Aug 2019 only day with response
      Only day with high prices in DA and RT
      DA prices ~$2,300, RT Prices ~$800
      ~100 MW of response
    22 Sep 2019
      RT prices ~$2,500, DA prices ~$53
      No response
    5 Oct 2019
      RT prices ~$1,200, DA prices ~$163
      No response

## Slide 4: High Day-Ahead and Real-Time Price Day

## Slide 5: Days with High Day-Ahead Prices
  Threshold $800
  Does not include 4CP/NearCP days (EEA1 days also not included)
  7 days in analysis window.
    16 Aug 2019 only day with response
      Only day with high prices in DA and RT
      DA prices ~$2,300, RT Prices ~$800
      ~100 MW of response
    19 Aug 2019
      RT prices ~$57, DA prices ~$1,000
      ~150 MW of response
    20 Aug 2019
      RT prices ~$59, DA prices ~$1,200
      ~50 MW of response
    14 Aug 2020
      RT prices ~$252, DA prices ~$1,200
      ~50 MW of response

## Slide 6: High Day-Ahead Price Day

## Slide 7: 4CP/NearCP Days no High Prices
  21 days in analysis window.
  14 days with response
  52 – 96 Load Resources
    Response ranged from 25 – 150 MW
    Average ~70 MW

## Slide 8: High Day-Ahead Price Day

## Slide 9: Questions?
ON
OFF
craish@ercot.com 512/248-3876