## Slide 1: Wholesale Market Working Group Report to WMS
David Detelich
Murali Sithuraj
November 3, 2021
From October 25 WMWG Meeting

## Slide 2: 2022 ERCOT Ancillary Service Methodology
ERCOT presented the proposed methodology for setting the 2022 AS quantities – second look at WMWG
Regulation
  ERCOT is not proposing any change to the methodology used to compute the minimum Regulation Service requirements for 2022.
  Methodology with the adjustment tables do result in increasing regulation quantities – solar is the main driver
RRS
  A floor of 2800 MW will be applied to RRS quantities during the peak.
  The additional RRS has directly impact ERCOT’s PRC during the peak hours.
  This change has effectively helped increase ERCOT’s operating margin during hours with higher net load.

## Slide 3: 2022 ERCOT Ancillary Service Methodology
Non-Spin
  ERCOT is proposing the following changes to the methodology used to compute minimum Non-Spin requirements in 2022
    Update the hourly net load forecast uncertainty calculation to use
      the 6 Hours-Ahead net load forecast instead of 3 hour ahead, and
      the highest 5-min net load within the hour
    Change percentile coverage to vary between 85th and 95th . The applicable coverage for any hour will continue to be based on risk of net load up ramp in the hour
    Build a table that tracks historical intra-day variations in thermal resource availabilities due to Forced Outages and use it to incrementally increase Non-Spin quantities.
  ERCOT will continue the practice of monitoring the weather near Real Time and may procure up to an additional 1,000 MW of Non-Spin for Operating Hours that are identified as having an increased potential of high forecast variability that may cause a higher net load during these hours.
  The resulting quantities are similar to current 6,500 MW method, some hours exceed that level

## Slide 4: AS Methodology Discussion
Comment: The extra RRS across the peak hours does not appear to have a reliability reason
  Inertia is the highest during those hours
  Would like to see additional explanation or formula
Comment to end the extra 1,000 MW of NSRS process
  Use of the Mid Term Load Forecast with the adjusted process described last month adds a bias already
  Difficult for loads to hedge
ERCOT noted that Beginning November 1, 2021, ERCOT has updated the Forecast Variability process to Current Day + 2

## Slide 5: Load Forecast Performance
No report presented this month
WMWG request metrics on the amount and frequency of over forecast
In addition, would like a review of the data in the Advance Action Notice Planning Assessment Input Details for the October events
  For 10/25 AAN102521_R3
    Load forecast – 61,518 Actual – 61,482
    Solar forecast – 3,529 Actual – 6,737
    Wind forecast – 5,516 Actual – 6,170

## Slide 6: Impact of Growth in Wind and Solar on Net Load
ERCOT presented analysis for information
  With increase in installed solar capacities, there are substantial changes in net load that can be expected (specially in Winter, Spring and late Summer).
    Seasonal and temporal variations in net load ramp direction and magnitude can be expected.
    Larger net load up ramps are likely to be correlated with sunset hours.
  ERCOT grid and market operations are expected to (and/or should) evolve to support these changes in net load.
Comments from participants
  Use of RUC could have adverse impacts
  Batteries could alleviate the issue
  ORDC should commit capacity

## Slide 7: RUC Deployment Issues
Review of the RUC deployment to self committed unit
Appears to be a timing issue between the RUC snapshot and the updating of the COP
Current process requires the QSE to Opt Out of RUC if they still want the self commitment
Updating the snapshot after the RUC study completes would require system changes and have settlement impacts
Market participant will review with ERCOT

## Slide 8: Review of Reliability Deployment Process Proxy Bid Curve
This concerns NPRR1093 and protocol section 6.5.7.3.1, Determination of Real-Time On-Line Reliability Deployment Price Adder
  Add the deployed MW from Load Resources other than Controllable Load Resources to GTBD linearly ramped over the ten-minute ramp period. …ERCOT shall generate a linear bid curve defined by a price/quantity pair of $300/MWh for the first MW of Load Resources deployed and a price/quantity pair of $700/MWh for the last MW of Load Resources deployed in each SCED execution. …The TAC shall review the validity of the prices for the bid curve at least annually.
ERCOT presented a method for this review based on review of days with high prices that are not 4CP or Near CP days
Results were inconclusive
Seeking input from WMS

## Slide 9: NPRR 1091 Changes to Address Market Impacts of Additional Non-Spin Procurement
Participants would prefer to wait for the PUC market reforms that are expected to include revisions to the ORDC by the new year
Propose NPRR remains tabled

## Slide 10: NPRR 1092 Remove RUC Offer Floor
Participants would prefer to wait for the PUC market reforms that are expected to include revisions to the ORDC by the new year
Propose NPRR remains tabled
ERCOT and the IMM will collaborate on analysis that may help justify a particular offer floor

## Slide 11: NPRR1084 Improvements to Reporting of Resource Outages and Derates
ERCOT discussed their recently filed comments
Some feedback is that these revisions will require additional personnel at power plants to manage the process
Propose this remain tabled for market participants to formulate comments
Will take up again at next meeting

## Slide 12: Remaining Key Topic Concepts (KTCs) from Battery Energy Storage Task Force (BESTF)
ERCOT presented a recommendation on KTC 15.3 Switchable Energy Storage Resources (SWESRs)
This KTC Recommendation contains recommendations in three areas
  Reliability and Operations
  Legal/Policy
  Settlements
Revisions to protocols and procedures as well as input from the PUC will be required
ERCOT requests feedback before they recommend that WMS send to TAC for approval

## Slide 13: Next meeting
To be rescheduled from November 16 - GCPA empowering Women conference
Any questions?