## Slide 1
OBDRR037/038 and HCAP Parameter Update - Alignment with Recent PUCT Direction on the ORDC Design
Dave Maggio
Director, Market Design & Analytics
TAC
January 31, 2022
ERCOT Public

## Slide 2: Agenda
This presentation largely covers information that was provided in Market Notices issued on December 7, 2021 (M-A120721-01 General) and December 17, 2021 (M-A121721-01 General)
Overview
Items for Technical Advisory Committee (TAC) vote today:
  Update to the HCAP per paragraph (1) of Protocol Section 4.4.11, System-Wide Offer Caps
  Other Binding Document Revision Request (OBDRR) 037 to change the Power Balance Penalty Curve and other language that references the $9,000/MWh HCAP value
  OBDRR038 to change the minimum contingency level (“X”) used in the ORDC process
Questions

## Slide 3: Overview
At open meetings in December, the Public Utility Commission of Texas (PUCT) approved the following items, both effective January 1, 2022:
  An amendment to §25.505 of the PUCT Substantive Rules, lowering the HCAP from its current value of $9,000/MWh to a value of $5,000/MWh
  An order directing ERCOT to change the minimum contingency level used in the ORDC process from 2,000 MW to 3,000 MW.
Additionally, parameters driven by HCAP, or the effective System-Wide Offer Cap (SWCAP) more generally, were also changed on January 1, 2022, including:
  The Value of Lost Load (VOLL);
  The Ancillary Service Penalty Factors for the Day-Ahead Market (DAM) and Supplemental Ancillary Service Market (SASM);
  The Power Balance Penalty Curve used in Security-Constrained Economic Dispatch (SCED); and
  Proxy Energy Offer Curves.

## Slide 4: Update to the HCAP
Per Protocol Section 4.4.11(1), the HCAP parameter is updated within the ERCOT Protocols through recommendation by TAC and approval by the ERCOT Board.
As discussed in the table above, ERCOT is seeking TAC’s recommendation of the update at the meeting today.

## Slide 5: Update to the Power Balance Penalty Curve
The Power Balance Penalty Curve was also updated to meet the purpose of the PUCT’s rule change.
Effective January 1, 2022, the curve was changed to be capped at $5,001/MWh, i.e., HCAP plus $1/MWh.
  This effectively means that the price on the curve will be at its maximum value at MW violations above 100 MW.
  This is equivalent to how the Power Balance Penalty Curve is adjusted when the Low System-Wide Offer Cap (LCAP) is in effect.
ERCOT has also sponsored OBDRR037 to bring the Power Balance Penalty Curve language into alignment with the PUCT’s rule change.
  Filed on December 14, 2021
  Related language clean-up is also addressed within the OBDRR.
  Like the HCAP update, ERCOT is seeking TAC’s approval of the OBDRR.

## Slide 6: Illustration of the updated Power Balance Penalty Curve when HCAP is in effect
Chart: MW Violation
| 0 | 5 | 5 | 10 | 10 | 20 | 20 | 30 | 30 | 40 | 40 | 50 | 50 | 100 | 100 | 150 | 150 | 200 | 200 | 3000
Current | 250 | 250 | 300 | 300 | 400 | 400 | 500 | 500 | 1000 | 1000 | 2250 | 2250 | 4500 | 4500 | 6000 | 6000 | 7500 | 7500 | 9001 | 9001
Effective 1/1/22 | 250 | 250 | 300 | 300 | 400 | 400 | 500 | 500 | 1000 | 1000 | 2250 | 2250 | 4500 | 4500 | 5001 | 5001 | 5001 | 5001 | 5001 | 5001

## Slide 7: Update to the ORDC Minimum Contingency Level
Effective January 1, 2022, the minimum contingency level used in the ORDC calculations was changed from 2,000 MW to 3,000 MW.
ERCOT has also sponsored OBDRR038 to bring the related ORDC methodology language into alignment with the PUCT’s order.
  Filed on December 22, 2021
  Again, ERCOT is seeking TAC’s approval of the OBDRR.

## Slide 8: Questions