## Slide 1
Demand Response CLR Settled at a Nodal Price
Sai Moorty
Market Design
CMWG
January 24th, 2022

## Slide 2: Phase I - Enhancements to the Current Market Design
From Project 52373 Blueprint (12-6-21)
Demand Response. Adopt changes that allow for more targeted demand response to increase utilization of load resources for grid reliability.
• Next steps:
Pursue market modifications and technical measures to improve transparency of price signals for load resources, such as changing demand response pricing from zonal to locational marginal pricing (LMP).

## Slide 3: Scope of this presentation
This slide deck is focused on settlement using nodal pricing for ERCOT registered Demand Response type Controllable Load Resources (CLRs).
Focus on single site CLR
  Recent trend in large numbers and MWs of crypto/data center/electrolyzer type loads seeking interconnection
  The size (MW) and price responsive capability of these loads
  Nodal price response aligns with proper congestion management
Not Discussing:
Energy Storage Resource (ESR) charging side modeled as ESR-CLR
Aggregated Load Resources (ALR)
Other Load Resources

## Slide 4: Discussion Items
Resource Node Settlement Point for CLR settled at nodal pricing is required
  Is there a minimum MW size requirement ?
  Impacts of increased number of Resource Nodes to CRR and MMS run time performance
    Will have high probability of reusing existing Resource Node at a site where CLR is co-located with Generation Resources
    ERCOT will be investigating impact of increasing the number of Settlement Points
    CRR has approximately 650 biddable settlement points. Vendor claims run time performance will be satisfactory up till approximately 800 biddable settlement points.
    CRR run time performance is also impacted by number of transactions
    DAM has approximately 770 settlement points (including Combined Cycle Logical Resource Nodes). No known issues as of now with increase in Resource Nodes
    DAM run time performance also impacted by number of offers/bids (mainly PTPs)
  CLR will participate with a Bid to Buy in DAM and Resource Specific Energy Bids will be co-optimized with Resource Specific AS Offers

## Slide 5: Discussion Items
The site meter configuration is crucial if there is any combination of Generation Resource, Load, CLR, ESR at a given site.
For example, if a site has both CLR and other Load – two options
    Site must have metering setup to separately measure consumption of other Load for Load Zone Price Settlement and consumption of CLR load for Nodal Price Settlement ?
    Entire site is settled at a Nodal Price and site requires only one meter ?
      Minimum size requirement for CLR ? Any issues for a scenario where, at a site, there is 10 MW of other Load and 1 MW of CLR load and the entire site is settled at a Nodal Price?
CLR co-located with Generation Resource/Energy Storage Resource at a Gen Site
  Design approach :
    Enable CLR and GR/ESR to offer full capacity to market (SCED, DAM, SASM)
    Settlements to ensure “No Harm Done” to other Market Participants
      Under normal operations, Settlements at this site should not result in uplift to other market participants
      Net Settlements ($) for this site is same as if the CLR and GR/ESR were at separate sites and the settlements ($) for these separate sites were netted

## Slide 6: Discussion Items
Outage Co-ordination/Approval
  Load Resources do not have to enter outages into the outage scheduler
  Load Resource status of OUT does not mean zero MW consumption
  With new types of loads (crypto) registered as CLR – what changes to: outage approval process?
    Should approval of transmission outages consider that a CLR has a helpful shift factor to potential overloads and since it is curtailable, the outage can be approved?
  If there is a large MW amount of these new types of loads, is there a change required to the TO Firm Load Shed Obligation determination?
    Issue is not a nodal vs zonal pricing issue but related to the new types of load (crypto/data center/electrolyzer)

## Slide 7: Preliminary Analysis
More details to be presented at next meeting
CLR co-located with Generation Resource/ Energy Storage Resource at a Gen Site
  To meet the design approach of enabling full capacity of GR/ESR and CLR co-located at a given gen site and to also ensure that “No Harm Done” to other Market Participants:
  For a site with only POI meters, the settlement will involve two meter prices for each meter
    15-minute net Base Point (only positive net BP = BP of GR/ESR minus BP of CLR) weighted Meter price for the Gen Channel of the POI meters
    15-minute net Base Point (only positive net BP = BP of CLR minus BP of GR/ESR) weighted Meter price for the Load Channel of the POI meters
    Gen Channel Settlement = Gen Channel MWh * Gen Channel meter price
    Load Channel Settlement = Load Channel MWh * Load Channel meter price
    RTMG used in Settlements (AS Imbalance, RUC, MRA, VSS, Emergency, Switchable Generation, Securitization, etc.) cannot be based on meter read MWh and GSPLIT – use average telemetered netMW instead?