## Slide 1
Annual Review of the Market Impacts of Reliability Unit Commitments
Analysis of 2021
Dave Maggio
Director, Market Design & Analytics
TAC
January 31, 2022
ERCOT Public

## Slide 2: Protocol Language
5.8 Annual RUC Reporting Requirement
(1) ERCOT shall report to the Technical Advisory Committee (TAC), each January, an assessment of market impacts and Settlements for the aggregate Reliability Unit Commitment (RUC) activity, delineated by type of RUC instruction as follows:
RUC instructions issued for Ancillary Service shortages (failure to sufficiently procure one or more Ancillary Service markets in the Day-Ahead Market (DAM) or subsequent Supplemental Ancillary Service Markets (SASMs));
RUC instructions issued for irresolvable transmission system constraints;
RUC instructions issued in anticipation of extreme cold weather/startup failures;
RUC instructions issued for capacity;
RUC instructions issued for system inertia; and
A summary of RUC Settlements;
(i) RUC charges associated with RUC Make-Whole Amount Total per RUC, as defined in Section 5.7.4.1, RUC Capacity-Short Charge; and
(ii) RUC Shortfall Total, as defined in Section 5.7.4.1.1, Capacity Shortfall Ratio Share.

## Slide 3: RUC-Instructed Resource-Hours in 2021
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, partial hour instructions, or otherwise not dispatchable by SCED.
 | Total | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  | 
Total Count | 4,052.0 | 1,252.0 | 2,800.0
Effective Resource-Hours* |  |  | 
Total Count | 3,853.1 | 1,205.1 | 2,648.0
Average LSL | 66.0 | 80.1 | 59.6
Average LDL | 89.9 | 151.4 | 61.8
Average BP | 95.8 | 169.2 | 62.3
Average HSL | 253.5 | 234.2 | 262.2

## Slide 4: RUC Instruction Reasons
3,853.1 effective RUC Resource-hours in 2021.
  159.5 Resource-hours (4.1%) for local thermal congestion or voltage concerns.
  3,693.6 Resource-hours (95.9%) for capacity concerns, among which:
    274 Resource-hours (7.1%) during the period of Winter Storm Uri.
      These are largely associated with the Department of Energy order regarding emissions limitations.
    3,361 Resource-hours (87.2%) occurred in the latter part of the year starting in June.
There were no Resource-hours committed for Ancillary Service shortages, system inertia, or startup failures.
1,205.1 effective Resource-hours (31%) were successfully bought back.
  This value is higher than last year (13% bought back in 2020).
  Included in this value are 18.1 effective Resource-hours (4.7% of total) where the Resource was DAM-committed.

## Slide 5: RUC-Instructed Effective Resource-Hours 2018 - 2021

## Slide 6: RUC-Instructed Resource Dispatch above LDL
When Resources did not successfully opt out, there were 45.7 Resource-hours when the Resource was dispatched above its LDL.
  For 1 of these Resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 44.7 of these Resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
    For 34.8 of these Resource-hours, the RUC-instructed Resource was mitigated.
    For 6.7 of these Resource-hours, the RUC-instructed Resource was not mitigated and had been DAM-committed, and the hours were treated as a RUC opt out.
    The remaining Resource-hours are associated with a RUC for additional capacity.

## Slide 7: Reliability Deployment Price Adders
Month of 2021 | Total RTORDPA Time (Hours) | Time-weighted Average RTORDPA ($/MWh)
Jan | 5.0 | 0.39
Feb | 112.0 | 5,003.26
Mar | 12.6 | 0.21
Apr | 8.0 | 0.56
May | 0.0 | 0.00
Jun | 71.1 | 6.42
Jul | 263.7 | 6.24
Aug | 121.7 | 3.22
Sep | 174.7 | 1.19
Oct | 214.9 | 7.73
Nov | 79.4 | 2.29
Dec | 7.0 | 3.17

## Slide 8: RUC Make-Whole and Claw Back 2018 - 2021
$5.246M in Make-Whole paid out. $15.39 uplifted to Load.

## Slide 9: Conclusions
In 2021, 4,052 instructed RUC Resource-hours resulted in 3,853.1 effective RUC Resource-hours.
  As compared to 224 and 220.1 for all of 2020, respectively.
  31.3% of effective resource-hours were bought back.
The total RUC make-whole amount was ~$5.25M.
  Almost exclusively covered through capacity-short charges.
The total RUC claw back charge amount was ~$3.11M.

## Slide 10: Appendix

## Slide 11: RUC-Instructed Effective Resource-Hours by Opt Out Status*
Month | 2018 | 2019 | 2020 | 2021
Jan | 46 | 0 | 3 | 5
Feb | 0 | 0 | 12 | 5
Mar | 0 | 8 | 1 | 5
Apr | 3 | 16 | 0 | 8
May | 333 | 59 | 0 | 0
Jun | 0 | 15 | 0 | 248
Jul | 0 | 0 | 21 | 968
Aug | 15 | 0 | 151 | 378
Sep | 4 | 8 | 0 | 339
Oct | 11 | 34 | 0 | 573
Nov | 50 | 4 | 3 | 107
Dec | 14 | 1 | 0 | 11
Month | 2018 | 2019 | 2020 | 2021
Jan | 0 | 0 | 0 | 0
Feb | 0 | 11 | 0 | 269
Mar | 0 | 0 | 0 | 24
Apr | 0 | 6 | 0 | 63
May | 40 | 13 | 6 | 0
Jun | 21 | 0 | 0 | 89
Jul | 4 | 0 | 11 | 229
Aug | 28 | 8 | 8 | 203
Sep | 16 | 19 | 0 | 139
Oct | 15 | 0 | 4 | 102
Nov | 12 | 0 | 0 | 73
Dec | 2 | 0 | 0 | 14
Did Not Opt Out
Opted Out
* Effective Resource-hours rounded to nearest whole number

## Slide 12: RUC Make-Whole and Claw Back 2018-2019
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2018 | 2019 | 2018 | 2019 | 2018 | 2019 | 2018 | 2019 | 2018 | 2019
Jan | -42 | 0 | 42 | 0 | 0 | 0 | 385 | 0 | 1,202 | 0
Feb | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mar | 0 | -9 | 0 | 9 | 0 | 0 | 0 | 0 | 0 | 253
Apr | 0 | -8 | 0 | 8 | 0 | 0 | 4 | 0 | 0 | 359
May | -102 | -13 | 102 | 13 | 0 | 0 | 2,372 | 108 | 2,824 | 915
Jun | 0 | -4 | 0 | 4 | 0 | 0 | 0 | 3 | 0 | 738
Jul | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Aug | -35 | 0 | 35 | 0 | 0 | 0 | 1 | 0 | 523 | 0
Sep | -24 | -11 | 24 | 11 | 0 | 0 | 0 | 1 | 206 | 110
Oct | -24 | -3 | 24 | 3 | 0 | 0 | 213 | 726 | 535 | 229
Nov | -381 | 0 | 381 | 0 | 0 | 0 | 79 | 49 | 977 | 0
Dec | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 15 | 0 | 0
Amounts rounded to nearest thousand. Data from most recent settlement run as of 01/07/2021.

## Slide 13: RUC Make-Whole and Claw Back 2020-2021
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2020 | 2021 | 2020 | 2021 | 2020 | 2021 | 2020 | 2021 | 2020 | 2021
Jan | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 1 | 0 | 0
Feb | 0 | 0 | 0 | 0 | 0 | 0 | 168 | 1256 | 394 | 0
Mar | 0 | -9 | 0 | 9 | 0 | 0 | 19 | 6 | 0 | 239
Apr | 0 | -19 | 0 | 19 | 0 | 0 | 0 | 0 | 0 | 263
May | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Jun | 0 | -466 | 0 | 466 | 0 | 0 | 0 | 91 | 0 | 7,004
Jul | -40 | -2,045 | 40 | 2,045 | 0 | 0 | 82 | 637 | 148 | 17,404
Aug | -356 | -865 | 356 | 865 | 0 | 0 | 210 | 59 | 2197 | 12,626
Sep | 0 | -833 | 0 | 833 | 0 | 0 | 0 | 54 | 0 | 11,812
Oct | 0 | -862 | 0 | 862 | 0 | 0 | 0 | 918 | 0 | 9,766
Nov | -8 | -61 | 8 | 61 | 0 | 0 | 0 | 89 | 140 | 1,312
Dec | 0 | -86 | 0 | 86 | 0 | 0 | 0 | 0 | 0 | 1,102
Amounts rounded to nearest thousand. Data for 2021 reflect most recent settlement run as of 01/20/2022.