## Slide 1
March 2, 2022
WMS
March 3, 2022
ROS
Nitika Mago
Implementing NPRR1093 & 1101: Load Resource Participation in Non-Spinning Reserve
  Minimum Capacity from SCED Dispatchable Resources to provide Non-Spin

## Slide 2: Background
NPRR1093 introduced protocol changes that allow Load Resources that are not controllable to provide Non-Spinning Reserve Service (Non-Spin).
NPRR1093 requires ERCOT to determine if any minimum capacity is required from SCED dispatchable Resources to provide Non-Spin. Further, any proposed limit is required to be reviewed and approved by the ERCOT Board.
ERCOT plans to implement NPRR1093 & NPRR1101 in R3 (late May, 2022). Design and code for NPRR1093 is being developed with a parameter that will account for a minimum limit from SCED dispatchable Resources for Non-Spin.
  Gray-Box for NPRR1093 and NPRR1007
  3.16 Standards for Determining Ancillary Service Quantities
  (3) The ERCOT Board shall review and approve ERCOT's methodology for determining the minimum Ancillary Service requirements, any minimum capacity required from SCED dispatchable Resources to provide Non-Spin, the minimum capacity required from Resources providing Primary Frequency Response to provide RRS and the maximum amount of RRS that can be provided by Resources capable of FFR.

## Slide 3: Introduction
Per the current protocols, SCED dispatchable Resources are able to provide Non-Spin.
With NPRR1093, Load Resources that are not controllable (Non-Controllable Load Resources or NCLRs) may also qualify to provide Non-Spin.
  An NCLR is able to offer and get awarded both RRS and Non-Spin in DAM, however in Real Time it cannot provide RRS and Non-Spin simultaneously.
  NCLR when providing Non-Spin should not have an under-frequency relay or the under-frequency relay should not be armed.
Non-Spin may be deployed when PRC is below 3,200 MW or when there isn’t sufficient capacity to meet the 30-minute net load ramp.
  For the purpose of deployment, per changes made by NPRR1101 in Nodal Protocol Section 6.5.7.6.2.3, ERCOT will create groups of ~500 MW with offline Generation Resources and NCLRs that have a Non-Spin obligation.

## Slide 4: Proposed Limit
ERCOT has some operational experience with NCLRs that provide Responsive Reserve Service via an under-frequency relay (i.e. RRS-UFR).
However, the requirements for NCLRs to provide Non-Spin are different. ERCOT will need to gain some operational experience with NCLRs that are providing Non-Spin.
As a result, ERCOT is proposing that for 2022, a minimum of 25% capacity of Non-Spin be procured from SCED dispatchable Resources.
  This would mean that, in 2022, between 635 MW and 1360 MW of Non-Spin will be procured from (online and offline) SCED dispatchable Resources, the remaining Non-Spin may come from any type of Resource that is qualified to provide Non-Spin.
This “minimum capacity of Non-Spin from SCED dispatchable Resources” will be documented in Methodology for determining Ancillary Service quantities and reviewed annually as a part of the methodology’s annual review process.
  This approach allows ERCOT to revisit this limit determination as soon as Fall of 2022 for applicability in 2023.

## Slide 5: Summary
ERCOT recommends that for 2022, the minimum amount of Non-Spin procured from SCED dispatchable Resources shall not be less than 25% of the total Non-Spin requirement.
ERCOT seeks this group’s endorsement of this proposed limit.
Following is the timeline for discussing this Ancillary Service Methodology change,
  3/2/2022: WMS
  3/3/2022: ROS
  3/30/2022: TAC
  4/12/2022: BoD