## Slide 1
March 30, 2022
TAC
Nitika Mago
Manager, Balancing Operations Planning
2022 Ancillary Service Methodology Update
  Minimum Capacity from SCED Dispatchable Resources to provide Non-Spin

## Slide 2: Introduction
NPRR1093 introduced protocol changes that allow Load Resources that are not controllable (NCLRs) to provide Non-Spinning Reserve Service (Non-Spin). Upon implementation of NPRR1093,
  NCLRs will be able to offer and get awarded both RRS and Non-Spin in DAM, however in Real Time RRS and Non-Spin cannot be provided simultaneously on the same NCLR.
  When providing Non-Spin, NCLRs should not have an under-frequency relay or the under-frequency relay should not be armed.
  For the purposes of deployment, NCLRs providing Non-Spin and Generation Resources providing offline Non-Spin may be deployed together in groups (of ~500 MW) when PRC falls below 3,200 MW or when there isn’t sufficient capacity to meet the 30-minute net load ramp.
ERCOT is required to determine if any minimum capacity is required from SCED dispatchable Resources to provide Non-Spin. Any proposed limit shall be reviewed and approved by the ERCOT Board.
ERCOT plans to implement NPRR1093 & NPRR1101 in R3 (late May, 2022). Design and code for NPRR1093 is being developed with a parameter that will account for a minimum limit from SCED dispatchable Resources for Non-Spin.
  Gray-Box for NPRR1093 and NPRR1007
  3.16 Standards for Determining Ancillary Service Quantities
  (3) The ERCOT Board shall review and approve ERCOT's methodology for determining the minimum Ancillary Service requirements, any minimum capacity required from SCED dispatchable Resources to provide Non-Spin, the minimum capacity required from Resources providing Primary Frequency Response to provide RRS and the maximum amount of RRS that can be provided by Resources capable of FFR.

## Slide 3: Recommendation on Limit for 2022
For 2022, the minimum amount of Non-Spin procured from SCED dispatchable Resources shall not be less than ERCOT’s Most Severe Single Contingency (MSSC) value. ERCOT’s current MSSC is set at 1,430 MW.
  There is no identified technical need for a limit on the minimum amount of Non-Spin to be procured from SCED dispatchable Resources. However, ERCOT recommended that a moderate limit be adopted until some operational experience with NCLRs that are providing Non-Spin can be attained.
  The Reliability and Operations Subcommittee (ROS) and Wholesale Market Subcommittee (WMS) have both proposed and endorsed a limit on the minimum amount of Non-Spin to be procured from SCED dispatchable Resources at the MSSC value.
  ERCOT does not oppose this recommendation from ROS and WMS. However, the need for a limit due to reliability reasons will diminish as more NCLRs get qualified, start providing Non-Spin in Real Time and ERCOT gains more experience with these. Hence, ERCOT expects that this limit will eventually be reduced to zero.
The proposed “minimum capacity of Non-Spin from SCED dispatchable Resources” will be documented in the Methodology for Determining Ancillary Service Requirements and reviewed annually as a part of the methodology’s annual review process.
  This approach allows ERCOT to revisit this limit determination as soon as Fall of 2022 for applicability in 2023.
  A redline version of the 2022 Ancillary Service Methodology document has been posted on today’s meeting page.
ERCOT seeks TAC’s endorsement of this proposed limit and associated 2022 Ancillary Service Methodology change.