## Slide 1
Medium-Term Load Forecast Review and Follow-up Q&A
Calvin Opheim
Load Forecasting & Analysis
SAWG
4/4/2022

## Slide 2: Agenda
Review
A Tale of Two Storms
New Reports

## Slide 3: Model Review
All internally developed forecasts (E, E1, E2, and E3) are configured exactly the same:
  Same exact model
  Same application of error correction
  Same application of tuning
The only difference is the weather forecast that is used in each forecast model

## Slide 4: Weather Forecast Sources
The following weather forecasts are available:
  European Model (Euro)
  Global Forecast System (GFS)
  Global Forecast System Ensemble (GENS)
  North American Model (NAM)
  3 vendor models

## Slide 5: Model Update
Typically, E2 uses the most extreme weather forecast for each Weather Zone for the Day Ahead
  Will result in different forecasts being used in different weather zones (i.e., Euro used in North Central while GFS is used in Coast)
Typically, E3 uses the most extreme weather forecasts for each Weather Zone for days 4+ in the future
  Will result in different forecasts being used in different weather zones (i.e., vendor 1 used in South Central while GENS is used in South)
Typically, E and E1 will use the same weather forecast for all Weather Zones
  The most extreme weather forecasts based on a single source (i.e., GFS, Euro, etc.) is used for E and E1. An example would be E using the GFS for all Weather Zones with E1 using the Euro for all Weather Zones.
  These forecasts should be considered the 50/50 forecast

## Slide 6: Model Update
On a seasonal basis or when weather patterns change, the internally developed forecasts (E, E1, E2, and E3) will be updated with a model that is appropriate for the conditions
Using a single model for all forecasts allows for:
  Better model maintenance/updates
  Clear enumeration of weather forecast impacts
  Allows multiple team members to make updates more efficiently
  Results in consistent back testing and analysis for events

## Slide 7
A Tale of Two Storms

## Slide 8: MTLF Performance – Landon
Chart: Day Ahead Forecast

## Slide 9: MTLF Performance – Late February
Chart: Day Ahead Forecast

## Slide 10: Comparing the Two Cold Events
Using the coldest weather forecast during Landon resulted in a high forecast error for February 4
The actual load exceeded the forecast even though the coldest weather forecast was being used in the selected forecast during the second cold event
Winter weather is more unpredictable, has more variability than other seasons
  Selecting the coldest weather forecast reduces the risk of the actual load exceeding the forecasted load but does not eliminate it

## Slide 11
New MTLF Reports

## Slide 12: MTLF New Reports
  Can be found https://www.ercot.com/gridinfo/load/forecast

## Slide 13
Appendix
MTLF Models

## Slide 14: MTLF Models
A3 Notes
  Uses recent history to update the model coefficients
  Prone to significantly over-forecast summer demands on very hot days
  Prone to significantly over-forecast winter demands on very cold days

## Slide 15: MTLF Models
A6 Notes
  Uses recent history to update the model coefficients
  Only uses one weather station per weather zone
  Prone to significantly over-forecast summer demands on very hot days
  Prone to significantly over-forecast winter demands on very cold days

## Slide 16: MTLF Models
E, E1, E2, E3
  Based on neural network and linear regression models with a separate model for each hour
  Common weather variables are incorporated (temperature, wind speed, cloud cover, solar irradiance, etc.) based on the particular month or season
  49 weather stations (expanded set)
  Other variables include day of week and holidays

## Slide 17: MTLF Models
M Notes
  The weighted average of the 6 other models
  Historically has shown to be the best Day Ahead forecast
  Provides a good benchmark for other models

## Slide 18: Questions?