## Slide 1: Guidance on Co-located CLR with Generation
Shams Siddiqi, Ph.D.
Crescent Power, Inc.
Representing Soluna Computing, Inc.
+1 (512) 619-3532
shams@crescentpower.net
April 6, 2022
Notes: <number>

## Slide 2: Guidance: Pursue Opt. 1 w/Netting
<number>
Large flexible load (e.g. data centers) are co-locating behind the meter (BTM) of generation resources to benefit from netting and consume renewable energy that would otherwise be curtailed
These loads can respond quickly to RTM prices but are currently not dispatched by SCED and net currently settled at Load Zone prices
Having these loads dispatched by SCED as CLR on a Nodal basis and settled on Nodal prices would greatly improve ERCOT’s ability to manage congestion and better dispatch resources and send an appropriate price signal to these flexible loads
Grid would benefit from GR and CLR providing full AS capability
However, Option 1, without additional clarification, may eliminate netting benefits and thus disincentivize such loads to be CLRs
Option 2 maintains benefits of netting at higher costs/complexity
Guidance: Pursue Option 1 while maintaining netting for TCOS and LRS cost allocation as required by current Protocol 10.3.2.3
Notes: <number>

## Slide 3: Implications of Opt 1 w/o Netting
<number>
For Load to be CLR under Option 1 without Netting implies:
  Load consuming what would’ve been wasted (curtailed) energy with no net injection into the grid would be charged full 4CP and LRS charges
  Under net injection scenarios, Load would still be charged full 4CP and LRS charges even though there is net injection at the POI. E.g., with 200MW generation and 50MW BTM Load so that 150MW is net injected into the grid, Load would still pay 4CP and LRS charges for the entire 50MW
These Loads would have strong disincentive to be CLR:
  They can provide UFR-RRS as NCLR for their full capacity and benefit from netting – no 4CP and LRS charges for netted Load
  They can passively respond to market prices without concern of following basepoints
ERCOT willing to net under Opt 2 but not under less costly Opt 1
  Then implement Opt 2. Opt 1 without netting is a waste of effort and money since these Loads co-located precisely for the benefit of netting
Guidance: Save time and money – pursue Option 1 with Netting
Notes: <number>