## Slide 1: Congestion Management Working Group
April 6, 2021
Katie Rich, Chair
Andy Nguyen, Vice Chair

## Slide 2: Nodal Settlement of Controllable Load Resources (CLRs)
ERCOT presented two options for settlement of co-located CLRs
Under Option 1, an additional meter would be added for the CLR. The injection to the grid and the CLR would be settled at a nodal price. If the site is net consumption over a 15-minute interval, aux and other load would be settled at a load zone price.
  In this scenario, CLR consumption is always measured and settled
Under Option 2, each point of interconnection (POI) meter will have two nodal prices:
  Weighted by the net of all basepoints (Generation Resource (GR) and CLR) if the net is positive
  Weighted by the net of all basepoints (GR and CLR) if the net is negative
    In this scenario, ERCOT is not involved in the settlements between the GR and CLR. ERCOT only settles the net at the POI meter.

## Slide 3: Nodal Settlement of Controllable Load Resources (CLRs)
ERCOT plans to file an NPRR selecting the Option 1 arrangement. The separate metering would result in CLRs receiving 4CP and other load charges.
  Following the CMWG meeting, ERCOT is reviewing the exclusion of 4CP charges
One stakeholder presented an alternative to ERCOT’s proposal that would continue to allow for netting of 4CP and load ratio share (LRS) cost allocation. Without this allowance, it could be argued that there’s a disincentive for loads to become CLRs.
CMWG is seeking feedback from WMS on how to proceed with this issue

## Slide 4: Panhandle GTLs
ERCOT explained that a GTC limit is determined as the lower of:
  Calculated static voltage stability limit from VSAT, or
  Table-based dynamic voltage stability limit under various outages
If the stability limit is not reached, then the output is 9999
CRRs and real-time will be based on the max dispatch

## Slide 5: NPRR 1111 and SCR 819 Implementation Plan
Intermittent Renewable Resources (IRRs) behind a binding GTC with a shift factor greater than X% on the GTC flow should not exceed their SCED basepoint when the not-to-exceed (NTE) limit is triggered
  The % threshold will vary by GTC
Implementation is expected for this fall, starting with the Panhandle and possible North Edinburg to Lobo GTCs
ERCOT will provide a report on NTE performance on a periodic basis

## Slide 6: Next Meeting: April 25

## Slide 7: Questions?