## Slide 1: Supply Analysis Working Group Update
April 4, 2022, report to WMS
Caitlin Smith, Chair
Pete Warnken, Vice Chair
Ian Haley, Returning/Acting Co-Vice Chair

## Slide 2: 1. Mid-Term Load Forecast Presentation
Review
  All internally developed forecasts (E, E1, E2, and E3) are configured exactly the same:
    Same exact model
    Same application of error correction
    Same application of tuning
  The only difference is the weather forecast that is used in each forecast model
Model Update
  On a seasonal basis or when weather patterns change, the internally developed forecasts (E, E1, E2, and E3) will be updated with a model that is appropriate for the conditions

## Slide 3: 1. Mid-Term Load Forecast Presentation
Using the coldest weather forecast during Winter Storm Landon resulted in a high forecast error for February 4
The actual load exceeded the forecast even though the coldest weather forecast was being used in the selected forecast during the second cold event
Winter weather is more unpredictable, has more variability than other seasons
  Selecting the coldest weather forecast reduces the risk of the actual load exceeding the forecasted load but does not eliminate it

## Slide 4: 2. Planned Project Success Factor Analysis
New Planned Report
  Success rates of planned generation projects
  Development cycle trends for planned projects (from initial request to operational)
  Delays to the in-service dates for planned projects
Demo
  https://public.tableau.com/app/profile/ercot.resource.adequacy/viz/ERCOTInterconnectionQueueTrends/SuccessRatesDashboard

## Slide 5: 2. Planned Project Success Factor Analysis
Success Rates and Development Cycle Analysis
  limited to projects requested between 2002 and 2018 into the ERCOT queue
  Successful projects are defined as a planned generation projects that have become operational resources
  only projects with a Full Interconnection Study (FIS) requested included

## Slide 6: 2. Planned Project Success Factor Analysis
Success Rates and Development Cycle Analysis
  limited to projects requested between 2002 and 2018 into the ERCOT queue
  Successful projects are defined as a planned generation projects that have become operational resources
  only projects with a Full Interconnection Study (FIS) requested included

## Slide 7: 3. Revamping the SARA Report
Goals
  Increase release frequency for more timely resource updates and fine-tuning of capacity forecasts and scenario assumptions for seasonal peak demand hours
  Discussing rolling monthly reporting with the PUCT
  Incorporate probabilistic risk assessment metrics
  Report multi-hour capacity reserve information to acknowledge net load risks
  Implement online interactive dashboard with data visualization tools
Next Steps
  This will be a standing discussion item at SAWG
  Would like to progress on the new report by the end of the year
  Plan is to keep releasing the seasonal SARA the rest of the year, while working on the revamp

## Slide 8: 4. Resource Adequacy Modeling Projects for 2022
ELCC:
  Overview:
    probability-based measure of the reliability benefit of a resource type (or combination of resource types) for the system during periods that have the highest risk of capacity reserve shortfalls
    estimation is based on probabilistic system simulations, the most common being Monte Carlo
    forward-looking
  Objectives:
    Use SERVM Monte Carlo simulations to do the following:
      Determine renewable and battery storage ELCC values for individual high-risk hours by season
      Conduct sensitivity analysis of ELCC values with respect to resource penetration levels, alternative technology types (solar), and grid location
    Intent is to lay the groundwork for specifying the recommended ELCC methodology for resource adequacy and planning studies
  Key Milestones:
    Project completion targeted for 7/30/2022
    Study report and SAWG presentation expected in September
    Next step is to develop Protocol revision request language to integrate into a broader NPRR on revised CDR methodologies

## Slide 9: 4. Resource Adequacy Modeling Projects for 2022
Zonal Study:
  Objectives:
    Determine the system reliability and reserve margin impacts of a zonal SERVM model as compared to the current single-zone model design
  Study Tasks
    Define load zones in the SERVM model and establish zonal transfer limits
    Convert the current ERCOT Long-Term Load Forecast into zonal load profiles and assign generating units to load zones
    Run SERVM simulations for two study years: 2023 and 2026
    Compare reliability and reserve margins results to the original single-zone model
  Key Milestones:
    Targeting study completion by mid-to-late June
    Will keep SAWG apprised of the study project
    Study report and SAWG presentation expected in July

## Slide 10: 4. Resource Adequacy Modeling Projects for 2022
NERC Probabilistic Assessment (ProbA) Study:
  Overview:
    Complements NERC’s Long Term Reliability Assessment (LTRA) by providing probabilistic reliability statistics of the forecasted resource portfolios reported in the LTRA data submissions
    ProbA conducted every even-numbered year
    Two study years: 2024, 2026
    NERC Probabilistic Assessment Working Group oversees ProbA scheduling, data submission and reporting procedures
    The study must include at least one risk scenario
  Key Milestones
    Base Case study completion in early August; PAWG peer review of Base Case results completed by 8/23/2022
    Summary of ProbA study and Base Case results to be included in NERC LTRA report to be release in mid-December 2022
    Scenario risk results due 1/11/2023 for all Assessment Areas
    ProbA Risk Scenario report released in June 2023

## Slide 11: 5. Additional Study Updates
CONE Study NPRR and Study
  Previous effort to implement a study and methodology to use when a change or update is needed to the Cost of New Entry (CONE) value paused after Winter Storm Uri
  Will resume discussing NPRR draft at next SAWG meeting
  Plan to begin study with consultant at the end of 2022
Reserve Margin Study
  Typically every even numbered year to estimate Economically Optimum and Market Equilibrium Reserve Margins (EORM and MERM), also paused after Winter Storm Uri
  ERCOT to resume process of procuring consultant for study now
  Study results expected in mid-2023

## Slide 12: 6. Annual DG Report
Major areas of DG growth in ERCOT (Total DG as of 2021= 2920 MW)
Solar PV <1 MW
Natural gas > 1 MW (co-located with load)
DGR Energy Storage> 1 MW

## Slide 13: SAWG News!!
New leadership nomination:
  Co-Vice Chair: Ian Haley, Luminant Generation
  Vote at May WMS
Next Meeting:
  May 13th
  In person + WebEx