## Slide 1
Modeling Upgrade to CIM16: Application and Data Products
Joel Koepke
May 16, 2022

## Slide 2: Overview – Upgrading from CIM10 to CIM16
ERCOT produces Network Models following CIM standards and in an XML format
  Since 2010, the Network Model Management System (NMMS) produces models using the CIM10 schema (with customizations)
  In 2021, a process was developed a post-process to translate a CIM10 models into CIM16 allowing for downstream systems to upgrade their importers
ERCOT is formalizing a project to enhance NMMS to natively produce CIM16 model files
  Reduce the need for ERCOT-specific legacy code in vendor applications
  Currently collecting vendor estimates and determining resource loading
  Tentatively scheduled to start in first half of 2023
  Project duration is estimated at 18-24 months
ERCOT will no longer produce CIM10 models after project completion

## Slide 3: Who/What is Affected?
Any processes utilizing files directly-created from NMMS will need to prepare for an updated schema.
Files include:
  MIS Secure:
    Redacted CIM Network Model - EMIL ID: NP3-450-SG
  MIS Certified:
    TSP Version of the CIM Network Model XMLs (via Citrix)
    Incremental CIM Change Requests XMLs (via Citrix/NMMS)

## Slide 4: Example Schema Change
Equipment
Power Transformer
Conducting Equipment
Transformer Winding
Terminal
CIM10
Power Transformer
Conducting Equipment
Terminal
Transformer End
CIM16
In CIM16 attributes associated to a TransformerWinding are moved to a new class called TransformerEnd