## Slide 1
Monitoring and Control
Wei Qiu
ERCOT TWG
May 19, 2022

## Slide 2: Challenges
“Loss of Monitoring and/or Control”
Lack of definitions
Different understanding

## Slide 3: Monitoring
The ability to accurately receive relevant information about the BES in Real Time and evaluate system conditions using Real-time data to assess existing (pre-Contingency) and potential (post-Contingency) operating conditions to maintain reliability of the BES. This could include, but not be limited to, the ability to evaluate:
  the current frequency
  the current status and capabilities of the generators
  the availability of generating operating reserves in real time
  the current status (open or closed) and real and reactive power flows on the BES tie-lines and facilities
  the current voltage profile
  resource balance in real time

## Slide 4: Control
The ability to take and/or direct actions to maintain the reliability of the BES in Real Time via entity actions or by issuing Operating Instructions. This could include, but not be limited to, the ability to maintain and/or adjust:
  ACE
  Current BES voltage profile using available reactive resources
  BES facility line flows and voltages within IROLs, SOLs and facility ratings using available generation dispatch, re-dispatch or load shedding as necessary
  Facility output and adjust in accordance to agree upon schedules
  Planned transmission facility outages based on current transmission system conditions and any unplanned element losses (generation or transmission) that could affect the reliability of the current plan

## Slide 5: Status
Draft -- Done
Comments -- ongoing
Approval --- NERC Event Analysis Subcommittee (EAS)
ERO Event Analysis Process Document

## Slide 6
Questions and Answers
Contact Information:
wei.qiu@nerc.net