## Slide 1
Analysis of Residential PV Performance in Competitive Area of ERCOT
Carl L Raish
Principal Load Profiling and Modeling
Wholesale Market Subcommittee – June 1, 2022

## Slide 2: Residential PV – Analysis Methodology
Find matching non-pv ESIIDs
  Same Weather Zone, Profile Type
  Stationcode, Zip Code
  Similar usage prior to PV installation
  Closest 5 with greater use and closest 5 with lower use
Baseline load for each PV ESIID is average of the load for the ten matching ESIIDs
Baseline load for non-match Esiids profiled based on average baseline of matched PV ESIIDs in same Weather Zone
PV output = Export + Load Offset (Baseline – Actual Load)
  Export and Actual metered interval data
  Baseline from matching ESIIDs

## Slide 3: Residential PV – High 2022 PV Output Day
6.5 KW of PV output per ESIID

## Slide 4: Residential PV – High 2021 PV Output Day
6.0 KW of PV output per ESIID

## Slide 5: PV Output During ERCOT 2021 Summer Peak
3.6 KW of PV output per ESIID during ERCOT peak interval
5.8 KW of peak PV output per interval

## Slide 6: PV Output During ERCOT 2021 Winter Peak
3.6 KW of PV output per ESIID during ERCOT peak interval
5.8 KW of peak PV output per interval

## Slide 7: Growth ESIIDs and Monthly Max PV Output

## Slide 8: Growth ESIIDs and Monthly Max PV Output
Based on 2020/21 growth, April 2023 totals:
~150,000 ESIIDs
~1,100 MW Annual Peak PV Output

## Slide 9: Residential PV – Performance by Install Year
PV output KWh increase:
5,000 to 13,000
PV output KW increase:
3 to 7
Baseline KWh decrease:
22,000 to 17,000

## Slide 10: Residential PV – Performance by Install Year
Import KWh decrease:
17,000 to 11,000
Export KWh increase:
3,000 to 8,000
Load Offset KWh increase:
3,000 to 5,500

## Slide 11: Residential PV – Performance by Install Year
Slope= -121 KWh/yr
Slope= -170 KWh/yr
Slope= -92 KWh/yr
Slope= -172 KWh/yr

## Slide 12: Residential PV – Performance by Install Year
Slope= -125 KWh/yr
Slope= -445 KWh/yr
Slope= -324 KWh/yr
Slope= -316 KWh/yr

## Slide 13: Questions?
ON
OFF
craish@ercot.com 512/248-3876

## Slide 14: Appendix
PV Growth by Weather Zone
PV performance 2021 by month

## Slide 15: Growth ESIIDs and Monthly Max PV Output by Wzone

## Slide 16: Growth ESIIDs and Monthly Max PV Output by Wzone

## Slide 17: Growth ESIIDs and Monthly Max PV Output by Wzone
Coast
East
FWest
NCent

## Slide 18: Growth ESIIDs and Monthly Max PV Output by Wzone
North
SCent
South
West

## Slide 19: Residential PV – Performance by Month