## Slide 1
Proposed NPRR on
CLR Settled at a Nodal Price
Sai Moorty
Market Design
WMS
June 1st, 2022

## Slide 2: Driver for Proposed NPRR
From Project 52373 Blueprint (12-6-21) - Phase I - Enhancements to the Current Market Design
Demand Response. Adopt changes that allow for more targeted demand response to increase utilization of load resources for grid reliability.
• Next steps:
Pursue market modifications and technical measures to improve transparency of price signals for load resources, such as changing demand response pricing from zonal to locational marginal pricing (LMP).

## Slide 3: Previous ERCOT Presentations
WMWG January 2021
https://www.ercot.com/files/docs/2021/01/20/Current_State_and_Expectations_for_Various_BTM_Scenarios_WMWG_012521.docx
CMWG January 2022
https://www.ercot.com/files/docs/2022/01/24/CMWG-%20Demand-Response-CLR-Nodal-Settlement-Discussion.pptx
CMWG February 2022
https://www.ercot.com/files/docs/2022/02/22/Revised_with_comments_CMWG_02212022_nodal_price_settl_of_CLR_.docx

## Slide 4: Core Objectives of this Proposed NPRR
ERCOT registered Controllable Load Resources (CLRs)*
Dispatch using Nodal Shift Factor
Settle energy consumed at Nodal price and;
Accommodate full capacity of Resources to be offered into the ERCOT Markets that are co-located behind the POI with net metering arrangement.
  Thus, eliminating the current co-ordination rules required where the Resources can only offer their excess capacity after netting to the ERCOT markets
* Not an Aggregate Load Resource (ALR)

## Slide 5: Changes Proposed by this NPRR
CLR* will be assigned a Resource Node (RN) Settlement Point
  ERCOT will monitor increase in Resource Node Settlement Points and its impact to clearing engines (CRR,DAM)
    For CLR* co-located with other Resources, it is likely that existing Resource Nodes can be used and there is no need for new Resource Nodes at such sites
  Aggregate Load Resources (ALR) will continue to use their applicable Load Zone as the Settlement Point
  * Not an Aggregate Load Resource (ALR)

## Slide 6: Changes Proposed by this NPRR
Real-Time Market (RTM) Energy Bids will be retired and replaced by Resource Specific CLR Energy Bids (move and rename RTM energy bids from Protocol Section 6 to Protocol Section 4)
  Resource Specific CLR Energy Bids are used in DAM and Real-Time Market (SCED) and have the same validation rules and submission timelines as Resource Specific RTM Energy Bids for CLRs, Aggregate Load Resources (ALRs) and the CLR component of Energy Storage Resources (ESR-CLRs)
  In the DAM, Resource Specific CLR Energy Bids will be co-optimized with Resource Specific AS Offers from CLR, ALR, or ESR-CLR
    CLR Energy Bids are always inclusive with AS Offers
    AS Offers from CLR cannot be blocky
  For distribution system connected CLR, energy and AS clearing (in DAM, RTM) follows same rules as DGR/DESR in scenarios where RN or RN electrical bus or mapped CIM Load de-energized
  Note: For ESR-CLR, their CLR Energy Bids can be updated any time (retain today’s ESR-CLR ability with RTM Energy Bids)
  Implementation for this change will attempt to minimize QSE system changes

## Slide 7: Changes Proposed by this NPRR – cont’d
Clarify in NPRR that ALL Resources (not just CLRs) in SCED shall follow UDBP  This is to mitigate potential frequency issues from fast responding Resources abruptly jumping to a new Base Point
Redefine OUTL status only for stand alone CLR
  CLR* can use OUTL status only when actual energy consumption is zero
    CLR* can update CLR Energy Bid, Ramp rates, LPC/MPC to restrict SCED Base Points (for consumption) instructions to a required value/range
  Other Load Resources including ALRs are not impacted by this change. i.e., can submit OUTL status indicating Load Resource out of the market but still consume energy
  Note: Current Nodal Protocols already state that ESR-CLR can submit a OUTL status only when the ESR is physically out of service
  * Not an Aggregate Load Resource (ALR)

## Slide 8: Changes Proposed by this NPRR – cont’d
CLR* total consumption must be separately metered from all other load and generation at a given facility
  For Real-Time Energy Imbalance Settlement, Metered energy adjusted for transmission/distribution losses and Unaccounted For Energy (UFE) shall be settled at the Nodal Meter Price (CLR Base Point weighted)
  For sites with TDSP read meters (AMI, IDR, non-EPS meters) that may have combination of zonal loads, Settlement Only Generation or Storage or CLR:
    CLR* total Load must be separately metered from all other load and generation
    ERCOT will not perform any net metering calculations for meter data coming into ERCOT systems
    Hence any netting required for appropriate settlements by ERCOT need to be performed by the TDSPs before sending the meter data to ERCOT
  * Not an Aggregate Load Resource (ALR)

## Slide 9: Changes Proposed by this NPRR – cont’d
  TDSP read meter sites (non-EPS meters)
M1
SOG/SOESR
CLR
Service Delivery Point meter
m2
CLR meter
Aux/zonal Load
M1
SOG/SOESR
CLR
m2
CLR meter
Aux/zonal Load
TDSP must transform m1 meter data before sending m1 meter data to ERCOT
No meter data transformation required before sending m1,m2 meter data to ERCOT

## Slide 10: Changes Proposal by this NPRR – cont’d
  Sites with net metering arrangement (requires EPS meters)
    Energy Settlements follows Non-WSL Charging Load template
M1
GR
CLR
POI/SDP meter
m2
CLR meter
Aux/Zonal Load

## Slide 11: Changes Proposed by this NPRR – cont’d
Transmission/Distribution Losses and UFE
  Of the total energy consumption measured by the CLR meter, only the portion of that energy supplied from the grid is adjusted for transmission/distribution losses and UFE
    For a site without net metering arrangement, the total CLR energy consumption measured by the CLR meter is adjusted for transmission/distribution losses and UFE
  Non-WSL Charging Load will also be adjusted for transmission/distribution losses and UFE in a similar manner

## Slide 12: Changes Proposed by this NPRR – cont’d
Load Ratio Share (LRS) charges/credits/obligations
  Total energy consumption of CLR* as measured by the CLR meter, appropriately adjusted for transmission/distribution losses and UFE, is added to the QSEs Real-Time Adjusted Meter Load (RTAML)
  All LRS charges/credits/obligations such as AS Obligations, RUC Capacity Short, ERCOT fee, etc. is based on the total energy consumption of CLR* as measured by the CLR meter and appropriately adjusted for transmission/distribution losses and UFE.
4CP allocation - CLR*
  Only the portion of that energy supplied from the grid, adjusted for transmission/distribution losses and UFE, is the amount (MWh) considered for 4CP TCOST allocation
    For a site without net metering arrangement, the total CLR energy consumption measured by the CLR meter, adjusted for transmission/distribution losses and UFE, is the amount (MWh) considered for 4CP TCOST allocation
  Non-WSL Charging Load will have same treatment for 4CP
* Not an Aggregate Load Resource (ALR)

## Slide 13: Changes Proposed by this NPRR – cont’d
M1
GR
CLR
POI/SDP meter
m2
CLR meter:
1. Measures total CLR consumption (from Grid+from co-located GR)
2. Total amount (MWh) settled at Nodal Price (note some of this volume is adjusted for T/D losses and UFE - not all) – Added to RTAML
3. Apart from 4CP, all other LRS charges/credits apply
Aux/Zonal Load
CLR energy consumption from grid is:
1. adjusted for T/D losses and UFE
2. included in 4CP
CLR energy consumption from co-located GR is:
1. NOT adjusted for T/D losses and UFE
2. excluded from 4CP

## Slide 14: Status Quo – No change proposed from current
CLR Bid to Buy is not mitigated in the Real-Time Market (SCED)  same as current for RTM Energy Bids  not a change introduced by this NPRR
No change to emergency settlements for CLR or Voltage Support Service

## Slide 15: Future NPRRs Related to CLRs?
Note the features in this proposed NPRR are already on the “Large Flexible Load Task Force (LFLTF)” issues list. Some other items impacting markets and settlements (also on LFLTF issues list) are:
Changes to RUC: How to model (dispatch) CLRs in RUC?
Changes to Emergency Settlements for HDL/LDL override on CLR
CLR impacts on Constraint Competitive Tests/Resource Mitigation