## Slide 1: RDPA: Flawed but Fixable
Shams Siddiqi, Ph.D.
Representing Rainbow Energy Marketing Corporation
(512) 619-3532
shams@crescentpower.net
WMS Meeting
June 1, 2022
Notes: <number>

## Slide 2: RDPA: What it is and is Not
<number>
Real-Time On-Line Reliability Deployment Price Adder (RDPA):
  Definition: A Real-Time price adder that captures the impact of reliability deployments on energy prices for each Security-Constrained Economic Dispatch (SCED) process
  RDPA is the delta (change) in RTM prices due to impact of reliability deployments
  RDPA is NOT the value of Operating Reserves (which the ORDC adder is)
Flawed implementation of RDPA treats it like an additional value of Operating Reserves that is paid to all available capacity
  RDPA related to RUC even paid to Resources moved down to resolve transmission constraints – Resources actually adversely impacting the constraint
  Paying RDPA to all available capacity is a huge unnecessary transfer of wealth from Consumers to Resources
  Flawed treatment of RDPA as value of Operating Reserves also results in increased AS imbalance charges and payments and uplift
  Real-Time Co-optimization maintains the current RDPA design and thus the same flaws
Fixing RDPA is straightforward and mostly Settlement related
  Use LMPs from the SCED pricing run as LMPs used for Settlement – ORDC adder is added to these LMPs to determine SPPs (eliminates RDPA)
  Only resources moved up or down in the pricing run compared to the dispatch run receive additional compensation to be indifferent and only for their delta MW
  Positive ΔMW paid ΔLMP times ΔMW
  Negative ΔMW paid negative ΔLMP times negative ΔMW
Notes: <number>

## Slide 3: Flawed RDPA Example: B2 RUCed
<number>
SCED Dispatch Run: A1=12000MW, B1=26000MW, B2=2000MW, LMPa=$0/MWh, LMPb=$50/MWh, SysLam=$37.50/MWh, T=$50/MW/hr
SCED Pricing Run: LMPa=$0/MWh, LMPb=$250/MWh, SysLam=$187.50/MWh, RDPA=$150/MWh
Thus, SPPa=$150/MWh, SPPb=$200/MWh (assume no ORDC adder)
If StartUpCost+MinEnergyCost for B2=$500k, RUC Makewhole=$100,000
AS (RDPA) Imbalance Payment: A1=3000x150=$450,000, B1=1000*150=$150,000 (assume B1 has 1,000MW AS responsibility)
Flawed in every way: AS (RDPA) Imbalance Uplift=$600,000, RUC Charge=$100,000, SPPa=Curtail Load at A (bad) and build more, SPPb=diluted price, Congestion Charge=T=$50/MWh – diluted/incorrect
Unnecessary huge transfer of wealth from consumers to useless capacity
Notes: <number>

## Slide 4: Flawed RDPA: Counterproductive
<number>

## Slide 5: Fixed RDPA Example: B2 RUCed
<number>
SCED Dispatch Run: A1=12000MW, B1=26000MW, B2=2000MW, LMPa=$0/MWh, LMPb=$50/MWh, SysLam=$37.50/MWh
SCED Pricing Run: LMPa=$0/MWh, LMPb=$250/MWh, SysLam=$187.50/MWh, T=$250/MW/hr, No RDPA separately calculated
Thus, SPPa=$0/MWh, SPPb=$250/MWh (assume no ORDC adder)
If StartUpCost+MinEnergyCost for B2=$500k, RUC Makewhole=$0
RDPA Indifference Payment ΔMWxΔLMP: A1=0, B1=1000*200=$200,000 Fixed in every way: RDPA Indifference Uplift=$200,000, RUC Charge=$0, SPPa=Do not Curtail Load at A nor build more, SPPb=Curtail Load and build more, Congestion Charge=$250/MW/hr – correct signal
Future: RDPA indifference payment can be significantly reduced by integrating area under Energy Offer Curve for ΔMW instead of using ΔLMP – greater system impact
Notes: <number>

## Slide 6: Fixed v Flawed RDPA
<number>
SCED pricing run already determines correct locational prices – uses those prices for all Settlements
Eliminate flawed RDPA – no RDPA related AS Imbalance Payment/Charge
Captures the impact of reliability deployments on energy prices
Possibly minimal impact on MMS and EMS – impact mainly on Settlement
Only resources moved up or down in the pricing run compared to the dispatch run receive additional compensation to be indifferent and only for their delta MW (optional since Resources making more – then no uplift!)
Sends correct locational price signals – strong prices where RUC needed
Massively reduces RDPA related uplift charges (getting worse w/West IRR)
Eliminates unnecessary and counter-productive payments to resources that adversely impact the constraints for which ERCOT RUCed other resources
Flexible load may harmfully curtail due to flawed RDPA on export side of constraint – need this fix now so LFLs respond to accurate price signals
Reduces (if not reverses) need for RUC makewhole payments
Sends correct congestion price signals
WMS Action: Direct WMWG to analyze this proposal and report back
Notes: <number>