## Slide 1
Analysis on Changing Generation Cost Scaling in HRUC

## Slide 2: Background
Cost scaling factor was introduced with NPRR 864 in October 2018.
Scaling factor modifies the Start Up and Minimum Energy Costs for Resources with a cold start time of one hour or less.
The intent was to make short lead time Resources appear more economical in the RUC optimization.
Under the previous operational approach, this would allow ERCOT to defer commitment decisions and provide market participants additional time to self-commit their Resources.
Ideally, it was hoped that commitments would not be needed due the deferred commitments.

## Slide 3: Background
Cost scaling of short lead time Resources is no longer effective with ERCOT’s current operational approach.
The scaling has led to ERCOT Operators needing to make many of their RUC decisions outside of the economic-based, RUC recommendations. This can lead to inefficiencies in the commitment decisions.
Changing the cost scaling factors to 100% will help ensure the commitment decisions recommended by the RUC optimization reflect the economically optimal commitment decision.
This will benefit both ERCOT and the general market.
Commitment of the most economic set of Resources.
Potentially decreases make whole payments.
Less burden on ERCOT staff to perform extra studies outside of RUC.

## Slide 4: Changes to Scaling
Original
Scaling Removed

## Slide 5: Summary of Study Cases
April 22nd, 2022 05:00
Commitments by operators were all recommended by HRUC
WESTEX constraint was the reason given by operators
Resources were committed for HE11-17
Maximum aggregate HSL of committed Resources was 531 MW
February 23rd, 2022 04:00
No commitments by operators were HRUC recommended
Resources committed for HE8-14
Maximum aggregate HSL of committed Resources was 1,176 MW
HASL margin was between -531 MW and 1100 MW for HE8-14
October 3rd, 2021 06:00
Most commitments were HRUC recommended
Resources committed for HE13-23
Maximum aggregate HSL of committed Resources was 889 MW
HASL margin was between -5,223 MW and -51 MW
September 2nd, 2021 07:00
No commitments were HRUC recommended
Resources committed for HE13-21
Maximum aggregate HSL of committed Resources was 1,141 MW
HASL margin was between -1,798 MW and 424 MW

## Slide 6: Apr 22nd, 2022 05:00 Case

## Slide 7: Original vs Scaling Removed Cases
Chart: Sum of HSL for Committed Resources
| 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Original | 1350.2 | 749.4 | 558.4 | 502.4 | 2685 | 2695 | 2097 | 1259.6 | 1166.4 | 817.4 | 1205.6 | 921.2 | 168
Scaling Removed | 1350.2 | 805.9 | 511.9 | 455.9 | 2439.1 | 3117.1 | 2452.2 | 1636.6 | 1200.2 | 780.6 | 1123.6 | 752.7 | 570.6
Chart: Sum of LSL for Committed Resources
| 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Original | 853.4 | 383 | 303 | 250 | 1470.8 | 1498.8 | 1249.8 | 692.8 | 696.8 | 582.8 | 791.8 | 513 | 90
Scaling Removed | 853.4 | 387 | 272 | 219 | 1028 | 1421 | 1207 | 720.8 | 597.2 | 344 | 592.6 | 326 | 80
Note: HSL for each Resource was maximum value over commitment block
LSL for each Resource was minimum value over commitment block

## Slide 8: Original vs Scaling Removed Cases
Note
Extensions: Resource Output is Extended
Short Lead Time: 0 < Startup Time < 1 hrs
Medium Lead Time: 1 <= Startup Time < 5 hrs
Long Lead Time: 5 <= Startup Time < 10 hrs
Very Long Lead Time: 10 hrs <= Startup Time
Chart: MWhs Recommended by Lead Time
| Extension | Short Lead Time | Medium Lead Time | Long Lead Time | Very Long Lead Time
Original | 122 | 9522.6 | 4073 | 0 | 0
Scaling Removed | 523 | 6482.5 | 5892 | 1872 | 0
Chart: Number of Resource Hours Recommended
| Extension | Short Lead Time | Medium Lead Time | Long Lead Time | Very Long Lead Time
Original | 1 | 166 | 25 | 0 | 0
Scaling Removed | 1 | 106 | 28 | 8 | 0

## Slide 9: Sum of HSL Committed by HRUC
Note
Extensions: Resource Output is Extended
Short Lead Time: 0 < Startup Time < 1 hrs
Medium Lead Time: 1 <= Startup Time < 5 hrs
Long Lead Time: 5 <= Startup Time < 10 hrs
Very Long Lead Time: 10 hrs <= Startup Time
Chart: Original Case
| 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Extension | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 122 | 0
Short Lead Time | 906.2 | 749.4 | 558.4 | 502.4 | 1049 | 1059 | 674 | 728.6 | 635.4 | 653.4 | 1041.6 | 760.2 | 168
Medium Lead Time | 0 | 0 | 0 | 0 | 934 | 934 | 776 | 531 | 531 | 164 | 164 | 39 | 0
Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Very Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Scaling Removed
| 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Extension | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 523
Short Lead Time | 906.2 | 805.9 | 511.9 | 455.9 | 599.1 | 812.1 | 360.2 | 436.6 | 435.2 | 274.6 | 617.6 | 219.6 | 47.6
Medium Lead Time | 0 | 0 | 0 | 0 | 1124 | 1369 | 1211 | 966 | 531 | 272 | 272 | 147 | 0
Long Lead Time | 0 | 0 | 0 | 0 | 234 | 234 | 234 | 234 | 234 | 234 | 234 | 234 | 0
Very Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Note: HSL for each Resource was maximum value over commitment block

## Slide 10: Feb 23rd, 2022 04:00 Case

## Slide 11: Original vs Scaling Removed Cases
Chart: Sum of HSL for Committed Resources
| 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Original | 0 | 0 | 511.5 | 664 | 618 | 714 | 226 | 226 | 674 | 942 | 748 | 748 | 2634.7 | 4100.7 | 4564.6 | 4564.6 | 3786.8 | 2871 | 2269
Scaling Removed | 126 | 126 | 239 | 676 | 454 | 805.3 | 454 | 454 | 854 | 976 | 976 | 976 | 2724 | 4767.8 | 5165 | 4409.8 | 4055.8 | 2886 | 2262
Chart: Sum of LSL for Committed Resources
| 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Original | 0 | 0 | 172 | 200 | 200 | 224 | 16 | 16 | 71 | 134 | 74 | 74 | 908.6 | 1193.6 | 1184 | 1184 | 968 | 809 | 707
Scaling Removed | 64.2 | 64.2 | 72.2 | 184.2 | 96 | 260 | 96 | 96 | 139 | 154 | 154 | 154 | 606 | 1081 | 1282.6 | 1026 | 1008.5 | 698 | 473
Note: HSL for each Resource was maximum value over commitment block
LSL for each Resource was minimum value over commitment block

## Slide 12: Original vs Scaling Removed Cases
Note
Extensions: Resource Output is Extended
Short Lead Time: 0 < Startup Time < 1 hrs
Medium Lead Time: 1 <= Startup Time < 5 hrs
Long Lead Time: 5 <= Startup Time < 10 hrs
Very Long Lead Time: 10 hrs <= Startup Time
Chart: MWhs Recommended by Lead Time
| Extension | Short Lead Time | Medium Lead Time | Long Lead Time | Very Long Lead Time
Original | 6590 | 14756.9 | 9516 | 0 | 0
Scaling Removed | 8487 | 8052.4 | 13822 | 2179.3 | 846
Chart: Number of Resource Hours Recommended
| Extension | Short Lead Time | Medium Lead Time | Long Lead Time | Very Long Lead Time
Original | 32 | 183 | 30 | 0 | 0
Scaling Removed | 43 | 96 | 43 | 15 | 9

## Slide 13: Sum of HSL Committed by HRUC
Note
Extensions: Resource Output is Extended
Short Lead Time: 0 < Startup Time < 1 hrs
Medium Lead Time: 1 <= Startup Time < 5 hrs
Long Lead Time: 5 <= Startup Time < 10 hrs
Very Long Lead Time: 10 hrs <= Startup Time
Chart: Original Case
| 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Extensions | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 513 | 635 | 635 | 635 | 635 | 635 | 635 | 635 | 635 | 757 | 240
Short Lead Time | 0 | 0 | 511.5 | 664 | 618 | 714 | 226 | 226 | 161 | 307 | 113 | 113 | 1640.7 | 1498.7 | 1439.6 | 1439.6 | 1420.8 | 1755 | 1909
Medium Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 359 | 1967 | 2490 | 2490 | 1731 | 359 | 120
Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Very Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Scaling Removed
| 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Extensions | 126 | 126 | 126 | 126 | 0 | 0 | 0 | 0 | 513 | 635 | 635 | 635 | 635 | 635 | 635 | 635 | 635 | 1282 | 1108
Short Lead Time | 0 | 0 | 113 | 322 | 226 | 322 | 226 | 226 | 113 | 113 | 113 | 113 | 674 | 1003.8 | 1401 | 1037.8 | 1206.8 | 616 | 226
Medium Lead Time | 0 | 0 | 0 | 228 | 228 | 228 | 228 | 228 | 228 | 228 | 228 | 228 | 741 | 2490 | 2490 | 2490 | 1967 | 741 | 851
Long Lead Time | 0 | 0 | 0 | 0 | 0 | 255.3 | 0 | 0 | 0 | 0 | 0 | 0 | 170 | 582 | 582 | 190 | 190 | 190 | 20
Very Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 504 | 57 | 57 | 57 | 57 | 57 | 57
Note: HSL for each Resource was maximum value over commitment block

## Slide 14: October 3rd, 2021 6:00 Case

## Slide 15: Original vs Scaling Removed Cases
Chart: Sum of HSL for Committed Resources
| 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Original | 0 | 0 | 226 | 1253 | 1740 | 2883 | 3809 | 4507 | 4206.4 | 4804.4 | 4644 | 2806.4 | 2068 | 246.9
Scaling Removed | 0 | 0 | 56.5 | 1237 | 1817 | 2887 | 3798.3 | 4507 | 4206.4 | 4804.4 | 4625.6 | 2814.5 | 2124 | 246.9
Chart: Sum of LSL for Committed Resources
| 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Original | 0 | 0 | 16 | 127 | 304 | 555 | 1158.2 | 1337.2 | 1113.2 | 1567.2 | 1435.2 | 713.2 | 474.5 | 133
Scaling Removed | 0 | 0 | 4 | 111 | 196 | 457 | 831 | 1337.2 | 1113.2 | 1567.2 | 1261 | 441 | 329 | 133
Note: HSL for each Resource was maximum value over commitment block
LSL for each Resource was minimum value over commitment block

## Slide 16: Original vs Scaling Removed Cases
Note
Extensions: Resource Output is Extended
Short Lead Time: 0 < Startup Time < 1 hrs
Medium Lead Time: 1 <= Startup Time < 5 hrs
Long Lead Time: 5 <= Startup Time < 10 hrs
Very Long Lead Time: 10 hrs <= Startup Time
Chart: MWhs Recommended by Lead Time
| Extension | Short Lead Time | Medium Lead Time | Long Lead Time | Very Long Lead Time
Original | 612.9 | 11415.2 | 19312 | 1380 | 0
Scaling Removed | 1146.9 | 7651.7 | 22242 | 1610 | 0
Chart: Number of Resource Hours Recommended
| Extension | Short Lead Time | Medium Lead Time | Long Lead Time | Very Long Lead Time
Original | 4 | 188 | 64 | 6 | 0
Scaling Removed | 7 | 126 | 76 | 7 | 0

## Slide 17: Sum of HSL Committed by HRUC
Note
Extensions: Resource Output is Extended
Short Lead Time: 0 < Startup Time < 1 hrs
Medium Lead Time: 1 <= Startup Time < 5 hrs
Long Lead Time: 5 <= Startup Time < 10 hrs
Very Long Lead Time: 10 hrs <= Startup Time
Chart: Original Case
| 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Extension | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 485 | 0 | 0 | 118 | 9.9
Short Lead Time | 0 | 0 | 226 | 254 | 616 | 727 | 1529 | 1578 | 1277.4 | 1390.4 | 1955 | 1148.4 | 714 | 0
Medium Lead Time | 0 | 0 | 0 | 999 | 1124 | 1926 | 2050 | 2699 | 2699 | 2699 | 2459 | 1658 | 999 | 0
Long Lead Time | 0 | 0 | 0 | 0 | 0 | 230 | 230 | 230 | 230 | 230 | 230 | 0 | 0 | 0
Very Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Scaling Removed
| 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Extension | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 485 | 195 | 217 | 240 | 9.9
Short Lead Time | 0 | 0 | 56.5 | 113 | 113 | 308 | 869.3 | 1578 | 1277.4 | 1390.4 | 1501.6 | 331.5 | 113 | 0
Medium Lead Time | 0 | 0 | 0 | 1124 | 1704 | 2349 | 2699 | 2699 | 2699 | 2699 | 2699 | 2036 | 1534 | 0
Long Lead Time | 0 | 0 | 0 | 0 | 0 | 230 | 230 | 230 | 230 | 230 | 230 | 230 | 0 | 0
Very Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Note: HSL for each Resource was maximum value over commitment block

## Slide 18: September 2nd, 2021 7:00 Case

## Slide 19: Original vs Scaling Removed Cases
Chart: Sum of HSL for Committed Resources
| 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Original | 0 | 0 | 346 | 951 | 1841.8 | 1649 | 1694 | 443 | 1169 | 1305 | 558 | 152 | 0 | 0
Scaling Removed | 0 | 0 | 395 | 952 | 1896.4 | 1662 | 1717.4 | 1015 | 1128 | 1283 | 540.5 | 0 | 0 | 0
Chart: Sum of LSL for Committed Resources
| 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Original | 0 | 0 | 92 | 389 | 1011.9 | 868 | 868 | 189 | 405 | 501 | 132 | 80 | 0 | 0
Scaling Removed | 0 | 0 | 36 | 169 | 591.5 | 514 | 568.4 | 179 | 187 | 252 | 39 | 0 | 0 | 0
Note: HSL for each Resource was maximum value over commitment block
LSL for each Resource was minimum value over commitment block

## Slide 20: Original vs Scaled Cases
Note
Extensions: Resource Output is Extended
Short Lead Time: 0 < Startup Time < 1 hrs
Medium Lead Time: 1 <= Startup Time < 5 hrs
Long Lead Time: 5 <= Startup Time < 10 hrs
Very Long Lead Time: 10 hrs <= Startup Time
Chart: MWhs Recommeded by Lead Time
| Extension | Short Lead Time | Medium Lead Time | Long Lead Time | Very Long Lead Time
Original | 0 | 10108.8 | 0 | 0 | 0
Scaling Removed | 919 | 2677.3 | 2075 | 4918 | 0
Chart: Number of Resource Hours Recommended
| Extension | Short Lead Time | Medium Lead Time | Long Lead Time | Very Long Lead Time
Original | 0 | 176 | 0 | 0 | 0
Scaling Removed | 2 | 51 | 13 | 17 | 0

## Slide 21: Sum of HSL Committed by HRUC
Note
Extensions: Resource Output is Extended
Short Lead Time: 0 < Startup Time < 1 hrs
Medium Lead Time: 1 <= Startup Time < 5 hrs
Long Lead Time: 5 <= Startup Time < 10 hrs
Very Long Lead Time: 10 hrs <= Startup Time
Chart: Original Case
| 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Extension | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Short Lead Time | 0 | 0 | 346 | 951 | 1841.8 | 1649 | 1694 | 443 | 1169 | 1305 | 558 | 152 | 0 | 0
Medium Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Very Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Scaling Removed
| 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Extension | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 435 | 484 | 0 | 0 | 0
Short Lead Time | 0 | 0 | 0 | 203 | 755.4 | 521 | 576.4 | 113 | 226 | 226 | 56.5 | 0 | 0 | 0
Medium Lead Time | 0 | 0 | 395 | 280 | 280 | 280 | 280 | 280 | 280 | 0 | 0 | 0 | 0 | 0
Long Lead Time | 0 | 0 | 0 | 469 | 861 | 861 | 861 | 622 | 622 | 622 | 0 | 0 | 0 | 0
Very Long Lead Time | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Note: HSL for each Resource was maximum value over commitment block

## Slide 22: Conclusions and Future Work on Scaling
Generally, changing the scaling induces the RUC optimization to favor extensions, medium and long lead time Resources over short lead time Resources
  This conclusion may not hold for cases with very low HASL margins (10/3/2021 3:00)
  Possibly because HRUC already recommends most of the Resources available
The Scaling Removed cases tend to have similar amounts of HSL capacity, but lower aggregate LSL and fewer Resources
  Optimization chooses larger Resources when scaling is removed
Change in behavior is consistent for morning and evening peaks
  All cases show positive results for afternoon peak
  February case shows that changes happened even when case was only 5 hours before peak
Scaling Removed cases were more aligned with Operator actions but could better ensure committed Resources are the most economical choice

## Slide 23: Process for Updating the Scaling Parameter
The scaling parameter for Off-Line Resources having a cold start time of one hour or less is driven by paragraph (9) of Protocol Section 5.5.2, Reliability Unit Commitment (RUC) Process.
Changing this parameter does not require a Nodal Protocol Revision Request (NPRR) and can be updated through a recommendation by the Technical Advisory Committee (TAC) and approval by the ERCOT Board.
Table in Protocol 5.5.2(9):

## Slide 24: Questions?