## Slide 1
June 16, 2022
PDCWG
ERCOT Staff
Introduction to FFR Advancement and ERCOT Contingency Reserve Service (ECRS) Projects

## Slide 2: 2022 Release Targets – Board Approved NPRRs / SCRs / xGRRs (June 2022 PRS | Link)
Go-live dates can differ from Protocol effective dates – Please refer to market notices for more details
Release targets are subject to change
APPENDIX
Red Text: New additions and target release changes
Strike-Through Text: Previous target release
(a), (b), etc.: Multiple phase release
February Various Dates | April 4/5 – 4/7 | May 5/24 – 5/26 | July 7/26 – 7/28 | October 10/4 – 10/6 | December 12/6 – 12/8
LPGRR068 NPRR1054(a) NPRR1005 NOGRR210 RRGRR025 NPRR917 NPRR1052 NPRR1065 NPRR1073 NPRR1016 PGRR082 NOGRR212 | None NPRR1092(a) | NPRR939 NPRR1093 NPRR1101 NPRR1113 NOGRR232 OBDRR032 OBDRR033 OBDRR035 SCR800 SCR809 SCR814 MarkeTrak User Interface Refresh | NPRR1108 NPRR935(b) | FFR Advancement (NPRR863 FFR) NPRR987(a) NPRR1002(a) | NPRR1097
Project Status Codes
NS = Not Started
I = Initiation
P = Planning
E = Execution
H = On Hold
R1
R2
R3
R4
R5
R6
ü
ü
ü
ü
Securitization Subchapter N March Go-Live
ECRS project started in 1/2022 with a go-live target prior to the EMS Freeze
1/1
EMS Freeze
Mid-2023 – Mid-2024
E
E
E
ü
ü
ü
ü
DGR/DESR
NPRR1054(a) – Portion of gray box
NPRR935(b) – New solar forecasts and reports
NPRR987(a) – ESR Contribution to PRC
NPRR1002(a) – Charging Restrictions in Emergency Conditions
NPRR1092(a) – RUC offer floor change
SCR789 Ph2
Late 2022
TBD Items | NPRRs: 484,825(b),826,829,841,857,879,885,904,918,930,936,941,945,962,963,965,975,995,1004,1006,1019,1023,1026,1030,1032,1034,1040, 1057,1063,1077,1090,1092(b),1105 SCRs: 799,805,807,810,812,813,816,818,819 PGRRs: 066,076,088,091,094,099 Other: OBDRR009,RRGRR028
E
ü
ü
ü
ü
NPRR1120 Firm Fuel Supply Service RFP
Issue no later than 8/1/2022
NPRR1120 Firm Fuel Supply Service
Contracts start in November
6/4 – 6/6
6/23
5/13
ü
ü
ü
ü
ü
ü
ü
ü
ü
ü
ü
ü

## Slide 3: Proposed NPRR 863 Ancillary Service Framework Changes (October 2018 WMS | Link)
Current Framework
FFR
Triggered at 59.85 Hz and full response in 15 cycles
Once deployed, sustain for up to 15 mins. Once recalled, restore within 15 mins
PFR
PFR capable capacity reserved on generators or Controllable Load Resources (CLR)
Minimum 1,150 MW must be provided by resources capable of PFR
Load Resources on UFR
Triggered at 59.70 Hz and full response in 30 cycles
Sustain until recalled. Once recalled, restore within 3 hours
Beyond the minimum PFR, up to 60% of total RRS can come from Load Resources on UFR or FFR.
Generation
Online or offline capacity that can be converted to energy within 10 minutes
Dispatched by SCED
Load Resources (UFR not required)
Up to 50% of ECRS capacity can come from Load Resources with or without UFR
Once deployed, must respond within 10 minutes. Restoration within 3 hours
Load Resources on UFR
Primary Frequency Response (PFR)
Fast Frequency Response (FFR)
ERCOT Contingency Reserve Service (ECRS)
Load Resources may or may not be on UFR
10 minute ramp
Responsive Reserve Service
Primary Frequency Response
Load Resources on Under Frequency Relay (UFR)
10 minute ramp
2,300 to 3,200 MW*
No Change
Regulation
Regulation
157 to 687 MW*
157 to 687 MW*
2,300 to 3,200 MW*
508 to 1,644 MW**
Responsive Response Service (RRS)
Non-Spin
No protocol changes.
Proposed methodology for Non-Spin Reserve Service quantities in this framework - quantities computed using 2018 A/S Methodology are reduced by ECRS quantities.
Non-Spin
967 to 2,361 MW*
0 to 1,180 MW***
*Quantities computed/estimated using 2018 Ancillary Service Methodology. **Quantities estimated using this reference. ***Quantities estimated using this reference and method in box on far left.
For Discussion Purposes Only. The intent of this slide is to represent NPRR 863 (with STEC comments from 10/1/2018). Protocol language prevails to the extent of any inconsistency with this one page summary.
Overall A/S: 3,807 to 5,958 MW*
Overall A/S: 3,807 to 5,958 MW*
Last Edited on 10/08/2018
NPRR 863 With STEC Comments (10/1)

## Slide 4: FFR Advancement Introduction (October 2021 Workshop | Link)
PR325-01 FFR Advancement (FFRA) project is the second in a series of projects that are being used to implement changes associated with NPRR 863.
Following is a high-level list of the changes that are being made as a part of the FFRA project.
  Upon the full implementation of FFR as a part of this project, for any operating hour in the Day Ahead Market (DAM),
    An ESR-Gen and ESR-CLR will be able to offer, get awarded and provide* (conventional) Regulation, RRS-PFR, and (online) Non-Spin simultaneously with RRS-FFR (assuming the ESR-Gen or ESR-CLR is qualified for the AS or AS sub-type it is offering or providing).
    A NCLR will be able to offer, get awarded and provide** either RRS-FFR or RRS-UFR (assuming the NCLR is qualified for the RRS sub-type it is offering or providing).
  RRS Offers in & Awards from DAM/SASM, RRS AS Responsibilities in COPs, Self-Arranged RRS and RRS AS Trade submissions will split by subtype namely, RRS-PFR, RRS-FFR and RRS-UFR.
  In Real Time, new telemetry will be setup to send Ancillary Service Responsibility and Ancillary Service Schedule for RRS-FFR.
    The existing Ancillary Service Responsibility and Ancillary Service Schedule telemetry will continue to be used for telemetering RRS-PFR and RRS-UFR.
*ESR-Gen will be required to use ONFFRRRS resource status to provide RRS-FFR in Real Time.
** NCLR will be required to use ONFFRRRSL resource status to provide RRS-FFR or ONRL resource status to provide RRS-UFR in Real Time.

## Slide 5: FFR Advancement Introduction, continued…
  For CLRs including ESR-CLRs and Generating Units operating in synchronous condenser fast response mode, RRS-PFR Awards from DAM/SASM, RRS-PFR COP submissions, and RRS-PFR Responsibility & Schedule telemetry in Real Time for CLRs will be limited by their corresponding RRS-MW-Limit (%) or tested MW as applicable.
  For all Resources providing RRS-FFR, RRS-FFR Awards from DAM/SASM, RRS-FFR COP submissions and RRS-FFR Responsibility & Schedule telemetry in Real Time will be limited by their respective FFR Qualified MWs.
  There will be changes to several reports primarily to include information breakdown by RRS subtype.

## Slide 6: ECRS Introduction
ECRS is 10-minute service from,
  Generation Resources and Controllable Load Resources.
  Load Resources with or without high set under-frequency relay during EEA using Resource Status ONECL.
  Quick Start Generation Resources (QSGRs).
  Generation Resources in synchronous condenser fast response mode using Resource Status ONECRS.
LFC will be used to deploy automatically deploy ECRS from Generation Resources and Controllable Load Resources to restore frequency to its scheduled value when frequency drops below 59.91 Hz. During tight operating conditions, ERCOT Operators may manually deploy SCED dispatchable ECRS (i.e. from Generation Resources and Controllable Load Resources). MMS’s Ancillary Service Manager will be used to deploy non-Controllable Load Resources that provide ECRS.
The total amount of ECRS that Load Resources other than Controllable Load Resources may provide shall not exceed 50% of the total ERCOT-wide ECRS requirement.
Non-Controllable Load Resources when providing ECRS may provide RRS-UFR as well.
ECRS project started in 1/2022 with a go-live target prior to the EMS Freeze.