## Slide 1
MTLF Update
Calvin Opheim
Load Forecasting & Analysis
SAWG
6/24/2022

## Slide 2: Agenda
Review
Summer Forecast Models
Questions

## Slide 3: Model Review
All internally developed forecasts (E, E1, E2, and E3) are configured exactly the same:
  Same exact model
  Same application of error correction
  Same application of tuning
The only difference is the weather forecast that is used in each forecast model

## Slide 4: Weather Forecast Sources
The following weather forecasts are available:
  European Model (Euro)
  Global Forecast System (GFS)
  Global Forecast System Ensemble (GENS)
  North American Model (NAM)
  3 vendor models

## Slide 5: Model Update previously provided (4/4)
Typically, E2 uses the most extreme weather forecast for each Weather Zone for the Day Ahead
  Will result in different forecasts being used in different weather zones (i.e., Euro used in North Central while GFS is used in Coast)
Typically, E3 uses the most extreme weather forecasts for each Weather Zone for days 4+ in the future
  Will result in different forecasts being used in different weather zones (i.e., vendor 1 used in South Central while GENS is used in South)
Typically, E and E1 will use the same weather forecast for all Weather Zones
  The most extreme weather forecasts based on a single source (i.e., GFS, Euro, etc.) is used for E and E1. An example would be E using the GFS for all Weather Zones with E1 using the Euro for all Weather Zones.
  These forecasts should be considered the 50/50 forecast

## Slide 6: Model Update for this Summer
E2 will not necessarily use the most extreme weather forecast for each Weather Zone for the Day Ahead
  Target for this forecast is to be 1-2% higher than the base 50/50 forecast
E3 will use one of the most extreme weather forecasts for the ERCOT system for days 4+ in the future
  Note the subtle changes here. No longer the most extreme for each weather zone.
  Based on ERCOT System-Wide Temperature
  Discretion is applied to which extreme model is used
Typically, E and E1 will use the same weather forecast for all Weather Zones
  These forecasts should be considered the 50/50 forecast

## Slide 7: Questions?