## Slide 1: Reduced SCED Time

## Slide 2: Description
Reduce the SCED run time from the current 5 minute basis to something shorter in order to:
  Improve the accuracy of energy pricing
  Reduce impact of voluntary load response
  Reduce amount of regulation required
  Reduce financial impact to regulation providers (energy pricetakers)
  Reduce manual SCED intervention by operators

## Slide 3: Voluntary Load Shed Impact on Regulation
Energy prices are created by Security Constrained Economic Dispatch
  Load and generation levels are matched as closely as possible
    Bias factors try to estimate certain variations
    Load response offered in SCED is appropriately accounted
  Voluntary large load response is generally not appropriately considered
    Difference must be covered by Regulation Up or Regulation Down
    Usually at a price that is opposite the desired deployment
    High prices = load curtailment, must be covered by Regulation Down
    Low prices = load returns, must be covered by Regulation Up

## Slide 4: Reducing SCED Interval
Less time at high or low price
  Similar benefit seen reducing interval from 15 minutes in zonal to 5 in nodal
  New SCED interval is able to incorporate actual remaining load in calculation
  Limits the value of voluntary price chasing
Logically will fall into a divisor of 15 minutes to match the settlement interval
  This leaves 1 min, 1.5 min, 2.5 min, or 3 min.
  Limited by duration of the worst case SCED run
Propose to move to shortest duration possible

## Slide 5: Points for Consideration
Future market enhancements may impact decisions about decreasing the SCED timeframe, e.g., real-time co-optimization or a multi-interval real-time market
If the timeframes are changes, need to revisit other processes that are based on the current 5-minutes, e.g., state estimator and real-time contingency analysis
Should consider more automatic triggering events to initiate off-cycle SCED executions.
  This solution could be an alternative to or complimentary with reductions to the SCED timeframe

## Slide 6: Questions?