## Slide 1
Illustration of Potential Revenue Neutrality Allocation Due to a Local RDPA Approach
CMWG
Dave Maggio
July 18, 2022

## Slide 2: Introduction
This short presentation is to follow up on questions that were raised during the meeting on June 13, 2022, regarding potential impacts of a local Reliability Deployment Price Adder (RDPA) approach on Revenue Neutrality Allocation.
The following illustration uses the previous example shared by Shams Siddiqi with a change to one of the Generator offer prices.
  https://www.ercot.com/files/docs/2022/06/07/RDPA_Flawed_but_Fixable.ppt
The specific circumstance that leads to Revenue Neutrality Allocation is the case in which a transmission constraint is not binding in the dispatch run, but becomes binding in the pricing run, and there are Point-to-Point (PTP) Obligations that must be paid out do the local RDPA differences.

## Slide 3: Illustration using last month’s example setup – Dispatch run
Generator dispatch in dispatch run:
  A1: 11000 MW (Slightly more expensive than B1)
  B1: 27000 MW (Cheapest Resource, so dispatched to its High Ancillary Service Limit (HASL))
  B2: 2000 MW (RUCed Resource dispatched to its Load Sustained Limit (LSL))
With a line flow of 1000 MW between A and B, there is not a binding constraint and the price at both A and B is $60/MWh.
Instead, assume a $60/MWh offer. No other changes.
Basic setup taken from the presentation by Shams Siddiqi on June 13, 2022 (https://www.ercot.com/files/docs/2022/06/07/RDPA_Flawed_but_Fixable.ppt)

## Slide 4: Illustration using last month’s example setup – Pricing run
Generator dispatch in pricing run:
  A1: 12000 MW (Dispatch increased but limited by transmission limit. Setting price at A)
  B1: 27000 MW (Cheapest Resource, still at HASL)
  B2: 1000 MW (LSL relaxed and dispatch decreased. Setting price at B)
Constraint is now binding and with price at A of $60/MWh and price at B of $250/MWh
Instead, assume a $60/MWh offer. No other changes.
Basic setup taken from the presentation by Shams Siddiqi on June 13, 2022 (https://www.ercot.com/files/docs/2022/06/07/RDPA_Flawed_but_Fixable.ppt)

## Slide 5: Illustration using last month’s example setup – Settlement
Generator settlement:
  (-11000 MW*$60/MWh)+(-27000 MW*$250/MWh)+(-2000 MW*$250/MWh) = -$7.91M
Load settlement:
  (10000 MW*$60/MWh)+(30000 MW*$250/MWh) = $8.1M
Congestion rent collected:
  $8.1M – $7.91M = $190k
Assuming the same PTP Obligation from the original example:
  -2000 MW*($250/MWh-$60/MWh) = -$380k
  Funding insufficient with $190k collected through Revenue Neutrality Allocation
Basic setup taken from the presentation by Shams Siddiqi on June 13, 2022 (https://www.ercot.com/files/docs/2022/06/07/RDPA_Flawed_but_Fixable.ppt)
Instead, assume a $60/MWh offer. No other changes.