## Slide 1
Large Flexible Load Task Force
LFLs in the CDR & SARA
Evan Neel
ERCOT – Resource Adequacy
7/25/2022

## Slide 2: LFL – Issue 49
Consider how co-located or Stand-alone LFLs and Resources should be considered in resource adequacy reports, including if they should be classified as Private Use Networks in ERCOT reports.
LFL – 49 Contributors:
  ERCOT (Evan Neel & Pete Warnken)
  ONCOR (Martha Henson)
  AEP (Blake Gross)
  Lancium (Eric Goff & Andrew Reimers)
  Jupiter Power (Caitlin Smith)
Note on SARA/CDR Redesign:
  Efforts are currently underway to redesign the CDR & SARA reports as instructed by the Public Utility Commission. Solutions proposed to LFLTF are intended to be applied to current CDR and SARA formats. Agreed upon ideas will be factored into the overall redesign effort, maintaining a consistent reporting of LFLs in resource adequacy reports.

## Slide 3: Separating Co-located LFLs and PUNs
All resources where netting occurs, and the load is not independently metered, are automatically considered PUNs in ERCOTs network model for the purpose of calculating accurate load zone prices (NPRR 945).
This does not mean they are a PUN from a legal standpoint.
We expect co-located LFLs to behave differently than traditional PUN sites and believe there is value in reporting them separately. This would allow us to:
  Create an independent means of predicting available peak capacity (Current PUN capacity contributions methods would yield inaccurate results for new co-located LFLs)
  Report the capabilities of both the generation resource and the large flexible load.
Reporting would have two aspects to it (Large Load tab):
  Line-item reporting of the generation units (same as capacities tab)
  Aggregate reporting of expected co-located LFL load during the peak hour
    This would include items detailing the total firm load and total expected load (firm + flexible) at these sites
This offers the load information privacy of a traditional PUN, while also increasing visibility into the capabilities of the resource/load pair.

## Slide 4: New “Large Loads” Tab (CDR & SARA)
Inspired by the commission’s intent to increase reporting transparency for large loads, we are proposing a new tab called “Large Loads”.
This will include the reporting for co-located LFLs (and associated generation resources), stand-alone LFLs, and critical loads (commission driven).
The inclusion criteria would be voluntary registration that would encompass identifying as an LFL via LFL-4 (Definition of Large Flexible Load).
Stand-alone loads would be reported individually, and their firm/flexible proportions would be aggregated and reported along with an ERCOT calculated peak LFL load forecast as a percentage of total LFL.

## Slide 5: New “Large Loads” Tab (CDR & SARA): Co-located

## Slide 6: LFL Accounting in the SARA
The contribution of LFLs will be accounted for in two different parts of the SARA.
  Co-located will be accounted for in the Forecasted Capacities tab (2 new line-items)
  Stand-alone will be accounted for in the Scenarios tab (Peak Load Forecast Adjustment)
When calculating the final Capacity Available for Operating Reserves (CAFOR), if a scenario sees CAFOR drop below ~3,000 MW (exact number dependent on LFL-38) then the remaining flexible portion of LFLs forecasted to be online would be credited to the CAFOR prior to EEA resources deployed by ERCOT.

## Slide 7: LFL Accounting in the CDR
CDR LFL accounting will all take place on the Seasonal Summary tab via 4 new line-items.
  Stand-alone as load forecast adjustments
  Co-located as resource capacity line-items
Steps will also be taken to make sure there is no double counting of LFL capacity being used for ancillary services (ex. RRS & non-spin).

## Slide 8: Moving Forward
The group is currently working on several other topics that will be discussed at a future meeting. These topics include:
  LFL peak demand consumption forecast calculations and methodology.
  RFI process/questions necessary to gather the appropriate information for the forecast calculations.
  SARA deterministic scenarios addressing large flexible loads.
In the meantime, the task force can expect to receive a white paper outlining the discussed topics in greater detail via the LFLTF email listserv.
Draft SARA and CDR documents incorporating LFLs are also in the works and will be shared with the task force when completed.