## Slide 1: LFLTF Load Shed Options – Assessment (Existing)
Option | Description | Pros | Cons
1 | ERCOT to telemeter TOs’ RT Load Shed obligation % | -Accuracy | -Complex and highly dependent on telemetry -Implementation logistics? -ERCOT systems changes? -No assurance of how the LFLs will actually behave in RT
2 | Exclude LFLs from LS table | -Simple | -Potentially increases LS allocation to other TOs (see Appendix example) -No assurance of how the removed loads will actually behave in RT
3 | ERCOT to QSE LFL Load Shed | -Keeps existing TO allocation the same -QSE allocation to be based on ERCOT registration requirements | -TO to be backstop for firm portion if LFL doesn’t respond? -Still need to account for/exclude LFLs consuming during 4CP intervals to ensure MW not included in TO allocations; at ERCOT-level?
4 | Load Ratio Share based on distribution load only | -May reduce complexity | -Skews LS obligation to be more burdensome on TOs with less industrial (i.e., transmission-connected) load -No assurance of how the LFLs will actually behave in RT

## Slide 2: LFLTF Load Shed Options – Assessment (Proposed Combo 2+3)
Option | Description | Pros | Cons
1 | ERCOT to telemeter TOs’ RT Load Shed obligation % | -Accuracy | -Complex and highly dependent on telemetry -Implementation logistics? -ERCOT systems changes? -No assurance of how the LFLs will actually behave in RT
2 + 3 | ERCOT excludes LFLs from TO-LS allocation percentages, and ERCOT directs LFL QSEs to stop consuming pre-emergency | -QSE “load shed” allocation to be based on ERCOT registration requirements | -Will TO be backstop for firm portion if LFL doesn’t respond? -Decouples transmission cost allocation (PUC level) from load shed allocations (ERCOT level)
4 | Load Ratio Share based on distribution load only | -May reduce complexity | -Skews LS obligation to be more burdensome on TOs with less industrial (i.e., transmission-connected) load -No assurance of how the LFLs will actually behave in RT

## Slide 3: LFLTF Load Shed Options – Assessment (Combo 2+3 + GSEC)
Option | Description | Pros | Cons
1 | ERCOT to telemeter TOs’ RT Load Shed obligation % | -Accuracy | -Complex and highly dependent on telemetry -Implementation logistics? -ERCOT systems changes? -No assurance of how the LFLs will actually behave in RT
2 + 3 | ERCOT excludes LFLs from TO-LS allocation percentages, and ERCOT directs LFL QSEs to stop consuming pre-emergency | -QSE “load shed” allocation to be based on ERCOT registration requirements | -Will TO be backstop for firm portion if LFL doesn’t respond? -Decouples transmission cost allocation (PUC level) from load shed allocations (ERCOT level)
4 | Load Ratio Share based on distribution load only | -May reduce complexity | -Skews LS obligation to be more burdensome on TOs with less industrial (i.e., transmission-connected) load -No assurance of how the LFLs will actually behave in RT -If excluded, transmission level load is free to decrease, increase or remain the same during an event. (GSEC) -Potentially shifts obligations to entities with higher ratio of distribution level load (GSEC)

## Slide 4: LFLTF Load Shed Options – TO Inventory/Straw Poll
Option | Description | Support | Oppose | Neutral
1 | ERCOT to telemeter TOs’ RT Load Shed obligation % | -GSEC -CNP (equitable) | -Oncor (complexity) | -AEP (generally support, but concerns with complexity) -PEC
2 + 3 | ERCOT excludes LFLs from TO-LS allocation percentages, and ERCOT directs LFL QSEs to stop consuming pre-emergency | -ERCOT -GSEC -Oncor -LCRA -AEP -TNMP -PEC |  | -CNP
4 | Load Ratio Share based on distribution load only | -CNP -AEP | -Oncor -GSEC -PEC | 

## Slide 5: LFLTF Load Shed – Recommendations/Consensus Statements
Large loads should not be required to consume energy during Energy Emergency Levels 1, 2, or 3
    Caveat: If providing RRS AS, LFL should consume until ERCOT directs the AS deployment
    Discussed/consensus reached during 6/25/22 LFLTF
    Caveat: provided EEA3 load shed allocation is changed so that an LFL does not create a load shed obligation with which a TO can’t comply. (GSEC)