## Slide 1
Telemetry Data for Crypto load and IRR
August 23, 2022
Resource Integration Working Group Meeting
Staff
ERCOT Balancing Operations Planning

## Slide 2: Co-located Crypto Load and IRR
POI
IRR
POI
GMW
IRR
Crypto Load
MW/HSL
Gross MW/Gross RT Power Potential
 | IRR + Co-located load with PUN designation or crypto load | Single IRR (WGR or PVGR)
High Sustained Limit | Reflect net power potential of the plant (re-use the existing HSL data point) | Existing today
Gross High Sustained Limit- changed to “Gross RT Power Potential” | New telemetry data point, added to reflect real-time power potential of IRR part | -
MW | Reflect actual power production of the plant (re-use the existing MW data point) | Existing today
Gross MW | Existing telemetry data point to reflect real-time power production of IRR part | Existing today
MW/HSL

## Slide 3: COP Update
ERCOT shares with the forecasting vendors the averaged GROSS RT Power Potential every 5 minutes as well as the meteorological data
Forecasting vendors will produce the forecast for GROSS Capability for the next 168 hours to estimate the power potential for IRR part
QSEs need to estimate the load consumption for PUN load or Crypto load for the next 168 hours
QSEs will deduct the estimated load consumption from the vendor-provided IRR forecast to update their COP HSL
  The COP HSL need to be reduced further if there is any equipment outage/derate not reported in the Outage Scheduler.

## Slide 4: Questions
Change to resource integration handbook
Pengwei.du@ercot.com