## Slide 1: Issue LFL - 41 Settlement of Price Sensitive Flexible Loads
Large Flexible Load Task Force
Floyd J. Trefny
October 24, 2022

## Slide 2: Background
Interval Data Recorders (IDR) meters measure retail load on 15-minute intervals
Load Zone Settlement Point Prices from ERCOT that retail consumers pay are based on 15-minute intervals.
  Calculated for each bus’s load weighted average of 5-minute bus LMPs from each SCED executed during the 15-minute period
  These 5-minute averages are further weighted by the change in system load over the 15 minute period
Retail Loads pay metered kWh multiplied by the 15-minute settlement point price
  There is a disconnect between what retail load pays and the 5-minute SCED prices that load may respond to
  Loads may not receive the proper price benefit of their demand response actions
  Discourages optimal demand response behavior

## Slide 3: Loads and Interruption Scenarios
 |  | SCED Intervals |  |  |  |  |  | 
Scenario | load | 5 | 10 | 15 |  | 15- Minute kWh | Price* | Cost
Base |  | Low price ($45) | Low price ($45) | Low price ($45) |  |  |  | 
 |  | 12,667 | 12,667 | 12,667 |  | 38,000 | $45 | $1,710
Large Loads look to the ERCOT postings of the Load Zone LMP from each SCED execution as the primary indicator of the eventual settlement point price
For example, a flat 152 MW load, consumes approximately
38,000 kWh every 15 minutes; 12,667 kWh for 5 minutes
*- 15-minute price assumes there is no effect from price weighting based on total load changes

## Slide 4: Loads and Interruption Scenarios
High Prices without an interruption costs significantly
An interruption of consumption in the first interval yields no cost, if it can be done quickly
  There is a delay in seeing the SCED prices on the ERCOT webpages
 |  | SCED Intervals |  |  |  |  |  | 
Scenario | load | 5 | 10 | 15 |  | 15- Minute kWh | Price* | Cost
Base |  | Low price ($45) | Low price ($45) | Low price ($45) |  |  |  | 
kWh |  | 12,667 | 12,667 | 12,667 |  | 38,000 | $45 | $1,710
 |  | High price ($3,000) | High price ($3,000) | High price ($3,000) |  |  |  | 
No Interruption - kWh |  | 12,667 | 12,667 | 12,667 |  | 38,000 | $3,000 | $114,000
*- 15-minute price assumes there is no effect from price weighting based on total load changes

## Slide 5: Loads and Interruption Scenarios
 |  | SCED Intervals |  |  |  |  |  | 
Scenario | load | 5 | 10 | 15 |  | 15- Minute kWh | Price* | Cost
Base |  | Low price ($45) | Low price ($45) | Low price ($45) |  |  |  | 
kWh |  | 12,667 | 12,667 | 12,667 |  | 38,000 | $45 | $1,710
 |  | High price ($3,000) | High price ($3,000) | High price ($3,000) |  |  |  | 
No Interruption - kWh |  | 12,667 | 12,667 | 12,667 |  | 38,000 | $3,000 | $114,000
 |  | Low price ($45) | High price ($3,000) | High price ($3,000) |  |  |  | 
Interrupt second interval - kWh |  | 12,667 | 0 | 0 |  | 12,667 | $2,015 | $ 25,523
*- 15-minute price assumes there is no effect from price weighting based on total load changes
High Prices in second and third interval costs even if the consumer interrupts as soon as 5- minute SCED prices are posted
Consumer should only be paying $570

## Slide 6: Loads and Interruption Scenarios
 |  | SCED Intervals |  |  |  |  |  | 
Scenario | load | 5 | 10 | 15 |  | 15- Minute kWh | Price* | Cost
Base |  | Low price ($45) | Low price ($45) | Low price ($45) |  |  |  | 
 |  | 12,667 | 12,667 | 12,667 |  | 38,000 | $45 | $1,710
 |  | High price ($3,000) | High price ($3,000) | High price ($3,000) |  |  |  | 
No Interruption |  | 12,667 | 12,667 | 12,667 |  | 38,000 | $3,000 | $114,000
 |  | Low price ($45) | High price ($3,000) | High price ($3,000) |  |  |  | 
Interrupt second interval |  | 12,667 | 0 | 0 |  | 12,667 | $2,015 | $ 25,523
 |  | Low price ($45) | Low price ($45) | High price ($3,000) |  |  |  | 
Interrupt third interval - kWh |  | 12,667 | 12,667 | 0 |  | 25,333 | $1,030 | $ 26,093
*- 15-minute price assumes there is no effect from price weighting based on total load changes
Consumer should only be paying $1,140

## Slide 7: Fixes
Generators (maybe CLRs) do not have the same problem as price responding loads
  Protocol section 6.6.3.1, Real-Time Energy Imbalance Payment or Charge at a Resource Node, addressed a similar problem with generation settlements
  ERCOT uses Base Points to adjust 15-minute energy data into 5 minute data for settlement purposes
Structure of Load settlement equations make it difficult to easily change calculations for individual loads
  Loads are summed up individually for each QSE by LZ and then pricing is applied to result in a charge to a QSE
  Use AMI metering or Load Telemetry to ERCOT to make adjustments to QSE settlement equations
  Settle Loads that desire 5-minute settlement who install appropriate metering