## Slide 1
NPRR1149 Implementation of Systematic Ancillary Service Failed Quantity Charges
WMWG
November 18, 2022

## Slide 2: NPRR1149 Background
In May 2019, ERCOT filed NPRR947, Clarification to Ancillary Service Supply Responsibility Definition and Improvements to Determining and Charging for Ancillary Service Failed Quantities, which proposed very similar changes as proposed in this NPRR. NPRR947 was withdrawn by ERCOT after months of deliberation because, although it is important to ensure that QSEs are providing the Ancillary Services for which they are being compensated, the improvements proposed in NPRR947 were deemed to be made obsolete and the issue would be resolved by the implementation of Real-Time Co-Optimization (RTC) of energy and Ancillary Services, scheduled for implementation in 2024.
As is widely known today, the effort to implement RTC is currently on hold and a new date for expected implementation is unknown.

## Slide 3: NPRR1149 Background
Following winter storm Uri, the ERCOT Independent Market Monitor (IMM), Potomac Economics, filed a recommendation at the PUCT in Project 51812, Issues Related to the State of Disaster for the February 2021 Winter Weather Event, that ERCOT should charge failed quantities based on Real-Time telemetry and outcomes during the storm.
The PUCT agreed with this recommendation (See Second Order Addressing Ancillary Services under Project No. 51812) and applicable charges were issued to QSEs by ERCOT.
ERCOT again proposes to implement a systemic charging of Ancillary Service failed quantities. This NPRR implements that process permanently for all periods and in a more systematic way, ensuring that Load is not charged or is reimbursed for Ancillary Services that are not delivered in Real-Time. It also addresses short-comings in the previously applied process for Load Resources that are not Controllable Load Resources that were not included in ERCOT’s application of the PUCT’s Order in 2021.

## Slide 4: Failed Quantities in 2022 – Jan 1 through Oct 31
Count of QSE’s per day, who had a daily AS shortage greater than 1 MWh/day, per AS type:
The sum of AS shortage amounts (MWh/day), considering the resources in the above count:
Product | Min | Mean | Max
REGDN | 1 | 2.39 | 7
REGUP | 1 | 3.42 | 7
RRS | 3 | 9.27 | 16
NSPIN | 1 | 2.46 | 8
Product | Min | Mean | Max
REGDN | 1 | 36 | 302
REGUP | 1 | 69 | 490
RRS | 6 | 118 | 3674
NSPIN | 1 | 121 | 1528

## Slide 5: NPRR1149 Key Functions
Clarify what is considered a Failure of AS Responsibility under 6.4.9.1.3:
  A QSE is considered to have failed on its Ancillary Services Supply Responsibility when ERCOT determines, in its sole discretion, that some or all of the QSE’s Ancillary Service capacity will not be available in Real-Time, was not available during any interval for which the QSE had an Ancillary Service Supply Responsibility, or that the QSE assigned all or part of an Ancillary Service Supply Responsibility to a Resource that has not been qualified to provide that Ancillary Service.
The addition of the Systematic Failed Quantity process will not replace the actions taken by the ERCOT operator. The Control Room will continue to assess shortages to AS during Real-Time and replace with a SASM if they so choose. This new process will account for those replacements at the end of the Operating Day.

## Slide 6: NPRR1149 Key Functions
Enhancing language in Section 4.4.7.4 to clarify that although a QSE may hold an Ancillary Service Supply Responsibility without having Resources, that responsibility must be met by Resources in Real-Time. The language proposed in this section does not create new responsibilities but clarifies existing requirements for how a QSE must meet its Ancillary Service Supply Responsibility.
  (5) A QSE’s Ancillary Service Supply Responsibility must be met by identified Resources that are qualified to provide the Ancillary Service, per Section 8.1.1.2.1 Ancillary Service Technical Requirements and Qualification Criteria and Test Methods and available to act on Dispatch Instructions.

## Slide 7: NPRR1149 Key Functions
A charge to each QSE that fails on its Ancillary Service Supply Responsibility, whether or not a SASM is executed due to its failure to supply, is calculated by service for a given Operating Hour following this general formula:
Sum of QSEs:
(Self Arranged + Trades (QSE is seller) + SASM Award + DAM Award + RUC Award) – (Trades (QSE is buyer) + Failed Quantity + Infeasible Failed Quantity)
Minus
Sum of Telemetered Responsibility for all QSE’s Resources

## Slide 8: NPRR1149 Key Functions
Special handling has been added to take a snapshot of the Responsibility prior to a deployment event for Load Resources due to behavior observed during Winter Storm Uri:
Where for Load Resources, other than Controllable Load Resources, during an RRS (also Non-Spin and ECRS) deployment event:
Telemetry: snapshot to be used will be from the time of deployment until 180 minutes after recall or if the time between a recall of Load Resources and a redeployment is less than 180 minutes, the snapshot to be used will be the time of the first deployment
Telemetry used prior to an event will be Min (NPF q, r – LPC q, r, TELRRSR q, r)

## Slide 9: NPRR1149 Proposed Formula for Responsive Reserve Failed Quantity
RRFQAMTQSETOT q = RRFQAMT q + RRRFQAMT q
Where:
RRFQAMT q = Max( MCPCRR m , AVGRTASIP) * (RRFQ q + TRRFQ q)
RRRFQAMT q = MCPCRR rs * RRRFQ q, rs
AVGRTASIP = (RTRSVPOR i + RTRDP i) / 4
Where for all Resources:
TRRFQ q = Max( [(SARRQ q + RRTRSQ q + ( RTPCRR q, m) + PCRR q + RUCRRQ q) – (RRTRPQ + RRFQ q +
RRRFQ q + RRINFQ q)] – TELRRSRC q, r, 0)
Where for Load Resources, other than Controllable Load Resources, during an RRS deployment event:
TELRRSRC q, r = Min (NPF q, r – LPC q, r, TELRRSR q, r) snapshot to be used will be from the time of deployment until 180 minutes after recall or if the time between a recall of Load Resources and a redeployment is less than 180 minutes, the snapshot to be used will be the time of the first deployment
Where for Load Resources, other than Controllable Load Resources, prior to an RRS deployment event:
TELRRSRC q, r = Min (NPF q, r – LPC q, r, TELRRSR q, r)
SARRQ q = DASARRQ q + RTSARRQ q

## Slide 10
Questions?