## Slide 1
Energy Storage Resource (ESR)
Dispatch and Settlement
Blake Holt
Market Design
11.18.2022

## Slide 2: Goals for today’s presentation
High level overview of current ESR modeling, energy offer and bid curves, and dispatch
High level overview of meter price composition
Fundamentals of Energy and Ancillary Service Imbalance
ESR settlement examples
Changes to this process coming with NPRR987 and OBDRR017

## Slide 3: ESR Modeling Today
Energy Storage Resources (ESRs) are currently modeled as two distinct units.
The Controllable Load Resource (ESR-CLR) and the battery (ESR-Gen) are dispatched and settled separately in the ERCOT systems.
This separation means that the two sides of the ESR must submit separate curves to indicate their willingness to charge from or dispatch energy into the grid.
The dispatch is based on the LMP at the electrical bus.
ESR-CLR bid curve
ESR-Gen energy offer curve

## Slide 4: Energy paid/charged meter prices, not “SPP”
Meter Price
RTLMP (LMP)
RTRSVPOR (ORDC)
RTRDP (RDPA)
ESR-CLR
ESR-Gen

## Slide 5: Energy and AS Imbalance settlement – Generator
Chart: 
RRS Award | 100 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 100

## Slide 6: Energy and AS Imbalance settlement – Generator
MCPC
Chart: 
RRS Award | 100 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 100
Notes: MCPC = Market Clearing Price for Capacity ($/MWh)

## Slide 7: Energy and AS Imbalance settlement – Generator
MCPC
Meter Price = LMP + ORDC + RDPA
Chart: 
RRS Award | 100 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 100
Notes: MCPC = Market Clearing Price for Capacity ($/MWh)
LMP = Locational Marginal Price ($/MWh)
ORDC = stands for the online reserve price adder ($/MWh)
RDAP = stands for the reliability deployment price adder ($/MWh)

## Slide 8: Energy and AS Imbalance settlement – Generator
MCPC
ORDC + RDPA
Meter Price = LMP + ORDC + RDPA
Chart: 
RRS Award | 100 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 100
Notes: MCPC = Market Clearing Price for Capacity ($/MWh)
LMP = Locational Marginal Price ($/MWh)
ORDC = stands for the online reserve price adder ($/MWh)
RDAP = stands for the reliability deployment price adder ($/MWh)

## Slide 9: Energy and AS Imbalance settlement – Generator
MCPC
ORDC + RDPA
Meter Price = LMP + ORDC + RDPA
Chart: 
RRS Award | 100 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 100
Notes: MCPC = Market Clearing Price for Capacity ($/MWh)
LMP = Locational Marginal Price ($/MWh)
ORDC = stands for the online reserve price adder ($/MWh)
RDAP = stands for the reliability deployment price adder ($/MWh)

## Slide 10: Energy and AS Imbalance settlement – Generator
MCPC
ORDC + RDPA
Meter Price = LMP + ORDC + RDPA
ORDC+
RDPA
Chart: 
RRS Award | 100 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 100
Notes: MCPC = Market Clearing Price for Capacity ($/MWh)
LMP = Locational Marginal Price ($/MWh)
ORDC = stands for the online reserve price adder ($/MWh)
RDAP = stands for the reliability deployment price adder ($/MWh)

## Slide 11: Energy and AS Imbalance settlement – Generator
MCPC
ORDC + RDPA
Meter Price = LMP + ORDC + RDPA
ORDC+
RDPA
DAM payment for Procured Capacity for RRS
(PCRRAMT)
Chart: 
RRS Award | 100 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 100
Ancillary Service Imbalance Charge
(RTASIAMT)
Ancillary Service Imbalance Payment
(RTASIAMT)
Energy Imbalance Payment
(RTEIAMT)
Key Take-Away:
When AS is deployed, a generator is only paid LMP + MCPC for the AS capacity that was reserved and deployed.
Notes: MCPC = Market Clearing Price for Capacity ($/MWh)
LMP = Locational Marginal Price ($/MWh)
ORDC = stands for the online reserve price adder ($/MWh)
RDAP = stands for the reliability deployment price adder ($/MWh)

## Slide 12: Energy and AS Imbalance settlement – CLR
Chart: MW
RRS award | 10 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 10

## Slide 13: Energy and AS Imbalance settlement – CLR
Chart: MW
RRS award | 10 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 10
MCPC

## Slide 14: Energy and AS Imbalance settlement – CLR
Chart: MW
RRS award | 10 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 10
MCPC
ORDC + RDPA

## Slide 15: Energy and AS Imbalance settlement – CLR
Chart: MW
RRS award | 10 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 10
MCPC
ORDC + RDPA
Meter Price = LMP + ORDC + RDPA

## Slide 16: Energy and AS Imbalance settlement – CLR
Chart: MW
RRS award | 10 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 10
MCPC
ORDC + RDPA
DAM payment for Procured Capacity for RRS
(PCRRAMT)
Ancillary Service Imbalance Payment
(RTASIAMT)
Energy Imbalance Charge
(RTEIAMT)
Meter Price = LMP + ORDC + RDPA
Key Take-Away:
A CLR is only charged LMP when consuming.

## Slide 17: ESR dispatch and settlement - normal
When the LMP rises above $60 the ESR-Gen is willing to generate. It gets a dispatch instruction of 10 to 20MW.
When the LMP drops below $40 the ESR-CLR is willing to charge. It gets a dispatch instruction of 15MW.
Chart: 100MW ESR example
ESR-CLR basepoint | 0 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | 0
ESR-Gen basepoint | 0 | 10 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 15 | 15 | 10 | 10 | 10 | 0
* positive dollars = payment, negative dollars = charge
 | ESR-CLR
Energy Imbalance (LMP) | (2,888)
Energy Imbalance (ORDC) | (825)
Energy Imbalance (RDPA) | (413)
 | ESR-Gen
Energy Imbalance (LMP) | 4,175
Energy Imbalance (ORDC) | 575
Energy Imbalance (RDPA) | 288

## Slide 18: ESR dispatch and settlement - normal
When the ESR-CLR is charging, the load is treated as online reserve. The ESR-Gen is also online (at a reduced state of charge) and providing online reserve with its dispatchable range.
When the ESR-Gen is online and generating below its HSL, the dispatchable range is treated as online reserve.
 | ESR-CLR
Energy Imbalance (LMP) | (2,888)
Energy Imbalance (ORDC) | (825)
Energy Imbalance (RDPA) | (413)
AS Imbalance (ORDC) | 825
AS Imbalance (RDPA) | 413
Net | (2,888)
 | ESR-Gen
Energy Imbalance (LMP) | 4,175
Energy Imbalance (ORDC) | 575
Energy Imbalance (RDPA) | 288
AS Imbalance (ORDC) | 2,925
AS Imbalance (RDPA) | 1,463
Net | 9,425
* positive dollars = payment, negative dollars = charge
Chart: 100MW ESR example
ESR-CLR basepoint | 0 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | 0
ESR-Gen basepoint | 0 | 10 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 15 | 15 | 10 | 10 | 10 | 0
ESR-Gen Online Reserve
ESR-CLR Online Reserve
ESR-Gen Online Reserve
 | ESR-Gen
AS Imbalance (ORDC) | 2,750
AS Imbalance (RDPA) | 1,375
Net | 4,125
50 HSL
100 HSL

## Slide 19: ESR dispatch and settlement - normal
* positive dollars = payment, negative dollars = charge
The ESR-CLR is essentially only charged LMP for consuming. The payments & charges from the ORDC and RDPA adders cancel out.
The ESR-Gen gets paid LMP+ORDC+RDPA for generation, and ORDC+RDPA for any headroom while online.
 | ESR-CLR
Energy Imbalance (LMP) | (2,888)
Energy Imbalance (ORDC) | (825)
Energy Imbalance (RDPA) | (413)
AS Imbalance (ORDC) | 825
AS Imbalance (RDPA) | 413
Net | (2,888)
 | ESR-Gen
Energy Imbalance (LMP) | 4,175
Energy Imbalance (ORDC) | 575
Energy Imbalance (RDPA) | 288
AS Imbalance (ORDC) | 2,925
AS Imbalance (RDPA) | 1,463
Net | 9,425
Chart: 100MW ESR example
ESR-CLR basepoint | 0 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | 0
ESR-Gen basepoint | 0 | 10 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 20 | 15 | 15 | 10 | 10 | 10 | 0
ESR-Gen Online Reserve
ESR-CLR Online Reserve
ESR-Gen Online Reserve
50 HSL
100 HSL
 | ESR-Gen
AS Imbalance (ORDC) | 2,750
AS Imbalance (RDPA) | 1,375
Net | 4,125

## Slide 20: ESR dispatch and settlement - extreme
When the LMP drops below $2000 the ESR-CLR is willing to charge. It gets a dispatch instruction of 15MW.
When the LMP rises above $2000 the ESR-Gen is willing to generate. It gets a dispatch instruction of 100MW.
* positive dollars = payment, negative dollars = charge
Chart: 100MW ESR example
ESR-CLR basepoint | 0 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | 0
ESR-Gen basepoint | 0 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 0
 | ESR-CLR
Energy Imbalance (LMP) | (79,290)
Energy Imbalance (ORDC) | (9,956)
Energy Imbalance (RDPA) | (192,004)
 | ESR-Gen
Energy Imbalance (LMP) | 769,373
Energy Imbalance (ORDC) | 18,465
Energy Imbalance (RDPA) | 212,162

## Slide 21: ESR dispatch and settlement - extreme
When the ESR-CLR is charging, the load is treated as online reserve. The ESR-Gen is also online (at a reduced state of charge) and providing online reserve with its dispatchable range.
The ESR-Gen is dispatched up to its HSL and does not receive any additional payments for providing online reserve. The entire unit is being used for energy.
 | ESR-CLR
Energy Imbalance (LMP) | (79,290)
Energy Imbalance (ORDC) | (9,956)
Energy Imbalance (RDPA) | (192,004)
AS Imbalance (ORDC) | 9,956
AS Imbalance (RDPA) | 192,004
Net | (79,290)
 | ESR-Gen
Energy Imbalance (LMP) | 769,373
Energy Imbalance (ORDC) | 18,465
Energy Imbalance (RDPA) | 212,162
AS Imbalance (ORDC) | 0
AS Imbalance (RDPA) | 0
Net | 1,000,000
* positive dollars = payment, negative dollars = charge
Chart: 100MW ESR example
ESR-CLR basepoint | 0 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | 0
ESR-Gen basepoint | 0 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 0
ESR-Gen On Rsv
ESR-CLR On Rsv
 | ESR-Gen
AS Imbalance (ORDC) | 26,549
AS Imbalance (RDPA) | 512,010
Net | 538,559
40 HSL

## Slide 22: ESR dispatch and settlement - extreme
Chart: 100MW ESR example
ESR-CLR basepoint | 0 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | -15 | 0
ESR-Gen basepoint | 0 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 0
The ESR-CLR is essentially only charged LMP for consuming. The payments & charges from the ORDC and RDPA adders cancel out.
The ESR-Gen gets paid LMP+ORDC+RDPA for generation, and ORDC+RDPA for any headroom while online.
* positive dollars = payment, negative dollars = charge
 | ESR-Gen
AS Imbalance (ORDC) | 26,549
AS Imbalance (RDPA) | 512,010
Net | 538,559
ESR-Gen On Rsv
ESR-CLR On Rsv
40 HSL
 | ESR-CLR
Energy Imbalance (LMP) | (79,290)
Energy Imbalance (ORDC) | (9,956)
Energy Imbalance (RDPA) | (192,004)
AS Imbalance (ORDC) | 9,956
AS Imbalance (RDPA) | 192,004
Net | (79,290)
 | ESR-Gen
Energy Imbalance (LMP) | 769,373
Energy Imbalance (ORDC) | 18,465
Energy Imbalance (RDPA) | 212,162
AS Imbalance (ORDC) | 0
AS Imbalance (RDPA) | 0
Net | 1,000,000

## Slide 23: ESR dispatch and settlement – post NPRR987 and OBDRR017
The remaining portions of NPRR987 and ODBRR017 will be implemented at a future date and will incorporate an ESR state of charge into the ORDC pricing and AS Imbalance settlement
Real-Time Energy Imbalance pricing and settlement will remain the same
OBDRR017 changes
Rs = RTOLCAP = RTOLHSL – RTBP + RTCLRCAP + RTNCLRCAP + RTESRCAP – RTOLNSRS – RTPBPC
RTESRCAP = Min(ESR Gen HSL – ESR Gen Base Point, SOC Telem – SOC OperMin) + ESR CLR Base Point