## Slide 1: ERCOT IBRTF: NERC and Other Industry Updates
Julia Matevosyan
12/01/2022
Chief Engineer
ESIG

## Slide 2: Agenda
FERC Order and Notice of Proposed Rulemaking (NOPR)
Upcoming NERC Reliability Guideline: EMT Modeling and Simulations

## Slide 3: Recent FERC Order E-1 and NOPR E-2
Items E-1 and E-2, an order and a NOPR directed to NERC, to account for the increasing number of IBRs in the resource mix.
Items E-1 and E-2 are supported by NERC event reports, Alerts, Reliability Guidelines, and other technical reports and white papers – pertaining to the effects of IBRs on the reliability of the Bulk-Power System (BPS).

## Slide 4: FERC Order E-1
Item E-1 is an order directing NERC to submit (within 90 days) a plan for identification and registration of owners and operators of BPS-connected IBRs that are currently not required to register but, in the aggregate, have a material impact on the reliability of the BPS. These IBRs are currently not required to comply with mandatory Reliability Standards or respond to NERC Alerts.
The order directs NERC to do three things.
  To complete modifications to its registration processes in ≤ 12 months after FERC’s approval of the plan.
  To identify all owners and operators of such IBRs in ≤ 24 months of FERC’s approval of the plan.
  To register owners and operators of such IBRs in ≤ 36 months after FERC’s approval of the plan.
The order acknowledges that NERC may determine that only a subset of Reliability Standard Requirements need not apply to all newly registered IBR generator owners or operators.

## Slide 5: FERC NOPR E-2
Item E-2 is a NOPR preliminarily finding that the Reliability Standards do not fully address the impacts of IBRs on the reliable operation of the BPS.
The NOPR proposes to direct NERC to develop new or modified Reliability Standards that address four reliability gaps related to IBRs.
  Data sharing: currently, IBR owners and operators do not consistently share IBR planning and operational data, and the information that is shared is often inaccurate or incomplete.
  Model validation: once planners have IBR data, they must ensure the accuracy of such data to create valid system models.
  Planning and operational studies: once planners and operators validate system models, they must include those models in planning and operational studies to assess the reliability impacts—both of individual and collective IBRs—on Bulk-Power System performance.
  Performance requirements, such as IBRs’ ability to ride through system disturbances.

## Slide 6: FERC NOPR E-2
The NOPR proposes to direct NERC to submit a compliance filing detailing a plan explaining how NERC will prioritize the development and implementation of new or modified Reliability Standards to address these four reliability gaps.
The plan is to be submitted by NERC within 90 days of the effective date of the final rule
NERC’s plan should take into account:
  the risks posed to the reliable operation of the BPS,
  standards already underway,
  resource constraints, and
  other factors as necessary.
Comments in response to the NOPR would be due 60 days after the date of publication in the Federal Register, with reply comments due 30 days later.
https://www.ferc.gov/news-events/news/joint-presentation-items-e-1-registration-inverter-based-resources-and-e-2

## Slide 7: NERC IBR Strategy
Risk Analysis
Event Analysis
Disturbance Reports
Interconnection Process Improvements
Best Practices and Education
Regulatory Enhnacements
Inverter-Specific Requirements and Standards
Reliability Guidelines
Outreach and Engagement
Webinars and Workshops
Enhanced Interconnection Requirements
IEEE 2800-2022
Improvements to GIAs and GIP
Modeling and Study Improvements
NERC Standards Projects
BES Definition Review
Risk-Based Compliance
Emerging Reliability Risk Issues
Alerts
Lessons Learned
NERC IBR Strategy

## Slide 8: Why EMT Guidelines?
Studying and de-risking some of the causes of the recent disturbance events is only possible with EMT models:
  Majority of grid faults are unbalanced
  Control instability and interaction with other IBRs
  Causes of IBR trip/output reduction from recent disturbance reports
    Instantaneous inverter AC overcurrent
    Instantaneous inverter AC overvoltage
    Inverter DC unbalance protection
    Unbalance current protection
To address gaps identified in recent disturbance reports
    Models not matching facilities
    Inability to reproduce unreliable performance reported – trips, output reduction

## Slide 9: Reliability Guideline: EMT Modeling and Simulation - in 2 parts Vol. 1: EMT Model Requirements and Quality Control Enable TP, PC, GO obtain and verify high quality EMT models - Modeling requirements - Model quality assessment - Screening for EMT study need: how to tell if EMT studies are needed - Assess ride-through capability and performance - Resourcing for EMT studies - Different flavors of EMT models Vol. 2: EMT Studies - Scoping detailed EMT studies - Building EMT study models - Interconnection studies - Transmission planning studies - Material modification and model updates during interconnection study process and post COD

## Slide 10: Vol 1 - Schedule
Schedule for Vol 1 Publication
Key Dates | Milestones
Dec 15, 2022 | Consensus to post for public comment at IRPS monthly meeting
Dec 16, 2022 | Draft out to RSTC for review to authorize via email ballot posting for comment
Feb 2023 | Incorporate comments
Mar 2023 | RSTC final approval and publication

## Slide 11
Julia Matevosyan
julia@esig.energy