## Slide 1
Annual Review of the Market Impacts of Reliability Unit Commitments
Analysis of 2022
Dave Maggio
ERCOT
Technical Advisory Committee (TAC)
January 24, ‘23
ERCOT Public

## Slide 2: Protocol Language
5.8 Annual RUC Reporting Requirement
(1) ERCOT shall report to the Technical Advisory Committee (TAC), each January, an assessment of market impacts and Settlements for the aggregate Reliability Unit Commitment (RUC) activity, delineated by type of RUC instruction as follows:
RUC instructions issued for Ancillary Service shortages (failure to sufficiently procure one or more Ancillary Service markets in the Day-Ahead Market (DAM) or subsequent Supplemental Ancillary Service Markets (SASMs));
RUC instructions issued for irresolvable transmission system constraints;
RUC instructions issued in anticipation of extreme cold weather/startup failures;
RUC instructions issued for capacity;
RUC instructions issued for system inertia; and
A summary of RUC Settlements;
(i) RUC charges associated with RUC Make-Whole Amount Total per RUC, as defined in Section 5.7.4.1, RUC Capacity-Short Charge; and
(ii) RUC Shortfall Total, as defined in Section 5.7.4.1.1, Capacity Shortfall Ratio Share.

## Slide 3: RUC-Instructed Resource-Hours in 2022
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, partial hour instructions, or otherwise not dispatchable by SCED.
 | Total | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  | 
Total Count | 8,244.8 | 1,651.0 | 6,593.9
Effective Resource-Hours* |  |  | 
Total Count | 7,910.5 | 1,610.0 | 6,300.5
Average LSL | 76.9 | 89.6 | 73.6
Average LDL | 96.8 | 174.9 | 76.8
Average BP | 102.3 | 195.2 | 78.5
Average HSL | 294.2 | 323.7 | 286.6

## Slide 4: RUC Instruction Reasons
7,910.5 effective RUC Resource-hours in 2022.
  1,023.6 Resource-hours (12.9%) for local thermal congestion or voltage concerns.
  6,886.8 Resource-hours (87.1%) for capacity concerns.
There were no Resource-hours committed for Ancillary Service shortages, system inertia, or startup failures.
1,610.0 effective Resource-hours (20.4%) were successfully bought back.
  This value is lower than last year (31% bought back in 2021).
  Included in this value are 135.5 effective Resource-hours (1.7% of total) where the Resource was DAM-committed.

## Slide 5: RUC-Instructed Effective Resource-Hours, 2019 - 2022

## Slide 6: RUC-Instructed Effective Resource-MWh, 2019 - 2022
Top: Duration multiplied by Resource’s Base Point (BP).
Bottom: Duration multiplied by Resource’s High Sustained Limit (HSL).

## Slide 7: Average Age of Effective Resource-Hours, 2019 - 2022
In the case of Resources with multiple physical generators, the age of the oldest generator is used.

## Slide 8: RUC-Instructed Effective Resource-Hours by Resource Age, 2019 - 2022
Top: non-opt-out Resource-hours.
Bottom: opt-out Resource-hours.
In the case of Resources with multiple physical generators, the age of the oldest generator is used.

## Slide 9: RUC-Instructed Resource Dispatch above LDL
When Resources did not successfully opt out, there were ~281 Resource-hours when the Resource was dispatched above its LDL.
  For 59.7 of these Resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 221.4 of these Resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
    For 214.7 of these Resource-hours, the RUC-instructed Resource was mitigated.
    6.8 of these Resource-hours are associated with a RUC for additional capacity.
    There were no Resource-hours for which a non-mitigated RUC-instructed Resource was DAM-committed. (Hours meeting these criteria are treated as a RUC opt out.)

## Slide 10: Reliability Deployment Price Adder
Month of 2022 | Total RTORDPA Time (Hours) | Time-weighted Average RTORDPA ($/MWh)
Jan | 37.0 | 0.67
Feb | 162.0 | 9.16
Mar | 68.2 | 3.32
Apr | 97.9 | 2.78
May | 160.5 | 3.11
Jun | 143.4 | 1.21
Jul | 221.2 | 15.81
Aug | 227.8 | 2.39
Sep | 363.9 | 1.35
Oct | 123.5 | 2.04
Nov | 218.6 | 1.88
Dec | 86.7 | 0.95

## Slide 11: RUC Make-Whole and Claw Back, 2019 - 2022
$39.942M in Make-Whole paid out. $39.47 uplifted to Load.

## Slide 12: Conclusions
In 2022, 8,244.8 instructed RUC Resource-hours resulted in 7,910.5 effective RUC Resource-hours.
  As compared to 4,052.0 and 3,853.1 for 2021, respectively.
  20.4% of effective resource-hours were bought back.
The total RUC make-whole amount was ~$34.109M.
  Almost exclusively covered through capacity-short charges.
The total RUC claw back charge amount was ~$24.846M.

## Slide 13: Appendix

## Slide 14: RUC-Instructed Effective Resource-Hours by Opt Out Status*
Month | 2019 | 2020 | 2021 | 2022
Jan | 0 | 3 | 5 | 80
Feb | 0 | 12 | 5 | 930
Mar | 8 | 1 | 5 | 200
Apr | 16 | 0 | 8 | 328
May | 59 | 0 | 0 | 382
Jun | 15 | 0 | 248 | 511
Jul | 0 | 21 | 968 | 672
Aug | 0 | 151 | 378 | 870
Sep | 8 | 0 | 339 | 1,124
Oct | 34 | 0 | 573 | 305
Nov | 4 | 3 | 107 | 517
Dec | 1 | 0 | 11 | 381
Month | 2019 | 2020 | 2021 | 2022
Jan | 0 | 0 | 0 | 26
Feb | 11 | 0 | 269 | 62
Mar | 0 | 0 | 24 | 62
Apr | 6 | 0 | 63 | 163
May | 13 | 6 | 0 | 219
Jun | 0 | 0 | 89 | 108
Jul | 0 | 11 | 229 | 236
Aug | 8 | 8 | 203 | 176
Sep | 19 | 0 | 139 | 225
Oct | 0 | 4 | 102 | 106
Nov | 0 | 0 | 73 | 209
Dec | 0 | 0 | 14 | 19
Did Not Opt Out
Opted Out
* Effective Resource-hours rounded to nearest whole number

## Slide 15: RUC Make-Whole and Claw Back, 2019-2020
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2019 | 2020 | 2019 | 2020 | 2019 | 2020 | 2019 | 2020 | 2019 | 2020
Jan | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 0
Feb | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 168 | 0 | 394
Mar | -9 | 0 | 9 | 0 | 0 | 0 | 0 | 19 | 253 | 0
Apr | -8 | 0 | 8 | 0 | 0 | 0 | 0 | 0 | 359 | 0
May | -13 | 0 | 13 | 0 | 0 | 0 | 108 | 0 | 915 | 0
Jun | -4 | 0 | 4 | 0 | 0 | 0 | 3 | 0 | 738 | 0
Jul | 0 | -40 | 0 | 40 | 0 | 0 | 0 | 82 | 0 | 148
Aug | 0 | -356 | 0 | 356 | 0 | 0 | 0 | 210 | 0 | 2197
Sep | -11 | 0 | 11 | 0 | 0 | 0 | 1 | 0 | 110 | 0
Oct | -3 | 0 | 3 | 0 | 0 | 0 | 726 | 0 | 229 | 0
Nov | 0 | -8 | 0 | 8 | 0 | 0 | 49 | 0 | 0 | 140
Dec | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 0 | 0 | 0
Amounts rounded to nearest thousand. Data retrieved on 01/11/2023.

## Slide 16: RUC Make-Whole and Claw Back, 2021-2022
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2021 | 2022 | 2021 | 2022 | 2021 | 2022 | 2021 | 2022 | 2021 | 2022
Jan | 0 | -320 | 0 | 320 | 0 | 0 | 1 | 38 | 0 | 3,760
Feb | 0 | -6,970 | 0 | 6,970 | 0 | 0 | 1,256 | 7,628 | 0 | 7,519
Mar | -9 | -749 | 9 | 749 | 0 | 0 | 6 | 102 | 239 | 6,203
Apr | -19 | -742 | 19 | 742 | 0 | 0 | 0 | 1,285 | 263 | 7,138
May | 0 | -3,302 | 0 | 3,302 | 0 | 0 | 0 | 7,293 | 0 | 10,604
Jun | -466 | -6,014 | 466 | 6,014 | 0 | 0 | 91 | 12 | 7,004 | 17,784
Jul | -2,045 | -4,702 | 2,045 | 4,702 | 0 | 0 | 637 | 5,509 | 17,404 | 17,815
Aug | -865 | -3,464 | 865 | 3,464 | 0 | 0 | 59 | 986 | 12,626 | 14,129
Sep | -833 | -4,666 | 833 | 4,666 | 0 | 0 | 54 | 365 | 11,812 | 20,059
Oct | -862 | -889 | 862 | 889 | 0 | 0 | 918 | 528 | 9,766 | 7,153
Nov | -61 | -809 | 61 | 809 | 0 | 0 | 89 | 952 | 1,312 | 8,361
Dec | -86 | -1,479 | 86 | 1,479 | 0 | 0 | 0 | 148 | 1,102 | 6,437
Amounts rounded to nearest thousand. Data retrieved on 01/11/2023.