## Slide 1
2022 Analysis of REP and NOIE Demand Response
Carl L Raish
Principal Load Profiling and Modeling
Retail Market Subcommittee – Feb 7, 2022

## Slide 2: Overview
  Summer 2021 Analysis Update
  Total System-level Demand Response
    Total ERCOT Demand Response
    Responding NOIE and ESIID counts
  4CP Participation Trends
  DR/PR Events

## Slide 3
Total System-Level Demand Response

## Slide 4: Load Reductions by Category/System Level
HE 17:00 MW Reductions
Table shows Days with Total System DR > 3,000 MW (59 days > 50 MW)
Overlap = Category Total – Total System DR (To eliminate double counting)

## Slide 5: ESIIDs/NOIEs by Category/System Level
HE 17:00 ESIIDs/NOIEs with Reductions
Table shows Days with Total System DR > 3,000 MW (59 days > 50 MW)
Overlap = Category Total – Total System DR (To eliminate double counting)

## Slide 6: Responding ESIIDs and Reductions
Table Shows Days with Total System DR > 3,500 MW

## Slide 7: Responding NOIEs and Reductions
Days with Total System DR > 3,500 MW

## Slide 8: Total Competitive and NOIE Demand Response
Day with Highest Total System DR

## Slide 9: Total Competitive and NOIE Demand Response
Day with 2nd Highest Total System DR - ERCOT Peak Day

## Slide 10: Total Competitive and NOIE Demand Response
Day with 3rd Highest Total System DR – ERS Deployed

## Slide 11
Price Response and Retail DR Participation Trends

## Slide 12: 4CP Response Trend
Blue Squares: 4CP Days Red Circles: HE17 Price > $500
Red Arrows: HE17 Price > $1,000
2014
2015
2016
2017
2018
2019
2020
2021
2022

## Slide 13: 4CP Response Trend

## Slide 14: Indexed Real Time Response Trend
2019
2020
2021
2022

## Slide 15: NOIE Real Time Response Trend
2019
2020
2021
2022

## Slide 16
DR/PR Events

## Slide 17: 4CP Events 2022
4CP Days
Date | ESIIDs | HE 17 Reduce MW | NOIEs | HE 17 Reduce MW | Total
23-Jun | 4,005 | 1,863 | 18 | 1,275 | 3,138
20-Jul | 3,525 | 1,915 | 21 | 1,771 | 3,687
2-Aug | 3,326 | 1,616 | 15 | 1,068 | 2,684
20-Sep | 4,602 | 2,002 | 17 | 978 | 2,980

## Slide 18: 4CP/NearCP Events 2022
Near-CP Days
Date | ESIIDs | NOIEs | HE 17 Reduce MW
6-Jun | 3,755 | 11 | 2,013
7-Jun | 3,654 | 18 | 2,500
8-Jun | 4,820 | 10 | 1,877
9-Jun | 3,302 | 11 | 2,081
10-Jun | 4,231 | 20 | 3,364
13-Jun | 4,735 | 22 | 3,394
16-Jun | 4,258 | 20 | 3,189
20-Jun | 3,613 | 15 | 2,821
21-Jun | 4,217 | 14 | 2,012
24-Jun | 4,423 | 17 | 3,399
Date | ESIIDs | NOIEs | HE 17 Reduce MW
6-Jul | 3,590 | 16 | 1,842
7-Jul | 3,588 | 19 | 2,635
8-Jul | 4,019 | 20 | 3,427
11-Jul | 4,289 | 21 | 4,453
12-Jul | 3,794 | 18 | 3,299
13-Jul | 3,787 | 20 | 3,449
18-Jul | 3,132 | 17 | 2,550
19-Jul | 3,434 | 20 | 3,640
27-Jul | 3,711 | 13 | 1,522
28-Jul | 3,773 | 13 | 1,645
41 Near-CP Days, reductions 1,051 – 4,453 MW

## Slide 19: 4CP/NearCP Events 2022
Near-CP Days (cont.)
Date | ESIIDs | NOIEs | HE 17 Reduce MW
3-Aug | 3,322 | 19 | 2,643
4-Aug | 3,655 | 20 | 2,735
5-Aug | 4,708 | 4 | 1,233
9-Aug | 4,357 | 8 | 1,683
10-Aug | 3,858 | 5 | 1,637
11-Aug | 2,756 | 4 | 1,238
12-Aug | 3,771 | 16 | 1,388
16-Aug | 3,165 | 7 | 1,427
17-Aug | 2,970 | 9 | 1,838
23-Aug | 3,882 | 5 | 860
26-Aug | 3,718 | 7 | 1,497
Date | ESIIDs | NOIEs | HE 17 Reduce MW
1-Sep | 5,425 | 15 | 2,394
2-Sep | 5,793 | 12 | 1,593
6-Sep | 3,106 | 7 | 1,894
7-Sep | 3,651 | 15 | 3,272
8-Sep | 4,055 | 10 | 1,724
16-Sep | 4,348 | 4 | 1,352
19-Sep | 4,655 | 13 | 2,651
21-Sep | 4,236 | 17 | 3,039
22-Sep | 4,308 | 14 | 2,533
23-Sep | 4,432 | 10 | 2,317
41 Near-CP Days, reductions 1,051 – 4,453 MW

## Slide 20: Indexed Real-Time High Price Events
Date | ESIIDs | HE 17 Reduce MW | Avg Price $/MWh
13-Jun | 5,709 | 262 | $308
14-Jun | 6,779 | 171 | $357
15-Jun | 6,130 | 274 | $551
16-Jun | 6,435 | 248 | $435
8-Jul | 18,153 | 1,007 | $421
11-Jul | 18,016 | 1,018 | $308
12-Jul | 15,077 | 1,009 | $706
13-Jul | 18,240 | 1,066 | $2,810
18-Jul | 15,030 | 831 | $886
Table lists Days with Event Average Price > $300
20 Days with High Real-Time Prices (>$200) Reductions: 51 – 1,066 MW

## Slide 21: Indexed Real-Time High Price Events
Date | ESIIDs | HE 17 Reduce MW | Avg Price $/MWh
20-Jul | 15,496 | 974 | $940
3-Aug | 15,276 | 807 | $338
8-Aug | 16,575 | 481 | $426
9-Aug | 21,170 | 554 | $565
11-Aug | 14,183 | 517 | $353
17-Aug | 15,058 | 697 | $415
22-Aug | 21,801 | 288 | $345
23-Aug | 20,083 | 301 | $369
25-Aug | 15,247 | 279 | $302
6-Sep | 15,604 | 898 | $365
(Cont.)
Table lists Days with Event Average Price > $300
20 Days with High Real-Time Prices (>$200) Reductions: 51 – 1,066 MW

## Slide 22: Indexed Day-Ahead High Price Events
Date | ESIIDs | HE 17 Reduce MW | Avg Price $/MWh
High DA Only |  |  | 
10-Jun | 325 | 51 | $325
23-Jun | 304 | 58 | $401
14-Jul | 395 | 49 | $545
15-Jul | 378 | 54 | $353
19-Jul | 311 | 52 | $430
4-Aug | 299 | 53 | $314
10-Aug | 269 | 49 | $318
16-Aug | 291 | 52 | $306
Table lists Days with Event Average Price > $300
26 Days with High Day-Ahead Only Prices (>$200) Reductions: 2 – 60 MW

## Slide 23: Indexed Day-Ahead High Price Events
Date | ESIIDs | HE 17 Reduce MW | Avg Price $/MWh
High RT Only |  |  | 
13-Jun | 22 | 8 | $308
14-Jun | 37 | 7 | $357
29-Jun | 49 | 7 | $260
3-Aug | 319 | 57 | $338
22-Aug | 350 | 53 | $345
23-Aug | 354 | 69 | $369
6-Sep | 294 | 51 | $365
Table lists All Days with Response
7 Days with High Real-Time Only Reductions: 7 – 69 MW

## Slide 24: Indexed Day-Ahead High Price Events
Date | ESIIDs | HE 17 Reduce MW | Avg Price $/MWh
High DA & RT |  |  | 
6/15/2022 | 32 | 6 | $551
6/16/2022 | 24 | 8 | $435
7/8/2022 | 346 | 46 | $743
7/11/2022 | 355 | 31 | $1,131
7/12/2022 | 328 | 50 | $706
7/13/2022 | 355 | 48 | $2,810
7/18/2022 | 313 | 42 | $886
7/20/2022 | 319 | 55 | $940
8/8/2022 | 293 | 41 | $426
8/9/2022 | 399 | 45 | $565
8/11/2022 | 285 | 52 | $353
8/17/2022 | 339 | 52 | $415
8/25/2022 | 311 | 70 | $302
Avg Event Price: Greater
of DA or RT
All Days with Response
Reductions: 6 – 70 MW

## Slide 25: NOIE High Price Response Events
Date | NOIEs | HE 17 Reduce MW | Avg Price $/MWh
29-Jun | 1 | 59 | $260
8-Jul | 19 | 1,595 | $743
11-Jul | 17 | 2,370 | $421
12-Jul | 16 | 1,341 | $706
13-Jul | 13 | 1,301 | $2,810
18-Jul | 15 | 877 | $886
19-Jul | 1 | 225 | $391
20-Jul | 19 | 1,699 | $940
25-Jul | 1 | 144 | $378
Date | NOIEs | HE 17 Reduce MW | Avg Price $/MWh
3-Aug | 12 | 376 | $338
8-Aug | 5 | 208 | $426
9-Aug | 5 | 256 | $565
11-Aug | 4 | 189 | $353
17-Aug | 6 | 321 | $415
22-Aug | 14 | 678 | $345
23-Aug | 3 | 45 | $369
25-Aug | 2 | 28 | $302
6-Sep | 6 | 160 | $365
Table lists All Days with Response
18 Days with High Real-Time Only Reductions: 28 – 2,370 MW

## Slide 26: Direct Load Control Events
Date | ESIIDs | HE 17 Reduce MW | Avg Price $/MWh
13-Jun | 4,666 | 82 | $308
15-Jun | 10,932 | 84 | $551
23-Jun | 7,629 | 79 | ⃰ $71
8-Jul | 12,839 | 90 | $743
11-Jul | 12,166 | 89 | $421
12-Jul | 5,291 | 77 | $706
13-Jul | 12,191 | 86 | $2,810
18-Jul | 12,074 | 81 | $886
20-Jul | 13,446 | 90 | $840
4-Aug | 7,970 | 88 | ⃰ $73
Table lists Event Days with Reductions > 75 MW
47 Event Days with Reductions > 10 MW Reductions: 10 –90 MW
⃰ Not High Price Day

## Slide 27: Peak Rebate Events
Date | ESIIDs | HE 17 Reduce MW | Avg Price $/MWh
24-Jun | 36,510 | 41 | ⃰ $58
8-Jul | 41,111 | 51 | $743
11-Jul | 42,285 | 57 | $421
13-Jul | 42,735 | 54 | $706
14-Jul | 47,199 | 62 | ⃰ $55
18-Jul | 34,984 | 39 | $886
20-Jul | 40,507 | 49 | $391
4-Aug | 36,664 | 38 | ⃰ $73
10-Aug | 33,052 | 36 | ⃰ $74
16-Aug | 36,359 | 37 | ⃰ $97
17-Aug | 37,428 | 40 | $415
⃰ Not High Price Day

## Slide 28: ERS Event – Competitive Load Only
Date | ESIIDs | HE 17 Reduce MW | Avg Price $/MWh
13-Jul | 27,839 | 713 | $2,810
Differences from ERS Performance:
  Includes response from deployed ESIIDs:
    with no Time-Period 4 obligations
    in deployed Generator only Resources
  Best baseline by ESIID … weather sensitivity determined at ESIID-level
  Baseline days limited to non-4CP/high price days for ESIIDs responding on such days
  Event day-of-adjustment factor calculated using intervals 1 through the interval ending 1 hour prior to beginning of high price event
  MBMA baseline based on intervals prior to beginning of high prices
  Non-responding ESIIDs (<3% Load reduction) excluded

## Slide 29: Next Steps
Suggested OBDRR and possible NPRR (next month?)
  Discontinue NAESB submissions
  Modify ESIID List Provide
    Automatic (currently by request)
    Add dates for 4CP beginning
    Identify Crypto ESIIDs
    Add a solar buy-back category
    Other ???
Possible Winter Survey - snapshot date Feb 1.
Update Residential Consumption Analysis
Update Residential PV Analysis.
Training Session (timing? After Aug 1 so participation is locked down)

## Slide 30: Questions?
ON
OFF
craish@ercot.com 512/248-3876