## Slide 1
RRS-PFR Limits Study
Introduction
April 6, 2023
RRS-PFR Limits Study Workshop
Nitika Mago
Manager, Balancing Operations Planning

## Slide 2: Background
The Other Binding Document (OBD), Procedure for Calculating Responsive Reserve (RRS) Limits for Individual Resources, describes the methodology used to calculate a MW limit on the amount of Responsive Reserve Service (RRS) from Primary Frequency Response (PFR) that an individual Resource (i.e. Generation Resource, Energy Storage Resources or Controllable Load Resource) can provide. Per Section 4 of this document, currently,
  Thermal Generation Resources are able to provide upto 20% of their High Sustained Limit (HSL) as RRS-PFR.
  Non-thermal Resources (i.e. Energy Storage Resources or Controllable Load Resource) or Generation Resources with a Resource Category of either (i) aeroderivative simple cycle commissioned after 1996, or (ii) Reciprocating Engines may provide upto 100% of their HSL or Maximum Power Limit (MPC) based on verified capability.
  Generation Resources operating in synchronous condenser fast-response mode may provide RRS-PFR up to the Generation Resource’s ERCOT-validated 20-second response capability (which may be 100% of their HSL)
  These RRS limits are subject to change based on performance during actual FMEs as specified in Section 5 of the same OBD.

## Slide 3: Background (Continued)
In 2020, the PDCWG had several discussions on the topic of whether a different limit is needed for provision of RRS-PFR by non-thermal Resources.
  These non-thermal Resources by virtue of their characteristics are able to provide upto 100% of their capacity as RRS-PFR. There was a concern that absent a per Resource MW limit for provision of RRS-PFR by these non-thermal Resources, as the size of these Resources grow, there could be negative outcomes of various types resulting from too much RRS-PFR from a single resource/site.
During those discussions, it was recommended that a per Resource RRS-PFR limit, if necessary, should be evaluated more broadly to identify any reliability-related limitations that need to be imposed on Resources providing RRS-PFR
  The evaluation should look at the problem from a broad, technology-neutral perspective to identify the reliability reason(s) to impose such a limit;
  take into account the technology trends and the changes planned for the ERCOT grid in the foreseen future;
  leverage model, data, or operational experiences from other systems
A RFP was issued in January 2021, and since December 2021, GE Energy Consulting has been working with ERCOT to conduct studies on this topic.
  GE and ERCOT had presented the proposed approach at Feb 2022 PDCWG. Responses to the stakeholder comments/feedback from that conversation were posted on April 2022 PDCWG meeting page.

## Slide 4: Agenda for Today
GE staff will share their study results and recommendations.
Following is the list of the primary GE staff that worked on this effort and are present at today’s meeting.
  Jason Macdowell, Senior Technical Director, GE Energy Consulting (Project Manager & Principal Advisor)
  Nick Miller, Principal of HickoryLedge, LLC and retired Senior Director, GE Energy Consulting (Lead technical advisor and analysis expert)
  Dr. Sheila Tandon Manz, Technical Director (Technical advisor)
  Dr. Shruti Rao, Senior Engineer (Simulation and analysis expert)
ERCOT staff will share the complementary studies that ERCOT has conducted using GE’s recommended methodology on the issue of common mode failure.
Round Table discussion
Next Steps