## Slide 1: CSAPR Update to WMS
April 2023

## Slide 2: CSAPR / Ozone Transport – Status Update
On March 15, 2023, EPA signed the final Federal Implementation Plan (FIP) that would establish an allowance-based ozone season trading program with nitrogen oxides (NOx) emissions budgets for fossil fuel-fired power plants in 22 states, including Texas as a Group 3 state, in addition to source-specific emission limits for certain industrial units
  The rule has not yet been published in the Federal Register
    The rule will be effective 60 days after publication
  The final trading program FIP moves units to CSAPR Group 3 and restricts allowance allocations along with additional enhancements
  The state budgets are calculated based on EPA’s identified EGU control stringency of optimization of all existing post-combustion controls (SCRs and SNCRs) by the 2023 ozone season, the installation of state-of-the-art NOx combustion controls by the 2024 ozone season, and the addition of new post-combustion controls by 2026 and 2027
  Overall, EPA relaxed the short-term requirements versus the rule proposal.
The precursor for EPA’s trading program FIP was the disapproval of numerous state implementation plans (including Texas, Illinois, and Ohio) that EPA finalized on February 13, 2023
  On March 3, 2023, Texas AG, TCEQ, PUC, AECT, TCC, TX Oil and Gas, Business Coalition for Clean Air and others filed a motion to stay the disapproval

## Slide 3: Key Changes to CSAPR – Compliance
Potentially higher variability limit than proposed
  EPA will determine each state’s variability limit for a given control period so that the percentage value used will be the higher of 21 percent or the percentage (if any) by which the total reported heat input of the state’s affected EGUs in the control period exceeds the total historical heat input of the state’s affected EGUs
  Will be implemented starting with the 2023 control period instead of the 2025 control period
Backstop daily limit
  Applies in 2024 only to coal-fueled units with existing SCRs
  Applies to units with new SCRs in second control period after installation, no later than 2030
  3-for-1 allowance surrender applies after 50-ton threshold
Assurance level backstop beginning in 2024
  If state exceeds assurance level of 121% of budget, secondary backstop limit applies to any unit with post-combustion controls responsible for contributing to an exceedance of the state’s assurance level
    3-for-1 allowance surrender applies after 50-ton threshold
    Unit must have operated at least 10% of the hours of the control period
  Secondary emission limit is higher of of 0.10 lb/mmBtu or 125% of the unit’s lowest previous seasonal average emissions rate would
  Potential administrative or judicial action and subject to penalties and other forms of relief under the CAA’s enforcement authorities

## Slide 4: Key Changes to CSAPR – Budgets
Budgets are higher than proposed
Beginning in 2026, significant reductions expected
Proposed generation shifting is no longer included in the budget determination but will be reflected in dynamic budgets
New preset budgets are provided through 2029 based on
  Inventory adjustments for announced retirements, addition of new units
  Ozone Season 2021 heat rate as baseline with EPA-determined controlled emission rate
New preset budgets establish the floor and may be replaced by the contemporaneously calculated dynamic budgets where the dynamic budget is higher
  For ozone seasons 2026 – 2029 only
  Dynamic budgets will be calculated and provided March 1 one year before and finalized by May 1 of prior year
After 2030, new dynamic budgets establish allocations with no preset
New bank recalibration target set at 21% until 2030 when it tightens to 10.5%

## Slide 5: Response to Reliability Concerns
EPA did not believe it necessary to add at reliability safety valve based on disagreement that the rule could cause resource adequacy or reliability issues
In response to consultations with the RTOs, EPA made several changes to address the timing of new features of the rule
  Applicability of the daily backstop NOx emission rate for units that do not have SCR controls delayed until 2030 or upon installation of controls
    Units with SCR subject to backstop in 2024
    3 to 1 retirement of allowances triggered after first 50 tons
  Recalibration of the bank to 10.5% is delayed until 2030, with a banking limitation of 21% set at beginning in 2024
  Establishing a preset budget for years 2025 – 2029 that sets the floor for future budgets
    Dynamic Budgeting will be calculated annually and the larger of the preset or dynamic will apply