## Slide 1
Dec 23, 2023 Analysis of Response During Winter Storm Elliott
Carl L Raish
Principal Load Profiling and Modeling
Wholesale Market Subcommittee – May 3, 2023

## Slide 2: ESIIDs with Dec 23 Load Reductions
High Price Event: Dec 23, Intervals 21 – 35, Load Reduction 3,700 MW.
Down Ramp:
  Started Dec 21 at interval 66, load reduction increased to 300 MW by interval 96.
  Dec 22, Interval 96 reduction 2,000 MW.
Dec 24: Average reduction 3,300 MW.
Dec 25: Average reduction 3,000 MW.
Largest competitive load reduction during summer 2022 occurred on July 13 and totaled 2,400 MW.

## Slide 3: Methodology
Analysis targeted competitive Non-weather sensitive ESIIDs:
  4CP billing ESIIDs, and/or
  ESIIDs reported on Indexed pricing for 2022 Demand Response Survey and still with reporting REP on Dec 31, 2022.
Baselines developed at ESIID-level – average load on weekdays Dec 15 – 21.
ESIIDs identified as responding based on significant load reduction during Dec 23 high-price event.
Weather sensitive ESIIDs and NOIEs also were examined.
  Typically would use Regression baselines, but Dec 23 was a Friday, holiday - regression models yielded unreliable estimates
  Examined actual loads over Dec 15 – 31 … no apparent, significant load reductions found.

## Slide 4: ESIIDs with Dec 23, 2022 Load Reductions
Quantified 2021 Christmas Holiday related load reductions for ESIIDs identified as responding to Dec 23, 2022 high price event
  Note: applied same baseline methodology to the 2021 data
  Dec 24 load was about 100 MW lower than baseline
  Dec 25 load was about 200 MW lower than the baseline

## Slide 5: ESIIDs with Dec 23, 2022 Load Reductions
Quantified 2020 Christmas Holiday related load reductions for ESIIDs identified as responding to Dec 23, 2022 high price event
  Note: applied same baseline methodology to the 2020 data
  Dec 24 load was about 250 MW lower than baseline
  Dec 25 load was about 525 MW lower than the baseline

## Slide 6: Seasonal Load Reduction Adjustment
Looking at prior year seasonal load reductions,
  Reduction for Friday, December 24, 2021: 100 MW
  Reduction for Thursday, December 24, 2020: 250 MW
  A plausible assumption for Friday, Dec 23, 2022: 250 MW
  Response for Dec 23 High-price event:
  Total response 3,700 MW
  Season response -250 MW
  High price response 3,450 MW

## Slide 7: Questions?
ON
OFF
craish@ercot.com 512/248-3876