## Slide 1: NPRR1177 – Fuel Supply Contracts, MOC Impacts, and EFC Process
WMWG May 5th, 2023

## Slide 2: Fuel Supply Contract
Contractual gas costs for some fuel supply agreements are based on volumes and variable rates set by the intrastate pipeline
These incremental costs are also subject to hourly, daily & cumulative imbalance charges. Resources have to pay the pipeline:
  To leave gas on the pipeline they purchase & deliver but do not burn
  To draw gas from the pipeline for burns in excess of the gas purchased & delivered
Resources price their Energy Offer Curves (EOC) based on the purchased & delivered gas, incremental heat rates, and these contractual costs for variances and incremental fuel balancing.

## Slide 3: Mitigation Details
Mitigation occurs when the Resource’s EOC is bypassed and the Resource is dispatched along an ERCOT estimated, incremental cost curve
The Mitigated Offer Curve (MOC) estimates the resource cost by taking an estimated market gas price (FIP) + Fixed Price FIP adder * capacity factor multiplier
When Resources are mitigated and dispatched along the MOC with an inaccurate cost, it results in significant uneconomic dispatch and unrecoverable losses
  Between Jun-Oct 2022, Constellation Resources were mitigated and suffered unrecoverable losses

## Slide 4: MOC v Contractual Cost Illustrative Example
The MOC uneconomically dispatches the contractual cost of the Resource ~$100/MWh

## Slide 5: MOC v Cost Economics
Assuming $50/MWH RT Price, the MOC would cause the Resource to uneconomic

## Slide 6: Current Exceptional Fuel Cost (EFC) Process
Resource Submits EFC with signed attestations
By day 15, Resource provides ERCOT with actual Weighted Average Fuel Price (WAFP)
By Day 60, Resource provides ERCOT with supporting information
Today a Resource can use the EFC process to include fuels costs in the Mitigated Offer Cap calculation
The issue with the current EFC process is that some Resources do not pre purchase fuel and their costs are determined based on contractual fuel supply contracts which include variable transportation costs

## Slide 7: Proposed Changes
Resource Submits EFC with signed attestations
By Day 15, Resource provides ERCOT with actual WAFP or Energy Offer Curve consistent with the fuel supply contract if the unit was flagged or subject to mitigation
By Day 60, Resource provides ERCOT with supporting documentation if the unit was flagged or subject to mitigation
Ten Business Days prior to submitting an EFC, a Resource must provide ERCOT with its fuel supply contract
ERCOT/IMM can request additional information at any time during the process
These changes will allow real-time Energy Offer Curves to reflect their short-run marginal costs