## Slide 1
Review of Potential DAM Price Correction for Certain Days in February-March ‘23 – Inclusion of ESR CLRs in Load Zone Pricing
Matthew Young
Supervisor, Market Validation
May 23, 2023

## Slide 2: Background
On March 9, 2023, ERCOT discovered an error in the ERCOT Market Management System (MMS) that impacted Load Zone calculations for both the RTM and the DAM. Market Notice M-C030923-01 was issued on March 9, 2023 at 4:14 PM, notifying the market of the issue and ERCOT’s intent, upon completion, to seek ERCOT Board of Directors (Board) approval for price correction for Operating Days (ODs) that meet criteria, as specified by ERCOT Protocols Sections 6.3(7)(b) and 4.5.3(6)(b).
ERCOT Protocols Sections 6.6.1.2 and 6.6.1.4 require that, for the RTM, the calculation of Load Zone prices exclude the Controllable Load Resources (CLRs) associated with Energy Storage Resources (ESRs). Contrary to ERCOT Protocols Sections 6.6.1.2 and 6.6.1.4, an error identified by ERCOT resulted in the ERCOT MMS including those CLRs in the calculation of Real-Time Load Zone prices.
Due to the same error, the DAM was also impacted where CLRs associated with ESRs were incorrectly mapped to a Load Zone. As a result of this, the Load Distribution Factors for those CLRs were included in the calculation of Day-Ahead Shift factors for certain Load Zones.
The constraint represents a stability limit for transient voltage instability associated with large power exports out of the Greater Valley.

## Slide 3: Load Zone LMP Calculation Example
The Load Zone LMP is calculated as the load weighted average of all Electrical Bus LMPs in the Load Zone.
North Load Zone LMP (LZ_NORTH)
Bus 2
LMP: $20
Load: 15 MW
Bus 3
LMP: $15
Load: 10 MW
Total Load = 30 MW
Bus 1
LMP: $10
Load: 5 MW

## Slide 4: Load Zone LMP Calculation Example
Electrical Bus 3 is now mapped to a Controllable Load Resource associated with an Energy Storage Resource.
North Load Zone LMP (LZ_NORTH)
Bus 2
LMP: $20
Load: 15 MW
Bus 3
LMP: $15
Load: 10 MW
Total Load = 20 MW
Bus 1
LMP: $10
Load: 5 MW

## Slide 5: Background
ERCOT determined that the error was related to the method in which MMS determines if an Electrical Bus is associated with an ESR Load Resource. The MMS relies on a set of tables from the Network Model Management System (NMMS) to determine if an Electrical Bus is associated with an ESR Load Resource. Those associated Electrical Buses are then excluded from Load Zone Price calculations. However, this table dependency and a recent change to one of those NMMS tables resulted in the MMS incorrectly including those Electrical Buses in the Load Zone calculations
ERCOT staff implemented a fix to the MMS on March 8, 2023, that resolved this issue. This took effect for the RTM for Operating Day (OD) March 8, 2023, and for the DAM for OD March 9, 2023.
Potential impact to the RTM was limited to February 8, 2023 through March 7, 2023.
Potential impact to the DAM was limited to February 9, 2023 through March 8, 2023.
Upon completion of the investigation, an update notice, M-C030923-02, was sent on April 25, 2023 @ 3:56 PM.
ERCOT has since implemented additional MMS model validation steps to ensure this doesn’t happen in the future.

## Slide 6: RTM Impact Analysis
ERCOT has concluded that there were zero ODs that met criteria for seeking ERCOT Board of Directors (Board) approval for price correction.
ERCOT Protocols Section 6.3(7)(b) requires that the absolute value impact to any single Counter-Party (CP) meet one of the following two criteria before seeking approval from the Board.
  2% and also greater than $20,000; or
  20% and also greater than $2000.
The absolute value impacts across all ODs for the RTM to any single CP with a dollar impact greater than $2,000 are shown in the table below.
Dollar Impact | Percent Impact
$4,670.87 | 0.160%
$3,846.93 | 0.330%
$3,778.90 | 0.101%
$2,573.72 | 1.432%

## Slide 7: DAM Impact Analysis
ERCOT has determined that there were 16 ODs for the DAM that meet the criteria for seeking Board approval for price correction, as specified in Protocol Section 4.5.3(6)(b). The number of Counter-Parties meeting one of the two criteria for significance are shown in the table below for each OD that met the criteria for seeking Board approval for price correction for the DAM:
Operating Day | Counter-Parties meeting criteria in Protocol Section 4.5.3(6)(b)(i) | Counter-Parties meeting criteria in Protocol Section 4.5.3(6)(b)(ii)
2/10/2023 | 3 | 2
2/11/2023 | 2 | 2
2/13/2023 | 4 | 0
2/15/2023 | 1 | 2
2/16/2023 | 5 | 6
2/18/2023 | 2 | 5
2/19/2023 | 0 | 1
2/20/2023 | 2 | 7
2/22/2023 | 3 | 4
2/27/2023 | 0 | 1
2/28/2023 | 1 | 5
3/1/2023 | 0 | 2
3/2/2023 | 5 | 3
3/3/2023 | 1 | 2
3/5/2023 | 0 | 1
3/8/2023 | 0 | 1

## Slide 8: DAM Impact Analysis
For each OD that met the criteria for DAM, the table below has the maximum estimated absolute value impact to Counter-Parties:
Operating Day | Maximum Amount ($Thousands) | Maximum Percentage for Criteria (i)* | Maximum Percentage for Criteria (ii)**
2/10/2023 | $65.13 | 8.13% | 108.79%
2/11/2023 | $36.36 | 10.29% | 99.11%
2/13/2023 | $36.84 | 11.06% | 12.12%
2/15/2023 | $32.19 | 2.07% | 61.37%
2/16/2023 | $117.32 | 21.27% | 56.16%
2/18/2023 | $55.08 | 5.25% | 162.41%
2/19/2023 | $11.26 | NA | 29.79%
2/20/2023 | $75.20 | 647.52% | 647.52%
2/22/2023 | $44.70 | 4.51% | 677.15%
2/27/2023 | $9.15 | NA | 43.15%
2/28/2023 | $39.71 | 2.31% | 159.80%
3/1/2023 | $15.63 | NA | 62.96%
3/2/2023 | $44.36 | 16.68% | 341.84%
3/3/2023 | $21.36 | 3.35% | 51.67%
3/5/2023 | $23.90 | 1.83% | 32.84%
3/8/2023 | $11.25 | NA | 22.97%
* The maximum of percentage change to any single Counter-Party with impact more than $20,000 (set as NA when no single Counter-Party has impact more than $20,000)
** The maximum of percentage change to any single Counter-Party with impact more than $2,000 (set as NA when no single Counter-Party has impact more than $2,000)

## Slide 9: DAM Impact Analysis
For each OD that met the criteria for DAM, the table below has the maximum estimated change in charges due to ERCOT. Negative amounts are increased payments to Market Participants; positive amounts are increased charges. The percent amount is the absolute value of the percent impact to the previously settlement net amount due to/from ERCOT.
Operating Day | Change in Statement Charges Due to ERCOT ($ thousands) | 
2/10/2023 | $(152.36) | 1.40%
2/11/2023 | $(7.58) | 0.10%
2/13/2023 | $121.90 | 1.73%
2/15/2023 | $(84.39) | 1.06%
2/16/2023 | $(133.77) | 1.35%
2/18/2023 | $(305.89) | 3.67%
2/19/2023 | $49.50 | 0.75%
2/20/2023 | $31.63 | 0.43%
2/22/2023 | $(193.66) | 1.65%
2/27/2023 | $(24.31) | 0.30%
2/28/2023 | $(8.52) | 0.08%
3/1/2023 | $24.34 | 0.20%
3/2/2023 | $299.44 | 2.78%
3/3/2023 | $32.34 | 0.37%
3/5/2023 | $108.96 | 1.16%
3/8/2023 | $70.74 | 0.43%

## Slide 10: Next Steps
ERCOT intends to seek an approval of correction to DAM prices for the impacted ODs that met the necessary criteria at the Reliability and Market Committee on June 19, 2023, and the Board meeting on June 20, 2023.