## Slide 1
IDR to AMS Project
Retail Market Subcommittee (RMS) Update
Kathy Scott
Tuesday, June 6, 2023

## Slide 2: June 8, 2021 ERCOT Board and PUCT Approved LPGRR068:
With the Approval of Load Profile Guide Revision Request (LPGRR) 068:
  Would improve the accuracy of Initial Settlements that occurs on Day 5 (Operating Day(OD)+ 4) by ERCOT by processing 15-minute interval usage data received daily from the TDSPs for an AMS Metered Premise with a Peak Demand >/= 700kW/700kVA, in addition;
  Created 16 Load Profile as unique identifiers that affirms to ERCOT and REPs of the Record that Customer’s ESI ID Peak Demand is eligible for 4CP Billing.
    CenterPoint Energy’s (2) New Load Profiles are:
      BUSLRG_COAST_IDR_WS_NOTOU
      BUSLRGDG_COAST_IDR_WS_NOTOU

## Slide 3: IDR to AMS Load Profiles Project Update:
Questions during previous IDR vs. AMS Workshops | CenterPoint Energy’s Responses (Effective 04/04/2023)
Total Number of BUSIDRRQ Load Profiled ESI IDs? | 4,846
Total Number of ESI IDs eligible to transition to BUSLRG? | 2,277 (47.0% Approximately)
Total Number of ESI IDs eligible to transition to BUSLRGDG? | 0
Total Number of ESI IDs remaining on BUSIDRRQ Profile? | 2,569 (53.0% Approximately)

## Slide 4: Why some BUSIDRRQ Profiles will not Change?
Questions during previous IDR vs. AMS Workshops | CenterPoint Energy’s Responses
Under what scenarios for ESI IDs with an IDR Meter and Load Profile of BUSIDRRQ will NOT transition to BUSLRG or BUSLRGDG? Therefore, the 15-minute interval data REPs of Record currently receive today for these ESI IDs will continue to be available only on the Monthly 867_03IDR Details Usage transaction. 2,569 (approx.) will remain BUSIDRRQ | Coincident Peak Customers on Private Use communications’ network or telephone lines ERCOT Polled Settlement (EPS) ERCOT is Meter Reading Entity (MRE) where these IDR meters are read daily by ERCOT, and that 15-minute interval data is already processed daily by ERCOT for their settlements. Multiple Metered Premises Subtractive Meters Transmission Voltage

## Slide 5: BUSIDRRQ Transition to BUSLRG or BUSLRGDG Load Profile:
Questions from previous IDR vs. AMS Workshops | CenterPoint Energy’s Responses
What will be provided to the Market for ESI IDs where Customer’s Load: >/= 700 kVA 4CP Threshold previously met Load Profile currently BUSIDRRQ 2,277 (approx.) will transition to BUSLRG NOTE: There are no BUSLRGDG currently identified in CNP’s BUSIDRRQ population. | Current population already has AMS Meters installed that capture kVAR channels, therefore, NO Meter exchange will be necessary. Load Profile: BUSLRG NOTE: Load Profile changes must be completed on ESI ID Cycle Read Date Daily 15-Minute Interval Data is sent to: ERCOT for Settlements Smart Meter Texas (SMT) for REP of Record & Customer 867_03 Monthly will contain 867_03IDR details (Historical 867_03 IDR data will be available)

## Slide 6: AMS Metered Premise Process for Customer Load < 700kVA:
Slide 8 here....
Questions during previous IDR vs AMS Workshops | CenterPoint Energy’s Responses
What will be provided to the Market for ESI IDs where Customer’s Load is < 700 kVA? | Meter Type: AMS Load Profile: BUSHI NOTE: Load Profile changes must be completed on ESI ID Cycle Read Date. Daily 15-Minute Interval data is sent to: ERCOT for Settlements Smart Meter Texas (SMT) for REP of Record and Customer 867_03 Monthly Usage transaction contains Summary Level Data Only

## Slide 7: AMS Metered Premise Process for Customer Load >/= 700kVA:
Questions from previous IDR vs. AMS Workshops | CenterPoint Energy’s Responses
What will be provided to the Market for ESI IDs where Customer’s Load: >/= 700 kVA 4CP Threshold recently met Load Profile is BUSHI or BUSXXX | AMS Meter exchange required that captures kVAR channels Load Profile: BUSLRG or BUSLRGDG NOTE: All Load Profile changes must be completed on ESI ID Cycle Read Date. Daily 15-Minute Interval Data is sent to: ERCOT for Settlements Smart Meter Texas (SMT) for REP of Record & Customer Following this Meter Exchange Monthly 867_03IDR Details will be recorded on a going forward basis.

## Slide 8: Load Profile after Move-Out (MVO) or Move-In (MVI) Completes:
Slide 11
Questions from previous IDR vs. AMS Workshops | CenterPoint Energy’s Responses
What will be provided to the Market for ESI IDs where: 4CP Threshold previously met Load Profile is BUSLRG or BUSLRGDG Moved Out or new Move-In completed | AMS Meter capturing kVAR Channels previously installed, NO Meter Exchange will be necessary. Load Profile: BUSHI NOTE: Load Profile changes must be completed on ESI ID Cycle Read Date. Daily 15-Minute Interval Data is sent to: ERCOT for Settlements Smart Meter Texas (SMT) for REP of Record & Customer 867_03 Monthly will contain 867_03IDR details (Historical 867_03 IDR data will be available)

## Slide 9: Current and Future Usage Data Availability
BUSIDRRQ, BUSLRG and BUSLRGDG Load Profiles:
  Monthly 867_03 with 15-minute interval data (IDR details) will include kVAR interval data will apply to all three Load Profiles.
  Historical Usage will continue to be taken from the Monthly 867_03IDR Details and available for all three Load Profiles via the Competitive Retailer Information Portal (CRIP).
    NOTE: If Meter needed to be exchanged to capture kVAR channels, NO historical usage data will be available prior to the meter exchange date.
  3rd Parties (Aggregators, Brokers, Non-ROR) 15-minute Interval Data Historical Usage accessibility for all three Load Profiles will continue to be available with a completed LOA that is communicated via email to: Usage.Req@centerpointenergy.com
BUSLRG and BUSLRGDG Load Profiles:
  LSE files containing daily 15-minute Interval data will be communicated to ERCOT and Smart Meter Texas (SMT) for both Load Profiles.

## Slide 10: BUSLRG and BUSLRGDG Load Profiles Transition Plan and Production Go-Live
IDR to AMS Project Go-Live: Monday, July 17, 2023
Transition Plan:
  Email Market Notice(s) to RMS Listserv providing IDR to AMS Project Go-Live information.
  Email REP of Records - IDR to AMS Load Profile Report (spreadsheet) that includes (7/10/23 – 7/14/23):
    List of REPs impacted ESI ID(s),
    Load Profile Assignment: “BUSLRG” or “BUSLRGDG” or “BUSIDRRQ” and;
    Load Profile Cycle Read Change Effective Date
  Since all Load Profile changes must be effective with Cycle Read Date. If Cycle Read Date has recently occurred prior to July 17, 2023, then we will determine if we should use the prior Cycle Read Date as our effective date for the new “BUSLRG” or “BUSLRGDG” Load Profile change(s).
    Benefit: We feel this will assist the Wholesale and Retail market by providing ERCOT with daily LSE files containing the 15-minute Interval data earlier instead of waiting until next month’s Cycle Read Date.
  After we receive ERCOT’s acknowledgement that “BUSLRG” or “BUSLRGDG” Load Profile change has loaded successfully in ERCOT’s systems. CNP will start sending LSE files to ERCOT and SMT to backfill ESI ID(s) missing 15-minute interval daily data starting with the effective date of the Load Profile change.

## Slide 11: Transition and LSE Backfill Process Following July 17, 2023 Go-Live
Go-Live July 17
July 16
July 14
July 15
July 13
Cycle 33 Read Date July 10
July 12
July 11
814_20 “BUSLRG” Load Profile
Effective Date 07/10/2023
LSE
LSE
LSE
LSE
LSE
LSE
LSE

## Slide 12: Questions?