## Slide 1
NPRR1178
Expectations for Resources Providing ERCOT Contingency Reserve Service
Jonas Kersulis
ERCOT Market Analysis
Wholesale Market Working Group
June 2, 2023
Notes: In recent PRS discussions, there have been questions about NPRR1178 and expectations for Resources providing ECRS. This presentation summarizes NPRR1178 with the goal of addressing those questions.

## Slide 2: NPRR1178 Overview
Clarify expected Resource Status for Load Resources other than CLRs providing ECRS and RRS simultaneously.
Clarify that $75/MWh Offer floor on capacity applies when providing ECRS concurrently with On-Line Non-Spin (not just Reg-Up and/or RRS).
Update ECRS deployment obligation requirements for Load Resources other than CLRs.
3.9.1, Current Operating Plan (COP) Criteria
6.4.4.1, Energy Offer Curve for On-Line Non-Spinning Reserve Capacity
6.5.7.6.2.4, Deployment and Recall of ECRS
8.1.1.4.4, ECRS Energy Deployment Criteria

## Slide 3: 1. Expected Resource Status Changes
3.9.1, Current Operating Plan (COP) Criteria
(5) A COP must include the following for each Resource represented by the QSE:
(b) The expected Resource Status:
(iii) Select one of the following for Load Resources. Unless otherwise provided below, these Resource Statuses are to be used for COP and/or Real-Time telemetry purposes.
(E) ONRL – Available for Dispatch of RRS or Non-Spin, excluding Controllable Load Resources. A Load Resource, excluding Controllable Load Resources, may not provide ECRS with this Resource Status;
(F) ONECL – Available for Dispatch of ECRS, or available for Dispatch of ECRS and RRS simultaneously, excluding Controllable Load Resources;
A Load Resource other than a CLR:
May not provide ECRS in ONRL.
Should use ONECL to indicate availability for simultaneous Dispatch of ECRS and RRS.
Notes: Note that these LRs cannot simultaneously provide ECRS and Non-Spin.

## Slide 4: 2. Offer Floor on Capacity
NPRR892 addressed Non-Spin with Reg-Up and/or RRS, but ECRS was not included at the time.
With NPRR1178, the $75/MWh Offer floor applies to Resources with RRS, ECRS, and/or Reg-Up in addition to Non-Spin.
6.4.4.1, Energy Offer Curve for On-Line Non-Spinning Reserve Capacity
(1) The following applies to Generation Resources that a QSE assigns Non-Spinning Reserve (Non-Spin) Ancillary Service Resource Responsibility in its COP to meet the QSE’s Ancillary Service Supply Responsibility for Non-Spin and applies to On-Line Non-Spin assignments arising as the result of Day-Ahead Market (DAM) or Supplemental Ancillary Services Market (SASM) Ancillary Service awards, or Self-Arranged Ancillary Service Quantity.
(b) If the QSE also assigns Responsive Reserve (RRS), ERCOT Contingency Reserve Service (ECRS), and/or Regulation Up Service (Reg-Up) to a Generation Resource that has been assigned Non-Spin, the QSE shall ensure that a valid Output Schedule or Energy Offer Curve for the Operating Hour has been submitted and accepted by ERCOT. The Energy Offer Curves submitted by the QSE for the capacity assigned to the sum of the RRS, ECRS, Reg-Up, and Non-Spin Ancillary Service Resource Responsibilities, as well as any Non-Frequency Responsive Capacity (NFRC) that is above the Resource’s High Ancillary Service Limit (HASL) and will not be utilized prior to deployment of a Resource’s On-Line Non-Spin, may not be offered at less than $75 per MWh.

## Slide 5: 2. Offer Example
100 MW GR
10 MW On-Line Non-Spin
15 MW ECRS, not deployed
HASL = 85 MW
Chart: MW
| 0 | 40 | 40 | 60 | 60 | 75 | 75 | 90 | 90 | 100 | 85 | 85
Floor only applies to Non-Spin | 40 | 40 | 45 | 45 | 50 | 50 | 50 | 50 | 75 | 75
Floor also applies to ECRS | 40 | 40 | 45 | 45 | 50 | 50 | 75 | 75 | 75 | 75
HASL | 0 | 90
On-Line Non-Spin should not be dispatched until prices reach the $75/MWh floor.
If the floor applies only to Non-Spin, this Resource may be dispatched up to HASL at $50/MWh; it no longer has a 10 MW standing deployment at the floor.
After NPRR1178, the ECRS capacity is also subject to the floor when a Resource carries ECRS (and/or Reg-Up and RRS) in addition to On-Line Non-Spin.
  This aligns ECRS with how Reg-Up and RRS work after NPRR892.
Notes: Without the ECRS award, the last 10 MW before reaching HASL would be subject to the floor.
In this scenario:
If ECRS is not deployed, the Resource no longer has a 10 MW Non-Spin standing deployment at the $75/MWh floor—the ECRS responsibility pushes HASL below it. In other words, the Resource can be dispatched all the way to HASL without encountering the floor, even though it is supposed to be carrying 10 MW of economically-deployed On-Line Non-Spin.
If ECRS is deployed, it will “jump ahead” of the Non-Spin and be used first.

## Slide 6: 3. ECRS Deployment Obligation Requirements
ECRS deployments remain in effect until recalled by ERCOT.
  Aligns language with RTC Protocols.
6.5.7.6.2.4, Deployment and Recall of ERCOT Contingency Reserve Service
(6) Following an ECRS deployment to SCED-dispatchable Resources, the QSE’s obligation to deliver ECRS remains in effect until ERCOT issues a recall instruction or its ECRS obligation expires, whichever occurs first. Following an ECRS deployment to Load Resources, excluding Controllable Load Resources, or Resources operating in synchronous condenser fast-response mode, the QSE’s obligation to deliver ECRS remains in effect until ERCOT issues a recall instruction.
8.1.1.4.4, ERCOT Contingency Reserve Service Energy Deployment Criteria
(1) …Control performance during periods in which ERCOT has deployed ECRS shall be based on the requirements below and failure to meet any one of these requirements shall be reported to the Reliability Monitor as non-compliance:
(b) …The QSE’s portfolio shall maintain this response until recalled or the Resource’s obligation to provide ECRS expires. The combination of the QSE’s ECRS responsibility and additional available capacity shall not exceed 150% of the sum of the QSE’s Ancillary Service Resource Responsibility for ECRS from non-Controllable Load Resources. Any additional available capacity from Load Resources other than Controllable Load Resources shall be deployed concurrently with ECRS.