## Slide 1
Issue LFL - 41 Settlement of Price Sensitive Flexible Loads
5/31/23

## Slide 2: What is the Concept of the Floyd Trefny Proposal?
“Improve” Real-Time settlement of Load that is responsive to prices but not registered as a Controllable Load Resource. This is Load that does not have a bid to buy in SCED and is not following Base Points but is capable to adjust consumption levels in response to prices
  Still settled using a price “based on” the Load Zone Price
  Still settled on a 15-minute interval basis. (Continue to use a 15-minute interval price and the 15-minute interval Metered Quantity)
  No change in the 15-minute metered quantity for each Load. No change to Load Ratio Share calculations.
  The 15-minute price for this load would have each SCED interval Load Zone Price weighted by the MWh consumption during the SCED interval as determined using the integrated telemetered MW consumption levels. (The calculated weighting factors that are applied to the SCED prices in the 15-minute interval to determine the 15-minute price.)
  This would have an impact on Real-Time Revenue Neutrality Allocation calculation.

## Slide 3: Additional Information
  All the prices shown in the tables of Floyd’s presentation are either a Load Zone price for a 5-minute SCED interval or a Load Zone price for a 15-minute interval? In other words, the proposal does NOT suggest to have a “Price Sensitive Flexible Load” settled using its nodal price at the bus. The proposal is for each “Price Sensitive Flexible Load” to have a unique price that is “based on” the Load Zone price.
  The proposal does NOT change the prices, or the mechanism used to settle (pay) the Resources that provide energy.
  With this proposal:
    the payments to Resources providing energy will not change,
    charges to “Price Sensitive Flexible Loads” that have “successfully” responded to SCED interval prices each SCED interval would be less (compared to what they are charged with today’s construct),
    other Loads will have to pay more (compared to what they are paying with today’s construct) and
    the sum of the “differences” realized by the “Price Sensitive Flexible Loads” …… is uplifted to all Loads based on Load Ratio Share

## Slide 4: The proposal from Floyd needs discussion at other subcommittees
  Impact to other Loads
  Telemetry questions
  What Load is eligible for this new pricing approach?
  What is the registration process?
  Is there a validation process? What is the criteria?
  How many ESIIDs are likely to want this new pricing approach?
  What is the priority to implement this change considering all the other ongoing approved NPRRs and changes?
  And more ….

## Slide 5: Appendix
Link to Floyd’s 4-12-23 Presentation
https://www.ercot.com/files/docs/2023/04/12/LFLTF-Settlement-of-Price-Responding-Loads-041223.pptx
Load Zone LMPs
Load Zone Price Calculation
Price Calculation for Settlement Meter for ESR-CLR

## Slide 6: Real-Time Energy Imbalance Payment or Charge at a Load Zone (6.6.32)
(2) The payment or charge to each QSE for Energy Imbalance Service at a Load Zone for a given 15-minute Settlement Interval is calculated as follows:
RTEIAMT q, p = (-1) * {[RTSPP p * [(SSSK q, p * ¼) + (DAEP q, p * ¼) + (RTQQEP q, p * ¼) – (SSSR q, p * ¼) – (DAES q, p * ¼) – (RTQQES q, p * ¼)]] + [RTSPPEW p * (RTMGSOGZ q, p – (RTAML q, p – RTAMLESRNW q, p))]}

## Slide 7: Load Zone LMPs (section 6.6.1.4)

## Slide 8: Real-Time Settlement Point Price for a Load Zone (section 6.6.1.2 paragraph 2)

## Slide 9: RT Settlement Point Price for a Load Zone (section 6.6.1.2)
The 15-minute Load Zone Prices are Load Weighted and SCED duration weighted.
The 15-minute Load Zone price is calculated using the State Estimated Load at each bus in the Load Zone (this is the load weighting) and uses the duration of each SCED interval (this it the SCED duration weighting.
The picture below is an example of the first 15-minute interval of the hour having four SCED intervals in the first 15-minute interval. Note that:
In the picture, the blue lines are when the SCED process sends out base points and SCED LMPs.
SCED interval 1 is 3 minutes long (180 seconds) [TLMP1]
SCED interval 2 is 4 minutes long (240 seconds) [TLMP2]
SCED interval 3 is 6 minutes long (360 seconds) [TLMP3]
SCED interval 4 is 2 minutes long (120 seconds) [TLMP4]
Total is 15 minutes (900 seconds). See how the SCED intervals that straddle the top of the hour, and the 12:15 mark are “handled”.

## Slide 10: Use 6.6.3.1 paragraph (3) at the template for the ESIID MW weighted price
Instead of Meter Price: …..15-minute price for the ESIID (signed up)
Instead of BP: … use the MW average telemetered consumption for the SCED interval
Instead of RTLMPb,y ….. use the LZLMPy for the mapped zone