## Slide 1
Outage Schedule Adjustment (OSA) Review for May ‘23
Mahnoush Yousefian
ERCOT Market Analysis
Wholesale Market Working Group
June 2, 2023

## Slide 2: Definitions and Acronyms:
Advance Action Notice (AAN)
Outage Adjustment Evaluation (OAE)
Outage Schedule Adjustment (OSA)

## Slide 3: Protocol 3.1.6.9
    Withdrawal of Approval and Rescheduling of Approved Planned Outages of Resource Facilities:
  “If ERCOT believes it cannot meet applicable reliability standards and has exercised all other reasonable options, and any actions taken pursuant to … Outage Coordination of Potential Transmission Emergency Conditions, have not resolved the situation, then ERCOT shall conduct a preliminary OAE and issue an AAN… .”

## Slide 4: ERCOT Issues an AAN
AAN shall describe:
The Reliability Problem
The date and time emergency condition begins and ends
A summary of the actions: the amount of capacity it would seek from OSA
The earliest time an OSA will be issued, if necessary
May 4, 2023 at 12:00, ERCOT issued an AAN due to a possible future Emergency Condition of reserve capacity deficiency beginning May 8, 2023 through May 10, 2023 HE 1600 - HE 2100 (Daily). ERCOT may Delay/Withdraw Approved or Accepted Resource Outages. ERCOT may seek 3,380 MW from an OAE and then make the OSA. On May 5, 2023 at 12:00 ERCOT will execute an OAE if deemed necessary. Please notify ERCOT by email aan@ercot.com if a specific resource cannot be considered in the OAE.

## Slide 5: QSE's Checklist Immediately Following an AAN
Update its Resource COPs and the Outage Scheduler to reflect any decisions to voluntarily delay or cancel any Outage
Notify ERCOT at AAN@ercot.com if a specific Resource cannot be considered for an OSA, due to Resource reliability, compliance with contractual warranty obligations, or other reasons beyond the Resource’s control
Notify ERCOT of any Resource that is currently on Outage and could be returned to service

## Slide 6: ERCOT May Issue One or Multiple OSA(s)
QSEs may be contacted for more information prior to issuing an OSA.
Nuclear Resources may not be considered for an OSA.
If a QSE has previously notified ERCOT that a resource cannot be considered for an OSA, the resource will not be considered.
ERCOT will divide the outages in categories of 0-2 days, 2-4 days, 4-7 days, or more than seven days duration, then withdraw approval on a last in, first out basis, so that shorter outages are delayed first
ERCOT website will update to state that it will issue one or more OSAs and shall provide verbal notice to TSPs and QSEs via the Hotline.

## Slide 7: OSA Event Timeline
5/5
5/6
5/7
5/8
5/10
5/11
OSA (4 units)
21:00 – OSA Ended
12:00 - ERCOT updated the AAN (1,130 MW), OAE completed and OSA executed.
OSA (1 unit)
5/4
12:00 - ERCOT issued the AAN 5/8 – 5/10 HE 16-21 Daily, 3,380 MW

## Slide 8: OSA Event Review
5 resources outages were withdrawn during 5/6 – 5/10
4 out of 5 were able to reschedule their outages on/after 5/10.
1 has not rescheduled their outage yet.
605MW of HSL was added by cancelling the outages.
One out of 5 received RUC instructions from 5/6 HE1 to 5/10 HE21.

## Slide 9: ERCOT Process and QSE's Obligations
Resource Status of On-Line or “OFF” in the COP
Update EOC to $4500/MWh for all MW (0-HSL)*
If On-Line: Start and End time of the On-Line period
  Status “ONRUC” (OR OFF) and cannot opt out of RUC Settlement
Resource to remain at LSL unless deployed by SCED
NO Three-Part Offer into DAM for any OD of the OSA
QSE
* ERCOT shall create proxy Energy Offer Curves for the resource upon implementation of NPRR930
One or Multiple RUC instructions
Issues One or Multiple OSA(s)
ERCOT

## Slide 10
Questions?