## Slide 1
Post Go-Live update to TAC for
ERCOT Contingency Reserve Service (ECRS)
Matt Mereness and other ERCOT staff
June 27, 2023

## Slide 2: Agenda
Readiness and Cutover
Observations of first 2 weeks
  DAM Prices
  Deployment Summaries

## Slide 3: Communication and Cutover
First, thank you TAC, QSEs, and vendors for the support and excellent coordination in preparations for ECRS implementation.
Market Readiness calls and scorecards were effective for ERCOT and MPs in identifying issues and risks to be mitigated before, during and after go-live
  June 8, 2023 (Thursday)
    System upgrade occurred June 8th starting between 3:30-4:00pm
      Completed closer to 5pm and Operations Message was posted to confirm completion
      Issue with qualification data transition affected PRC/ORDC calc and subsequent real-time price correction made
    MPs did not need to take any immediate action following the upgrade.
    After the upgrade ECRS system functionality was available for OD June 10, 2023
  June 9, 2023 (Friday)
    Starting at 12:01am Telemetry for On-Hold status was used (NPRR1085)
    Day-Ahead Market activities on June 9 for June 10 included ECRS
    After DAM, QSE submitted COP updates OD June 10 to include ECRS, and DRUC executed.
  June 10, 2023 (Saturday)
    First Operating Day with ECRS
    Starting at 12:01am, telemetry included ECRS values
ECRSCutover@ercot.com mailbox received a couple dozen emails, and responses were turned around within minutes or hours. No single theme of questions or issues (both technical and operational). Overall, there were no significant reliability or market issues.

## Slide 4: Day-Ahead Market ECRS June 10-19, 2023
ECRS daily procurement
2,073 average procured MW/hour
Trending of price comparison for ECRS to other Day-Ahead products below from June 10-19.

## Slide 5: Day-Ahead Market ECRS June 20-27, 2023

## Slide 6: ECRS Deployments
For the period of Jun 10-18, 2023, Quick Start Resources (~50%), Thermal Resources (~33%) and Energy Storage Resources (~12%) provided majority of the ECRS in Real Time. There were 3 events that resulted in deployment of SCED dispatchable ECRS.
Key Takeaway: ECRS performed well in all deployments and helped recover from the events that triggered deployment.
Date and Time Released to SCED | Date and Time Recalled | Duration of Event | Maximum MWs Released | Reason
6/14/2023 19:20 | 6/14/2023 19:33 | 12:28 | 600 | Insufficient capability for forecasted 10min Ahead Net Load
6/18/2023 19:20 | 6/18/2023 19:46 | 25:25 | 200 | 10min out Net Load Forecast
6/16/2023 18:31 | 6/16/2023 18:36 | 04:40 | 430 | Frequency below 59.91Hz

## Slide 7: Manual Deployments
6/14/2023 at 19:20
SCED Dispatchable MW Released: 600 MW
Deployment Duration: 12 minutes and 28 seconds
Min HDL – GEN: 1467.2
Max System Lambda: 136.9
Reason: Insufficient capability for forecasted 10min Ahead Net Load.
6/18/23 at 19:20
SCED Dispatchable MW Released: 200 MW
Duration: 25 minutes and 25 seconds
Min HDL – GEN: 1515.7
Max System Lambda: 873.8
Reason: Insufficient capability for forecasted 10min Ahead Net Load.
6/20/23 at 16:21 (fourth deployment on June 20th)
ERCOT deployed up to 1900 MW of ECRS in steps as dispatchable headroom reduced during the period of 16:21 and 21:01 (4 hours and 40 minutes)

## Slide 8: Automatic Deployment
6/16/2023 at 18:31
SCED Dispatchable MW Released: 430 MW
Duration: 4 minutes and 40 seconds
Reason: Frequency below 59.91Hz due to unit trip (~632 MW instantaneous, 1235 MW total)

## Slide 9: Wrap-Up and Question
ERCOT is prepared to help support future discussion and analysis of ECRS during the early weeks/months of this new AS product.
ERCOT looks to TAC as to how to best support those discussion.
Open to questions at today’s meeting.