## Slide 1
DRRS Discussion
Kenan Ögelman
Vice President Commercial Operations
Workshop
July 27, 2023

## Slide 2: HB1500 Dispatchable Reliability Reserve Service (DRRS) Requirements
Deliver December 1, 2024
Day Ahead and Real-Time procurement
  Note: true Real-Time procurement will only apply after Real-Time Co-optimization (RTC) implementation
Quantity based on historical variations in generation availability
Run at least 4 hours at High Sustained Limit (HSL)
Online within 2 hours of instruction
Dispatch flexibility to address inter-hour operational challenges
Reduce Reliability Unit Commitment (RUC) by the amount of DRRS procured
  Note: Since the ability to RUC is necessary to meet several NERC Reliability Standards, this requirement can only be achieved to the extent that RUCs are not needed to cover load and reserve obligations

## Slide 3: ERCOT DRRS as Sub-Type of NS
High Level Implementation
Keep the existing Non-Spin AS structure and method of deployment (e.g., on-line Non-Spin will still be automatically released to SCED). Partition the current Non-Spin by creating a new subtype that will become DRRS where a portion of Non-Spin (with a defined MW cap) can be provided by longer lead time Resources (e.g., Resources with a 2-hour lead time) that are off-line. DRRS will meet the requirement specified in HB1500.
With the new subtype, constraints would be added to market systems to limit the amount of Non-Spin that could be provided by the longer lead time Resources.
Qualification
DRRS, the new subtype, can be provided by generators that are off-line, that have a Cold Start Time greater than 30 minutes and less than or equal to 2 hours, and are able to sustain a deployment for at least 4 hours.
The component of the current ancillary service, that is a 30-minute service, will be retained with the current subtype still provided by on-line generators, off-line generators, ESRs, CLRs and non-Controllable Load Resources.

## Slide 4: ERCOT DRRS as Sub-Type of NS cont.
Procurement
ERCOT will perform a holistic review to determine the quantity of Non-Spin MWs to be provided by the DRRS subtype in addition to the 30-minute subtype.
There will not be any changes to the Ancillary Service offer structure to accommodate this new subtype. DRRS type will be identified based on the Cold Start Time of the resource and the fact that the resource has an off-line Non-Spin Offer. i.e., resources with off-line Non-Spin awards with Cold Start Times greater than 30 minutes and less than or equal 2 hours will be deemed to be providing the DRRS subtype.
DAM and SASM will be changed to recognize the new DRRS subtype.

## Slide 5: ERCOT DRRS as Sub-Type of NS cont.
DAM/SASM
DAM/SASM constraints will be re-designed to account for the DRRS max limit and the minimum limit on SCED Dispatchable NSPIN (1430 MW).
  a. Total Non-Spin requirements includes DRRS requirement
  b. Online GR/CLR Non-Spin (30 min) awards + Offline GR Non-Spin (30 Minutes) + NCLR (30 minute) Non-spin Awards + DRRS awards >= Total Non-Spin Requirement (which includes DRRS requirement)
  c. NCLR (30 minute) Non-spin Awards + DRRS awards <= (TotalNon-SpinReq – 1430)
  d. DRRS awards <= DRRS Req.
Trades
Ancillary Service trades will all have to identify and account for this distinct subtype, equivalent to how “NSRSM” is managed with the implementation of NPRR1093. For example, “30-minute” Non-Spin can’t be replaced with “2-hour” Non-Spin (however “2-hour” can be replaced with “30-minute”)
Self-arrangement will be subjected to limits

## Slide 6: ERCOT DRRS as Sub-Type of NS cont.
RUC
RUC functionality will be changed to consider the dispatch of NS subtype DRRS resources (off-line, cold start-time greater than 30 minutes and less than 2 hours providing off-line non-spin) as a first option (i.e., more economical) before committing and then dispatching an “OFF” resource to meet load forecast, capacity needs and manage congestion.
  Any 30-minute Non-Spin acquired above 30-minute NS requirement will be used as DRRS.
  RUC can still recommend committing other “OFF” resources for congestion purposes or capacity needs if NS subtype DRRS Resources are not sufficient.
  The treatment of 30-minute Non-Spin requirement will remain as is (i.e., RUC will protect that capacity and not use it to solve for capacity or congestion needs).
ORDC
ORDC remains a one-hour product
Assume no changes to reserve calculation or AS Imbalance i.e. treat all NS types like NS treated today (online and offline)

## Slide 7: Discussion
Market Participant discussion and ideas
Next steps
  Discussions with PUC and Stakeholders – July to August 2023
  Protocol Development and Impact Analysis – August 2023
  Stakeholder Protocol Process – September to November 2023
  Board Recommendation – December 2023
  PUC Approval – January 2023