## Slide 1
Preliminary Generation Expansion and Retirement Results for 2024-LTSA Current Trends
ERCOT, Resource Adequacy
Fred Khodabakhsh
Sep 19, 2023

## Slide 2: Assumptions for Current Trends
Energy Exemplar (vendor for the capacity expansion model) implemented the ORDC modifications for the bridging solution to Phase 2 of Market Redesign.
The amount of Large Flexible Loads (LFLs) are assumed to start with 5.84 GW at 2025 and increase to 7.36 GW by 2028 and stay constant for the rest of the study period.
LFL curtailment is modeled as price-responsive demand
  60% of LFLs at $100/MWh, this is an energy only curtailment for the standard mining equipment
  30% of LFLs at $200/MWh, this is also an energy only curtailment targeted toward LFLs with more efficient/newer crypto mining equipment that can curtail at higher price
  10% of LFLs at $1,000/MWh, this is for miners that are less price responsive to real time price swings
None of the EPA proposed environmental regulations are modeled in Current Trends. Some of these environmental regulations will be considered in the other 2024 LTSA scenarios.

## Slide 3: New Unit Capital Costs for 2024 LTSA, Overnight Costs, Nominal $/KW
Sources of capital cost assumptions:
  Lazard’s Levelized Cost of Energy Analysis (V16), April 2023
  NREL Cost Projections for Utility-Scale Battery Storage 2022
  EIA AEO 2022
Sources:
https://www.lazard.com/research-insights/levelized-cost-of-energyplus/
https://atb.nrel.gov/electricity/2022/utility-scale_battery_storage
https://www.eia.gov/outlooks/aeo/

## Slide 4: Starting Capacity Mix Overview
Operational resources are from the May 2023 CDR report, and planned resources meeting Planning Guide Section 6.9(1) requirements are obtained from the March 2023 GIS report .
Two combined cycles, Midlothian and Hays, are recategorized from CT to Combined Cycles in 2024 LTSA
Retirements include economic retirements from model, fixed age retirements ( Coal units retire after 45 years and gas units retire after 60 years), permanent mothballed units and unconfirmed retirement capacities from May 2023 CDR

## Slide 5: 15-Year Total Capacity Mix Comparison (2025 to 2039)
The total capacity mix of 2024LTSA include an additional 32 GW of Solar, 11 GW of Battery and 2.7 GW of CC and CT resources compare to 2022LTSA.

## Slide 6: Preliminary Results of 2024 LTSA Current Trends

## Slide 7: Questions
Send questions or comments to:
  Fred.Khodabakhsh@ERCOT.com