## Slide 1
2024 Long-Term Load Forecast
Kate Lamb
Load Forecasting & Analysis

## Slide 2: Agenda
Introduction
Model Variables
Waterfall Method
- Baseline Forecast
- PV Forecast
- EV Forecast
- LFL Forecast
- Net Forecast
Scenarios
- Summer and Winter Peaks
- Uri and Elliot
- 90th Percentile Forecast

## Slide 3
Introduction

## Slide 4: Input Data
Weather Zone level
- Weather
- Calendar
- Economic
- Actual Load

## Slide 5: Load Model Variables
Unique Model for Each Weather Zone
Variables used:
  Day Name, Hour, Month
  Dry Bulb, Temperature Squared, Temperature Cubed, and Lagged variables
  Interaction variables
  ERCOT Holidays
  Different Economic Drivers for each zone (Residential, Business, or Industrial)

## Slide 6: Waterfall Methodology

## Slide 7: Waterfall Methodology
Net Forecast = Gross Forecast + EV Forecast + LFL Forecast – PV Forecast
Benefits:
Gives us the ability to provide forecasts for many scenarios
Reconstitution to avoid double counting load

## Slide 8
Baseline/Gross Forecast

## Slide 9: How it works
15 Weather Year Forecasts per Weather Zone
  Rank by Year and Month
  Sort by Rank
  Averaged across Weather Years
  Map to a moderate Weather Year
  *Individual Weather Year Forecasts can be used for weather scenarios like LTSA, LTRA, MORA, and other weather studies.
Year | Month | Day | Hour | Rank | Forecast based on 2011’s Weather
2024 | 1 | 13 | 20 | 1 | 16,159
2024 | 1 | 13 | 19 | 2 | 16,140
2024 | 1 | 13 | 11 | 3 | 16,055
2024 | 1 | 12 | 9 | 4 | 15,993
2024 | 1 | 12 | 8 | 5 | 15,979

## Slide 10: 2024 LTLF Annual Energy
Chart: ERCOT Annual Energy
| 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Historical Annual Energy | 279859.6871 | 284353.9065 | 288361.9987 | 298432.4753 | 304957.9249 | 306569.309 | 310833.7322 | 307366.3563 | 318268.5325 | 333968.6178 | 324986.4682 | 331715.6797 | 340115.3201 | 347470.2521 | 351344.2118 | 357227.0858 | 376506.7889 | 384318.668 | 382572.9108 | 396848.4302 | 431665.1289
NET_ERCOT_15pct | 472118.791 | 488883.638 | 505479.912 | 521838.937 | 537265.483 | 549441.418 | 555619.525

## Slide 11: Annual Energy Forecast
Chart: GWh
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
2022 LTLF | 460428.7627 | 469633.6408 | 476838.7511 | 484883.461 | 490231.6813 | 496464.3935
2023 LTLF | 480009.0692 | 494259.9219 | 508344.4895 | 516425.159 | 521236.6728 | 527020.0229
2024 LTLF | 488883.638 | 505479.912 | 521838.937 | 537265.483 | 549441.418 | 555619.525

## Slide 12
Rooftop PV Forecast

## Slide 13: Rooftop PV Forecast
Rank | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | P50
1 | 21,257 | 20,994 | 20,757 | 20,752 | 21,015 | 20,748 | 21,295 | 21,047 | 21,857 | 21,799 | 21,132 | 20,842 | 21,582 | 21,349 | 20,738 | 21,144
2 | 21,211 | 20,840 | 20,099 | 20,542 | 20,981 | 20,368 | 21,162 | 20,950 | 21,830 | 20,910 | 20,979 | 20,839 | 21,558 | 21,064 | 20,689 | 20,935
3 | 21,191 | 20,763 | 20,095 | 20,422 | 20,769 | 20,330 | 20,938 | 20,851 | 21,631 | 20,904 | 20,926 | 20,746 | 21,353 | 20,998 | 20,542 | 20,831
4 | 21,059 | 20,740 | 20,088 | 20,294 | 20,726 | 20,305 | 20,934 | 20,814 | 21,617 | 20,825 | 20,926 | 20,718 | 21,249 | 20,977 | 20,470 | 20,783
5 | 20,923 | 20,446 | 19,976 | 20,221 | 20,708 | 20,144 | 20,844 | 20,797 | 21,568 | 20,804 | 20,897 | 20,677 | 21,211 | 20,968 | 20,462 | 20,710
Rooftop solar load forecast was generated by customer class (Residential/ Business)
Based on historical data from January 2012 to July 2023
Usage per customer was modeled to create a typical profile of rooftop solar customers
Along with weather and calendar drivers, solar irradiance was used to better capture solar generation
Customer forecast was generated using most recent growth rates with a gradual decline over time
The mapping year used was 2022

## Slide 14: Rooftop PV
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
PV Max | -1467.4909 | -2021.3918 | -2743.0729 | -3657.6839 | -4783.7237 | -6128.0058
PV On peak | -1061.39 | -1463.3 | -1986.118 | -2648 | -3458 | -4436

## Slide 15
EV Forecast

## Slide 16: EV Forecast Assumptions
Charging types used
County
Average miles traveled in LDV/MHDV
Fleet breakdown (Count of vehicle types)
Temperature
Breakdown of plug-in hybrid and battery electric vehicles
Calendar assumptions (days in season, day type, average driving hours by season)

## Slide 17: EV Peak Load Forecast
Chart: MW
| 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Peaks | 221.2179 | 299.1582 | 409.4223 | 570.1384 | 791.0953 | 1081.2835 | 1466.5599

## Slide 18: LFL Forecast

## Slide 19: LFL Adjustments
Two Scenarios were created
  - 100% LFL added to all hours and days of our baseline forecast
  - Summer response scenario: Reduce LFL to 15% from hours 14:00 to 21:00 for June, July, August, and September.

## Slide 20: LFL Peak Growth
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
 | 3153.6759 | 4000.3117 | 4846.9476 | 5693.5834 | 6540.2192 | 7386.855 | 8233.4908

## Slide 21
Forecast Breakdown

## Slide 22: Coast Summer NCP Forecast
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Gross | 21636.9472 | 21877.1386 | 22126.3343 | 22378.8601 | 22479.2225 | 22734.9433
Gross + EV | 21676.5868 | 21932.083 | 22175.298 | 22447.3566 | 22658.9088 | 22978.0238
Gross + EV + LFL 15% | 21682.4537 | 21940.3544 | 22185.974 | 22460.4372 | 22674.3455 | 22995.8577
Gross + EV + LFL 15% - PV | 21461.5638 | 21633.9472 | 21767.9936 | 21900.8303 | 22070.9304 | 22220.91

## Slide 23: Coast Winter NCP Forecast
Chart: 
| 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029
Gross | 16932.4899 | 17176.7892 | 17427.4821 | 17680.8322 | 17936.5928
Gross + EV | 17039.4056 | 17238.4068 | 17512.6152 | 17956.1183 | 18307.3787
Gross + EV + LFL 100% | 17086.1715 | 17301.0776 | 17591.1907 | 18050.5987 | 18417.7639
Gross + EV + LFL 100% - PV | 17082.8806 | 17296.5322 | 17585.0311 | 18042.4164 | 18407.1142

## Slide 24: FWest Summer NCP Forecast
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Gross | 6193.3874 | 6575.6894 | 6985.1427 | 7392.6567 | 7602.1101 | 7813.5028
Gross + EV | 6194.6273 | 6578.627 | 6989.9014 | 7400.2331 | 7613.2348 | 7823.7185
Gross + EV + LFL 15% | 7272.1136 | 7967.3846 | 8689.9303 | 9411.5333 | 9935.8063 | 10457.5613
Gross + EV + LFL 15% - PV | 7272.1136 | 7967.3846 | 8689.9303 | 9411.5333 | 9935.8063 | 10457.5613
* FWest Summer peaks at HE 22 due to LFL reduction on peak hours

## Slide 25: FWest Summer Peaks
Chart: 
| 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033
Fwest Historical | 1829.969 | 1805.013 | 1735.146 | 1760 | 1869.45 | 1767.031 | 1886.498 | 1739.459 | 1867.422 | 2102.653 | 2172.245 | 2278.671 | 2688.004 | 2811.841 | 2908.97 | 3164.186 | 3655.014 | 4307.553 | 4438.851 | 5127.551 | 5474.819 | 6639.787
Fwest Summer Peaks | 7272.1136 | 7967.3846 | 8689.9303 | 9411.5333 | 9935.8063 | 10457.5613 | 10964.1916 | 11467.4619 | 11962.9746 | 12442.9722

## Slide 26: FWest Winter NCP Forecast
Chart: 
| 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029
Gross | 6905.5233 | 7298.2979 | 7708.9149 | 7935.0234 | 8149.1313
Gross + EV | 6906.1312 | 7298.8107 | 7709.7583 | 7937.2216 | 8152.1662
Gross + EV + LFL 100% | 8131.1684 | 8827.9608 | 9543.0212 | 10074.5973 | 10593.6547
Gross + EV + LFL 100% - PV | 8131.1684 | 8827.9608 | 9543.0212 | 10074.5973 | 10593.6547

## Slide 27: NCENT Summer NCP Forecast
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Gross | 26934.3906 | 27073.3576 | 27229.9979 | 27393.6165 | 27556.4477 | 27716.2515
Gross + EV | 26974.5915 | 27159.6951 | 27352.0818 | 27564.5541 | 27793.4112 | 27918.848
Gross + EV + LFL 15% | 27064.6868 | 27281.4411 | 27505.4787 | 27749.6017 | 28010.1096 | 28167.1971
Gross + EV + LFL 15% - PV | 26652.529 | 26714.5983 | 26737.9143 | 26728.4505 | 26677.793 | 26464.7046
Hour Ending 19 | 26856.6336 | 26708.474

## Slide 28: NCENT Winter NCP Forecast
Chart: 
| 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029
Gross | 23193.9293 | 23341.2954 | 23501.3669 | 23664.5258 | 23826.206
Gross + EV | 23229.855 | 23359.6014 | 23527.0162 | 23761.4169 | 23958.5119
Gross + EV + LFL 100% | 23928.0298 | 24263.2874 | 24636.2132 | 25076.125 | 25478.7311
Gross + EV + LFL 100% - PV | 23916.0254 | 24247.527 | 24615.7357 | 25049.8611 | 25445.5294

## Slide 29: ERCOT Summer Coincident Peak
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Gross | 82775.9858 | 84000.2149 | 85196.8969 | 86409.5774 | 87326.6923 | 88237.9384
Gross + EV | 82866.6745 | 84195.3677 | 85474.7783 | 86802.6724 | 87871.332 | 88707.3933
Gross + EV + LFL 15% | 83300.3553 | 84753.7452 | 86157.8526 | 87610.4434 | 88803.7997 | 89764.5578
Gross + EV + LFL 15% - PV | 82239.008 | 83290.5122 | 84171.7346 | 84961.8845 | 85340.0626 | 85328.2493
Hour Ending 22 | 77922.2645 | 80185.4264 | 82360.3417 | 84607.5944 | 86623.4108 | 88141.4062

## Slide 30: ERCOT Winter Coincident Peak
Chart: 
| 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029
Gross | 68263.873 | 69523.3446 | 70733.2044 | 71773.8809 | 72669.9343
Gross + EV | 68293.1306 | 69565.0134 | 70892.913 | 71993.8698 | 72969.4293
Gross + EV + LFL 100% | 71607.8308 | 73709.9968 | 75868.1796 | 77799.4195 | 79605.2621
Gross + EV + LFL 100% - PV | 71573.5931 | 73663.0716 | 75805.0213 | 77716.051 | 79497.3646

## Slide 31: ERCOT Summer Non-Coincident Peak
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Gross_ERCOT | 83276.4705 | 84500.5025 | 85697.2025 | 86909.7475 | 87466.6338 | 88377.6945
Gross + EV | 83382.6517 | 84694.4691 | 85943.051 | 87256.9405 | 88046.1743 | 88988.0897
Gross + EV + LFL 15% | 84943.7655 | 86709.2001 | 88411.3992 | 90178.9059 | 91421.7086 | 92817.2338
Gross + EV + LFL 15% - PV | 84066.7895 | 85502.1504 | 87016.971 | 88496.5132 | 89916.8372 | 90928.4057

## Slide 32: ERCOT Winter Non-Coincident Peak
Chart: 
| 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029
Gross | 74010.9678 | 75266.8999 | 76474.2482 | 77507.288 | 78427.0849
Gross + EV | 74183.9394 | 75387.1345 | 76654.7366 | 77979.4332 | 79020.4879
Gross + EV + LFL 100% | 77496.7713 | 79529.9067 | 81627.4489 | 83782.0858 | 85653.0807
Gross + EV + LFL 100% - PV | 77477.8546 | 79504.8006 | 81594.5144 | 83739.4851 | 85598.8222

## Slide 33
Uri and Elliott

## Slide 34: Uri Peaks
Rank | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | P50
1 | 21,257 | 20,994 | 20,757 | 20,752 | 21,015 | 20,748 | 21,295 | 21,047 | 21,857 | 21,799 | 21,132 | 20,842 | 21,582 | 21,349 | 20,738 | 21,144
2 | 21,211 | 20,840 | 20,099 | 20,542 | 20,981 | 20,368 | 21,162 | 20,950 | 21,830 | 20,910 | 20,979 | 20,839 | 21,558 | 21,064 | 20,689 | 20,935
3 | 21,191 | 20,763 | 20,095 | 20,422 | 20,769 | 20,330 | 20,938 | 20,851 | 21,631 | 20,904 | 20,926 | 20,746 | 21,353 | 20,998 | 20,542 | 20,831
4 | 21,059 | 20,740 | 20,088 | 20,294 | 20,726 | 20,305 | 20,934 | 20,814 | 21,617 | 20,825 | 20,926 | 20,718 | 21,249 | 20,977 | 20,470 | 20,783
5 | 20,923 | 20,446 | 19,976 | 20,221 | 20,708 | 20,144 | 20,844 | 20,797 | 21,568 | 20,804 | 20,897 | 20,677 | 21,211 | 20,968 | 20,462 | 20,710
Chart: 
| 2021 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
 | 84682.5157 | 89580.417 | 91957.8701 | 94047.5712 | 96087.679 | 97937.0878 | 99684.8801 | 101412.4092

## Slide 35: Uri Peaks
2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
89,580 | 91,958 | 94,047 | 96,087 | 97,937 | 99,684 | 101,412

## Slide 36: Elliott Peaks
Chart: 
| 2022 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
 | 74476.7751 | 81392.0993 | 83471.6185 | 85508.0766 | 87552.3854 | 89303.9655 | 91033.8367 | 92740.1084

## Slide 37: Elliott Peaks
2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
81,392 | 83,472 | 85,508 | 87,552 | 89,304 | 91,034 | 92,740

## Slide 38
Questions?

## Slide 40: East Summer NCP Forecast
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Gross | 2923.5744 | 2948.4339 | 2973.3628 | 2997.1857 | 3022.1792 | 3048.2961
Gross + EV | 2925.9305 | 2951.8108 | 2976.7026 | 3002.2461 | 3033.0466 | 3063.3739
Gross + EV - PV | 2908.6324 | 2929.5467 | 2948.4172 | 2966.8327 | 2989.4091 | 3010.5012

## Slide 41: East Winter NCP Forecast
Chart: 
| 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029
Gross | 2872.8872 | 2898.8518 | 2924.1564 | 2949.535 | 2976.1606
Gross + EV | 2874.1175 | 2899.5949 | 2925.2776 | 2953.2176 | 2981.2216
Gross + EV - PV | 2873.9098 | 2899.3274 | 2924.9383 | 2952.7941 | 2980.7016

## Slide 42: North Summer NCP Forecast
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Gross | 1902.5191 | 1920.6424 | 1939.1796 | 1958.2017 | 1978.4014 | 1999.2245
Gross + EV | 1903.7064 | 1923.6018 | 1944.1553 | 1965.3509 | 1988.2791 | 2006.9251
Gross + EV + LFL 15% | 2152.4206 | 2247.0735 | 2342.3843 | 2438.3374 | 2536.023 | 2629.4264
Gross + EV + LFL 15% - PV | 2152.4206 | 2247.0735 | 2342.3843 | 2438.3374 | 2536.023 | 2629.4264

## Slide 43: North Winter NCP Forecast
Chart: 
| 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029
Gross | 1700.2395 | 1718.2726 | 1736.8045 | 1756.0707 | 1776.1912
Gross + EV | 1700.9213 | 1718.7047 | 1737.4356 | 1758.2753 | 1779.1677
Gross + EV + LFL 100% | 1983.4444 | 2075.1757 | 2167.8545 | 2262.642 | 2357.4823
Gross + EV + LFL 100% - PV | 1982.3277 | 2073.7738 | 2166.1127 | 2260.504 | 2354.892

## Slide 44: SCENT Summer NCP Forecast
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Gross | 14352.0402 | 14691.6221 | 14944.9988 | 15205.6813 | 15364.2048 | 15516.158
Gross + EV | 14369.4908 | 14728.0983 | 14996.0172 | 15277.5231 | 15463.0627 | 15603.995
Gross + EV + LFL 15% | 14508.442 | 14900.5826 | 15202.0347 | 15517.0737 | 15736.1464 | 15910.6119
Gross + EV + LFL 15% - PV | 14431.129 | 14790.3651 | 15047.6198 | 15304.9555 | 15450.9918 | 15536.0097
Hour Ending 22 | 14189.3108 | 14796.5987 | 15305.3408 | 15832.2222 | 16267.5135 | 16612.0443

## Slide 45: SCENT Winter NCP Forecast
Chart: 
| 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029
Gross | 13361.7627 | 13707.6926 | 13964.7606 | 14224.4772 | 14380.3297
Gross + EV | 13382.405 | 13736.3726 | 14004.9044 | 14279.4411 | 14408.2212
Gross + EV + LFL 100% | 14442.7358 | 15027.1669 | 15526.1624 | 16031.1627 | 16390.4064
Gross + EV + LFL 100% - PV | 14440.9378 | 15024.6117 | 15522.6048 | 16026.3159 | 16383.9468

## Slide 46: South Summer NCP Forecast
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Gross | 7251.8464 | 7315.8217 | 7382.6353 | 7449.8814 | 7356.7589 | 7424.1846
Gross + EV | 7254.8739 | 7320.3488 | 7389.5752 | 7460.276 | 7380.736 | 7456.9663
Gross + EV - PV | 7137.6368 | 7156.792 | 7165.1203 | 7157.878 | 7190.8354 | 7211.6763

## Slide 47: South Winter NCP Forecast
Chart: 
| 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029
Gross | 7027.6893 | 7092.962 | 7159.9398 | 7227.3956 | 7295.0378
Gross + EV | 7033.8362 | 7101.6813 | 7186.0643 | 7263.0972 | 7343.0254
Gross + EV - PV | 7033.3372 | 7101.1055 | 7185.4056 | 7262.351 | 7342.1882

## Slide 48: West Summer NCP Forecast
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Gross | 2081.7653 | 2097.7969 | 2115.5511 | 2133.664 | 2107.3092 | 2125.1338
Gross + EV | 2082.8445 | 2100.2043 | 2119.3196 | 2139.4005 | 2115.4952 | 2136.239
Gross + EV - PV | 2050.7642 | 2056.2093 | 2059.8703 | 2060.4288 | 2069.6859 | 2077.8122

## Slide 49: West Winter NCP Forecast
Chart: 
| 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029
Gross | 2016.4466 | 2032.7383 | 2050.823 | 2069.4281 | 2087.4355
Gross + EV | 2017.2677 | 2033.9621 | 2051.665 | 2070.6452 | 2090.7954
Gross + EV - PV | 2017.2677 | 2033.9621 | 2051.665 | 2070.6452 | 2090.7954