## Slide 1
ADER Pilot Project – Phase 1 Report and Phase 2 Governing Document
David Maggio
Principal, Market Design & Analytics
Technical Advisory Committee (TAC) Meeting
January 24, 2024

## Slide 2: Introduction
This presentation is intended to provide an update on the ADER Pilot Project, including:
  The current state of the Pilot Project;
  Observations from Phase 1; and
  Proposed changes for a Phase 2.
Included in the meeting materials with this presentation are drafts of the ADER Pilot Project Phase 1 report and a Governing Document for Phase 2 (provided as edits to the Phase 1 Governing Document), both with and without comments from external parties.
Several ADER Task Force participants have provided comments to the Phase 2 Governing Document. Those comments are still being reviewed and have not yet been incorporated into ERCOT’s draft.
  Feedback will be incorporated into the version that is expected to go the ERCOT Board in February.
While a vote from TAC is not required for the Governing Document, ERCOT did want to provide an update and opportunity for feedback and discussion.

## Slide 3: Pilot Project status overview
7.0 MW (6)
1.4 MW (2)
4.3 MW (1)
  9.4 MW capability for energy
  3.1 MW capability for Non-Spinning Reserve Service (Non-Spin)
ERCOT has accepted seven additional Details of the Aggregation (DOTA) forms. These potential ADERs are in various stages of registration and qualification and cannot fully participate at this time.
Discussions on what a second phase of the Pilot might look like have started. This presentation will share some initial observations and ERCOT staff’s current thoughts on phase 2 changes and scope.
There are currently 2 ADERs that have been qualified to participate in the wholesale electric market with participation starting in late August.
DOTA energy capability and ADER count for 9 ADERs with approved DOTA forms

## Slide 4: Participation limits tracking as of January 16, 2024
 |  | LZ_AEN | LZ_CPS | LZ_HOUSTON | LZ_LCRA | LZ_NORTH | LZ_RAYBN | LZ_SOUTH | LZ_WEST | ERCOT-WIDE
Energy | Limit (MW) | 2.8 | 5.3 | 20.3 | 3.1 | 28.7 | 1.2 | 10.3 | 8.2 | 80.0
 | Approved (MW) | 0 | 0 | 7 | 0 | 4.3 | 0 | 1.4 | 0 | 12.7
 | Unused (MW) | 2.8 | 5.3 | 13.3 | 3.1 | 24.4 | 1.2 | 8.9 | 8.2 | 67.3
 | % Full | 0% | 0% | 35% | 0% | 15% | 0% | 14% | 0% | 16%
Non-Spin | Limit (MW) | 1.4 | 2.7 | 10.1 | 1.6 | 14.3 | 0.6 | 5.2 | 4.1 | 40.0
 | Approved (MW) | 0 | 0 | 2.4 | 0 | 1.4 | 0 | 0.5 | 0 | 4.3
 | Unused (MW) | 1.4 | 2.7 | 7.7 | 1.6 | 12.9 | 0.6 | 4.7 | 4.1 | 35.7
 | % Full | 0% | 0% | 24% | 0% | 10% | 0% | 10% | 0% | 11%

## Slide 5: Summary statistics for actively participating ADERs, through December 2023
Metric | Resource-interval count
SCED Intervals evaluated | 76,538
SCED Intervals where the ADER was on-line | 46,952
SCED Intervals with non-zero Non-Spin Responsibility | 16,667
SCED Intervals with ADERs dispatched | 459
SCED Intervals with ADERs deployed for Non-Spin | 0
Majority of energy-dispatch participation has been between hours beginning 6 and 20.
Majority of Non-Spin provision has been between hours beginning 6 and 17.

## Slide 6: Evaluations and recommendations for Phase 2
While data around participation of ADERs in the market has been somewhat limited, both in terms of amount of time and number of Resources, there is sufficient information to share initial thoughts and propose incremental changes for a phase 2.
Telemetry validation processes and requirements
  ERCOT staff is proposing amendments to the “Validation” section of the Governing Document based on flaws identified in Phase 1.
  The concept is to have the validation analysis focused only on intervals in which the aggregated device/premise-level data is greater than 10% of the Resource’s requested energy capability.
    E.g., for a +/- 1 MW ADER, only evaluate intervals where the aggregate injection or withdrawal exceeds 0.1 MW.
  There will be a minimum number of intervals that must meet the criteria for evaluation to ensure the sample size is sufficient.
  Additional details are included in the draft report included with the meeting material.

## Slide 7: Evaluations and recommendations for Phase 2 cont.
Expanding Ancillary Service product eligibility to include ERCOT Contingency Reserve Service (ECRS)
  ERCOT recommends expanding ECRS eligibility to include ADERs capable of meeting the requirements of providing this service, as defined within the ERCOT Protocol.
  This has been requested by ADER participants and is an opportunity to increase their participation in the market, while allowing for continued monitoring by ERCOT and the participants through the Pilot Project
  Like Non-Spin, there will be a limit in the amount of ADER capability that can be qualified under the Pilot Project to provide ECRS in Phase 2.

## Slide 8: Evaluations and recommendations for Phase 2 cont.
Continued review of compliance metrics for ADERs
  As noted in the Governing Document, ADERs use the ALR participation model under the Nodal Protocols, which includes the requirement that performance will be evaluated using the existing Controllable Load Resource Energy Deployment Performance (CLREDP) and Base Point Deviation processes for ALRs
  Those thresholds are:
  Under the current tolerances, ADERs smaller than 2 MW will always meet the stated performance criteria, which is clearly not the intent of having performance measures.
  ERCOT does not have a formal recommendation at this time. However, ERCOT recommends that the ADER Task Force and participants work together to consider whether an alternative dispatch compliance regime would be more appropriate, particularly for smaller ADERs.

## Slide 9: Evaluations and recommendations for Phase 2 cont.
Alternative participation models for ADERs
  Under the current program rules, ADERs must be SCED-dispatchable to participate in the Pilot Project. This requirement may preclude the participation of some Resource types that are able to respond but lack the ability to smoothly ramp over a 5-minute interval.
  It may be possible to increase ADER Pilot Project participation by considering enabling a participation framework for a “blocky” Resource type.
  Prior to making a formal recommendation on whether and how to proceed with enabling participation of this Resource type, ERCOT and stakeholders would need to consider the following:
    To what extent is this Resource enabled to participate today? What barriers exist?
    What system changes would be required to fully enable the participation of this Resource type and what would be the commitment in terms of cost, resourcing and time? Are any work-arounds available?
    When and how could this work be accommodated given existing commitments?
    What is the scope of potential benefit (e.g., in terms of additional Resources/MW capability that may be enabled) of developing different frameworks?

## Slide 10: Evaluations and recommendations for Phase 2 cont.
Alternatives to dispatch using Load Zone shift factors
  Under the current participation model, ADERs are dispatched using Load Zone shift factors, and settled at their respective Load Zone price. The use of Load Zone shift factors may not be an accurate reflection of these Resources’ impact on power system flow and, therefore, transmission congestion.
  ERCOT staff has begun evaluating an alternative method to calculate ADER shift factors, which takes the average electrical bus shift factors of each of the ADER’s premises, weighted by its maximum injection capability.
    Initial results from the analysis are included in the draft report included with the meeting material.
  Intuitively, the use of “quasi-nodal” shift factors should result in improvements to overall congestion management. However, the current data indicate the impacts may be limited thus far.
  The recommendation for Phase 2 of the Pilot Project is to continue with the existing Load Zone shift factor paradigm and to continue to examine this issue for potential reliability risks and market inefficiencies.

## Slide 11: Next Steps
A presentation, Phase 1 report, and draft Phase 2 Governing Document are expected to go to the ERCOT Board in late February, including the Reliability and Markets Committee, with a potential vote on the Governing Document.
Between now and the deadline for posting material for the ERCOT Board, ERCOT staff will be working with ADER task force members and other interested parties to incorporate feedback and finalize the draft Governing Document.