## Slide 1
Annual Review of the Market Impacts of Reliability Unit Commitments
Analysis of 2023
Ryan King
Manager, Market Design
TAC
January 24, 2024
ERCOT Public

## Slide 2: Protocol Language
5.8 Annual RUC Reporting Requirement
(1) ERCOT shall report to the Technical Advisory Committee (TAC), each January, an assessment of market impacts and Settlements for the aggregate Reliability Unit Commitment (RUC) activity, delineated by type of RUC instruction as follows:
RUC instructions issued for Ancillary Service shortages (failure to sufficiently procure one or more Ancillary Service markets in the Day-Ahead Market (DAM) or subsequent Supplemental Ancillary Service Markets (SASMs));
RUC instructions issued for irresolvable transmission system constraints;
RUC instructions issued in anticipation of extreme cold weather/startup failures;
RUC instructions issued for capacity;
RUC instructions issued for system inertia; and
A summary of RUC Settlements;
(i) RUC charges associated with RUC Make-Whole Amount Total per RUC, as defined in Section 5.7.4.1, RUC Capacity-Short Charge; and
(ii) RUC Shortfall Total, as defined in Section 5.7.4.1.1, Capacity Shortfall Ratio Share.

## Slide 3: RUC-Instructed Resource-Hours in 2023
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, partial hour instructions, or otherwise not dispatchable by SCED.
 | Total | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  | 
Total Count | 2,726 | 527 | 2,199
Effective Resource-Hours* |  |  | 
Total Count | 2,500.6 | 509.5 | 1,991.1
Average LSL | 62.1 | 69.7 | 60.2
Average LDL | 76.2 | 123.8 | 63.8
Average BP | 81.0 | 140.3 | 65.7
Average HSL | 208.9 | 237.8 | 201.4

## Slide 4: RUC Instruction Reasons
2,500.6 effective RUC Resource-hours in 2023.
  80.6 Resource-hours (3.2%) for local thermal congestion or voltage concerns.
  2,420.0 Resource-hours (96.8%) for capacity concerns.
There were no Resource-hours committed for Ancillary Service shortages, system inertia, or startup failures.
509.5 effective Resource-hours (20.4%) were successfully bought back.
  This value is equal to last year (20.4% bought back in 2022).
  Included in this value are 27.0 effective Resource-hours (1.1% of total) where the Resource was DAM-committed.

## Slide 5: RUC-Instructed Effective Resource-Hours, 2020 - 2023

## Slide 6: RUC-Instructed Effective Resource-MWh, 2020 - 2023
Top: Duration multiplied by Resource’s Base Point (BP).
Bottom: Duration multiplied by Resource’s High Sustained Limit (HSL).

## Slide 7: Average Age of Effective Resource-Hours, 2020 - 2023
In the case of Resources with multiple physical generators, the age of the oldest generator is used.

## Slide 8: RUC-Instructed Effective Resource-Hours by Resource Age, 2020 - 2023
OPT-OUT
.
NON-OPT-OUT

## Slide 9: RUC-Instructed Resource Dispatch above LDL
When Resources did not successfully opt out, there were 92.7 Resource-hours when the Resource was dispatched above its LDL.
  For 38.7 of these Resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 54.0 of these Resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
    For 54.0 of these Resource-hours, the RUC-instructed Resource was mitigated.
    There were no Resource-hours associated with a RUC for additional capacity.
    There were no Resource-hours for which a non-mitigated RUC-instructed Resource was DAM-committed. (Hours meeting these criteria are treated as a RUC opt out.)

## Slide 10: Reliability Deployment Price Adder
Month of 2023 | Total RTORDPA Time (Hours) | Time-weighted Average RTORDPA ($/MWh)
Jan | 35.42 | 0.46
Feb | 79.67 | 1.35
Mar | 72.15 | 1.84
Apr | 156.34 | 0.80
May | 206.84 | 2.21
Jun | 143.03 | 0.81
Jul | 59.95 | 0.59
Aug | 84.97 | 14.68
Sep | 81.24 | 4.27
Oct | 27.92 | 0.52
Nov | 46.83 | 0.61
Dec | 7.00 | 0.01

## Slide 11: RUC Make-Whole and Claw Back, 2020 - 2023
$3.67M in Make-Whole paid out over the year. Only $17.43 uplifted to Load. Settlement data retrieved 01/11/2024.

## Slide 12: Exceptional Fuel Cost Submissions
No resources with RUC instructions reported exceptional fuel costs.

## Slide 13: Additional Observations
In 2023, 2,726 instructed RUC Resource-hours resulted in 2,500.6 effective RUC Resource-hours.
  As compared to 8,244.8 and 7,910.5 for 2022, respectively.
  20.4% of effective resource-hours were bought back.
The total RUC make-whole amount was ~$3.672M.
  Almost exclusively covered through capacity-short charges.
The total RUC claw back charge amount was ~$3.451M.
Settlement data retrieved 01/11/2024.

## Slide 14: Additional Observations
Several factors may have contributed to the reduction in RUC observed in 2023 v. 2022
  General changes in resource-owner real-time price expectations
  Higher demand (both from overall population growth and from an increase in the number of extreme hot weather days particularly in August)
  Introduction of ERCOT Contingency Reserve Service (ECRS)
  Lower average natural gas prices compared to 2022
Direct cause and effect of individual factors and their relative impacts on commitment decisions can be difficult to discern:
  Some factors may have been present all of the time
  All factors may have been present some of the time
ERCOT will continue to monitor and report on observations and factors contributing to changes in commitment (including ORDC Price Floors introduced in November 2023 and changes to the opt out process under NPRR1092).

## Slide 15: Appendix

## Slide 16: RUC-Instructed Effective Resource-Hours by Opt Out Status*
Month | 2020 | 2021 | 2022 | 2023
Jan | 3 | 5 | 80 | 167
Feb | 12 | 5 | 930 | 249
Mar | 1 | 5 | 200 | 147
Apr | 0 | 8 | 328 | 362
May | 0 | 0 | 382 | 445
Jun | 0 | 248 | 511 | 309
Jul | 21 | 968 | 672 | 114
Aug | 151 | 378 | 870 | 11
Sep | 0 | 339 | 1,124 | 74
Oct | 0 | 573 | 305 | 33
Nov | 3 | 107 | 517 | 73
Dec | 0 | 11 | 381 | 7
Month | 2020 | 2021 | 2022 | 2023
Jan | 0 | 0 | 26 | 99
Feb | 0 | 269 | 62 | 0
Mar | 0 | 24 | 62 | 38
Apr | 0 | 63 | 163 | 42
May | 6 | 0 | 219 | 102
Jun | 0 | 89 | 108 | 31
Jul | 11 | 229 | 236 | 67
Aug | 8 | 203 | 176 | 2
Sep | 0 | 139 | 225 | 41
Oct | 4 | 102 | 106 | 12
Nov | 0 | 73 | 209 | 76
Dec | 0 | 14 | 19 | 0
Did Not Opt Out
Opted Out
* Effective Resource-hours rounded to nearest whole number

## Slide 17: RUC Make-Whole and Claw Back, 2020-2021
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2020 | 2021 | 2020 | 2021 | 2020 | 2021 | 2020 | 2021 | 2020 | 2021
Jan | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 1 | 0 | 0
Feb | 0 | 0 | 0 | 0 | 0 | 0 | 168 | 1,256 | 394 | 0
Mar | 0 | -9 | 0 | 9 | 0 | 0 | 19 | 6 | 0 | 239
Apr | 0 | -19 | 0 | 19 | 0 | 0 | 0 | 0 | 0 | 263
May | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Jun | 0 | -466 | 0 | 466 | 0 | 0 | 0 | 91 | 0 | 7,004
Jul | -40 | -2,045 | 40 | 2,045 | 0 | 0 | 82 | 637 | 148 | 17,404
Aug | -356 | -865 | 356 | 865 | 0 | 0 | 210 | 59 | 2197 | 12,626
Sep | 0 | -833 | 0 | 833 | 0 | 0 | 0 | 54 | 0 | 11,812
Oct | 0 | -862 | 0 | 862 | 0 | 0 | 0 | 918 | 0 | 9,766
Nov | -8 | -61 | 8 | 61 | 0 | 0 | 0 | 89 | 140 | 1,312
Dec | 0 | -86 | 0 | 86 | 0 | 0 | 0 | 0 | 0 | 1,102
Amounts rounded to nearest thousand. Settlement data retrieved on 01/11/2024.

## Slide 18: RUC Make-Whole and Claw Back, 2022-2023
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2022 | 2023 | 2022 | 2023 | 2022 | 2023 | 2022 | 2023 | 2022 | 2023
Jan | -320 | -301 | 320 | 301 | 0 | 0 | 38 | 822 | 3,760 | 1886
Feb | -6,970 | -327 | 6,970 | 327 | 0 | 0 | 7,628 | 157 | 7,519 | 3045
Mar | -749 | -441 | 749 | 441 | 0 | 0 | 102 | 180 | 6,203 | 5695
Apr | -742 | -914 | 742 | 914 | 0 | 0 | 1,285 | 50 | 7,138 | 11694
May | -3,302 | -470 | 3,302 | 470 | 0 | 0 | 7,293 | 364 | 10,604 | 8601
Jun | -6,014 | -687 | 6,014 | 687 | 0 | 0 | 12 | 149 | 17,784 | 8007
Jul | -4,702 | -168 | 4,702 | 168 | 0 | 0 | 5,509 | 158 | 17,815 | 5137
Aug | -3,464 | -12 | 3,464 | 12 | 0 | 0 | 986 | 352 | 14,129 | 321
Sep | -4,666 | -35 | 4,666 | 35 | 0 | 0 | 365 | 998 | 20,059 | 561
Oct | -889 | -116 | 889 | 116 | 0 | 0 | 528 | 191 | 7,153 | 758
Nov | -809 | -195 | 809 | 195 | 0 | 0 | 952 | 30 | 8,361 | 2556
Dec | -1,479 | -5 | 1,479 | 5 | 0 | 0 | 148 | 0 | 6,437 | 305
Amounts rounded to nearest thousand. Settlement data retrieved on 01/11/2024.