## Slide 1
NPRR 1092 Introduction
Reduce RUC Offer Floor and Limit RUC Opt-Out Provision
February 13, 2024

## Slide 2: Topics to Be Covered
General Background
Main Concept
Requirements
Examples

## Slide 3: General Background
NPRR1092 was sponsored by the Independent Market Monitor (IMM) and approved by PUCT effective on May 12, 2022.
Comprised of two key changes
  RUC offer floor of $1,500/MWh was updated to $250/MWh according to TAC proposal effective on May 13, 2022
  Limiting RUC opt-out provision was implemented in 2024-R1 Market Facing Changes on January 25, 2024, along with following Business Practice Manual (BPM) changes.
    COP Practice by QSE
    ERCOT and QSE Operation Practices During the Operating Hour
Changes to Opt-Out Provision will be the focus of today’s discussion

## Slide 4: Main Concept
The previous rule where Opt-Out choice was determined by SCED telemetry no longer applies. Under 1092 the concept of an Opt-Out Snapshot Time is now in place.
  Snapshot Time is record of a Resource’s Current Operating Plan (COP) used to determine whether the Resource will opt out of RUC Settlement for a block of RUC-Committed Hours
The Snapshot is taken at the earlier of:
  Two hours prior to the end of the Adjustment Period for the first hour of a contiguous block of RUC-Committed Hours; or
  Two hours prior to the beginning of the hour that is at least N hours prior to the first hour of the contiguous block of the RUC-Committed hours, where N is the start time contained in the ERCOT computer system at the time of the RUC execution associated with the RUC instruction corresponding to the Resource’s warmth state. If the RUC-Committed Hours are an extension of a QSE-Committed Interval either before or after, N will be set to zero.

## Slide 5: Main Concept - Example
Assume HRUC commits UNIT1A as of 6:25AM for the same day HE 14 through HE 17 and the unit has a corresponding warmth state start time of 4 hours.
  If the unit is showing a resource status of OFF in its COP for HE13 and HE18 at RUC study, then (from description in previous slide) N = 4, time A=10am, and time B=7am. Opt-Out Snapshot is the earlier of A and B hence snapshot time is 7am. The QSE will need to update its HE14 COP to reflect its Opt-Out decision prior to 7am.
  If the unit has ON COP status for HE13 or HE18 at RUC study, then N = 0, A=10am, B=11am. Opt-Out Snapshot time is the earlier of A and B hence snapshot time is 10am. The QSE will need to update its HE14 COP to reflect its Opt-Out decision prior to 10am.

## Slide 6: Requirements and Examples
The Next slides will look at requirements using different examples
Example 1: RUC Combine Cycle Units
  For these units, the startup time being used corresponds to the individual configuration
  COP opt out decision can use any configuration of the same train
Example 2: How the requirement is applied where the COP status of a resource was changed to ‘ON’ between the study snapshot being taken but before publication
Example 3: Verbal Dispatch Instruction RUC which extends an existing RUC block
  Note: No optout for standalone VDI
Example 4: RUC with Contiguous Block across the day

## Slide 7: Example 1
Combine cycle unit can opt out using any configuration of the same train

## Slide 8: Example 2
QSE updates COP to ON between study snapshot and results publication and automatically opts out. No additional COP updates needed.

## Slide 9: Example 3
Standalone VDI RUC is generally treated as ONRUC except when it concatenates an existing HRUC or DRUC block, in which opt-out choice depends on the first hour’s COP snapshot of the whole commitment block

## Slide 10: Example 4
QSE opts out across the day block with first hour’s opt-out choice