## Slide 1
Ancillary Service Demand Curves
(ASDCs)
Market Analysis
RTCBTF
February 21, 2024
ERCOT Public

## Slide 2: Introduction
One of the key issues for discussion at the RTC+B Task Force is a “Review of the AS Demand Curves in the context of current policy”.
Purpose of this presentation:
  Review of AS Demand Curve concept under RTC
  Explanation of approach and methodology
  Illustration of results

## Slide 3: Overview
Under RTC, the ORDC will not be used. Instead, scarcity pricing and the value of reserves are set by AS Demand Curves (ASDCs)
Chart: MW
| 0 | 10 | 20 | 25 | 27 | 30 | 30 | 33
Demand | 100 | 100 | 100 | 100 | 50 | 25 | 0
Offer | 0 | 4 | 9 | 12 | 14 | 17 | 17 | 20
Sufficient remaining capacity and offers
Insufficient remaining capacity or offers
Chart: MW
| 0 | 10 | 20 | 25 | 27 | 30 | 30 | 33
Demand | 100 | 100 | 100 | 100 | 50 | 25 | 0
Offer | 0 | 4 | 9 | 12 | 14
Value of the AS product in shortage

## Slide 4: Overview
Chart: Reserves (MW)
Chart: Reserves (MW)
| 250 | 2000 | 2000.0001 | 2080.0001000000002 | 2160.0001000000002 | 2240.0001000000002 | 2320.0001000000002 | 2400.0001000000002 | 2480.0001000000002 | 2550.0001000000002 | 2725.0001000000002 | 2900.0001000000002 | 3075.0001000000002 | 3250.0001000000002 | 3425.0001000000002 | 3600.0001000000002 | 3750.0001000000002 | 3900.0001000000002 | 3950.0001000000002 | 4050.0001000000002 | 4250.0001000000002 | 4550.0001000000002 | 4950.0001000000002 | 5450.0001000000002 | 6150.0001000000002 | 7000.0001000000002
 | 9000 | 9000 | 6618 | 6379 | 6127 | 5866 | 5597 | 5322 | 5044 | 4799 | 4188 | 3591 | 3037 | 2518 | 2064 | 1666 | 1372 | 1118 | 1044 | 906 | 673 | 419 | 210 | 79 | 16 | 2
Chart: Reserves (MW)
| 250 | 2000 | 2000.0001 | 2080.0001000000002 | 2160.0001000000002 | 2240.0001000000002 | 2320.0001000000002 | 2400.0001000000002 | 2480.0001000000002 | 2550.0001000000002 | 2725.0001000000002 | 2900.0001000000002 | 3075.0001000000002 | 3250.0001000000002 | 3425.0001000000002 | 3600.0001000000002 | 3750.0001000000002 | 3900.0001000000002 | 3950.0001000000002 | 4050.0001000000002 | 4250.0001000000002 | 4550.0001000000002 | 4950.0001000000002 | 5450.0001000000002 | 6150.0001000000002 | 7000.0001000000002
ORDC | 9000 | 9000 | 6618 | 6379 | 6127 | 5866 | 5597 | 5322 | 5044 | 4799 | 4188 | 3591 | 3037 | 2518 | 2064 | 1666 | 1372 | 1118 | 1044 | 906 | 673 | 419 | 210 | 79 | 16 | 2
Chart: Reserves (MW)
| 250 | 250 | 250 | 250 | 250 | 250 | 250 | 250
REGUP | 9000 | 9000 | 9000 | 9000 | 9000 | 9000 | 9000 | 9000
RRS | 9000 | 6379 | 6127 | 5866 | 5597 | 5322 | 5044 | 4799 | 0
ECRS | 4188 | 3591 | 3037 | 2518 | 2064 | 1666 | 1372 | 1118
NSPIN | 1044 | 906 | 673 | 419 | 210 | 79 | 16 | 2
Chart: Reserves (MW)
| 0 | 250 | 250 | 250 | 250 | 250 | 250 | 250 | 250 | 250
REGUP | 9000 | 9000 | 9000 | 9000 | 9000 | 9000 | 9000 | 9000 | 9000 | 0
RRS | 9000 | 9000 | 6379 | 6127 | 5866 | 5597 | 5322 | 5044 | 4799 | 0
ECRS | 4188 | 4188 | 3591 | 3037 | 2518 | 2064 | 1666 | 1372 | 1118 | 0
NSPIN | 1044 | 1044 | 906 | 673 | 419 | 210 | 79 | 16 | 2 | 0
ASDCs will be based on the shape and pricing outcomes of the ORDC

## Slide 5: RTC Key Principles KP1.1
To reasonably reflect the current RTM pricing outcomes expected with the ORDC methodology changes being made starting in March, 2020, the following steps will be taken to develop a single aggregate ORDC for disaggregation into individual ASDCs:
  For all Security-Constrained Economic Dispatch (SCED) intervals where the sum of RTOLCAP and RTOFFCAP is less than 10,000MW, use the historical RTOLCAP and RTOFFCAP values to calculate the composite LOLP and composite price with composite price defined as:
  To account for lower reserve level areas where there are no historical observations, create a single point using the following assumptions:
    RTOFFCAP = 0, RTOLCAP = 2,000MW
    Set System Lambda equal to the average of system lambda, with the historical values capped at $250/MWh, during SCED timestamps with less than or equal to 4,000MW of total reserves
  Using the results of (a) and (b) above, use regression methods to fit a curve to the average reserve pricing outcomes for the various MW reserve levels.
The RTC Key Principles outline the methodology to calculate ASDCs and how it inherits the ORDC policy in place.

## Slide 6: RTC Key Principles KP1.1
ERCOT will design and implement parameters to represent the disaggregation of ASDCs so that potential future changes in values and distribution will not require system changes. The following steps will be taken to disaggregate the single aggregate ORDC into individual ASDCs:
  Place Reg-Up requirement at the highest priced MWs on the aggregate ORDC;
  Place Responsive Reserve Service (RRS) requirement at the highest priced open MWs on the aggregate ORDC;
  Place ERCOT Contingency Reserve Service (ECRS) requirement at the highest priced open MWs on the aggregate ORDC;
  Place Non-Spin requirement at the highest priced open MWs on the aggregate ORDC; and
  Fill remaining MWs on the aggregate ORDC priced at >= $0.01 as Non-Spin.
The RTC Key Principles outline the methodology to calculate ASDCs and how it inherits the ORDC policy in place.

## Slide 7: Methodology Summary
Calculate “Composite Price” using historical ORDC data
Take the average Composite Price per bin of reserve levels
Use regression methods to fit a curve to the binned average data
Apply LOLP = 1 to reserve levels below minimum contingency level (MCL)
Assign ancillary services to the curve in the following order
  REGUP (highest prices on the curve)
  RRS
  ECRS
  NSPIN (lowest prices on the curve)
The upcoming slides will provide a visualization for each step

## Slide 8: 1) Calculate “Composite Price” Using ORDC Outcomes
Composite price
Composite Price for each SCED interval between 01/01/2018 and 01/01/2024
Only considering reserve levels < 10,000 MW

## Slide 9: 2) Take the average Composite Price per bin of reserves
Reserve levels were split into 50 equally sized bins (200 MW each)
Calculated the average price per bin

## Slide 10: 3) Use regression methods to fit curve to binned averages
Determine mu and sigma to best fit binned averages
  Equation takes the form: (VOLL – 250) *(1-CDF(mu, sigma))
  CDF is the cumulative distribution function of a normal distribution
Polynomial and LOESS curve fitting methods were considered, but results were not guaranteed to be monotonically decreasing.
Best fit: Mu = 3760, sigma = 1180

## Slide 11: 4) Apply LOLP = 1 to reserve levels < MCL
Mu = 3760, sigma = 1180

## Slide 12: 5) Assign AS to the curve
Assign ancillary services to the curve in descending order of price.
The example below uses the AS plan for October 2024 Hour 19
  REGUP = 884 MW
  RRS = 2606 MW
  ECRS = 1748 MW
  NSPIN = 2403 MW

## Slide 13: ASDCs – Varying levels of AS procurement
Calculated ASDC for varying levels of total AS procurement from 2024 AS plan
Case Name | Month | Hour | REGUP (MW) | RRS (MW) | ECRS (MW) | NSPIN (MW) | Total AS (MW) | REGUP Max Price ($/MWh) | RRS Max Price ($/MWh) | ECRS Max Price ($/MWh) | NSPIN Max Price ($/MWh)
Min | 9 | 3 | 220 | 2529 | 1226 | 1651 | 5626 | 5000 | 5000 | 5000 | 2032
25% | 6 | 24 | 134 | 2491 | 1673 | 2475 | 6773 | 5000 | 5000 | 5000 | 1540
Mean | 9 | 17 | 484 | 2300 | 2853 | 1926 | 7563 | 5000 | 5000 | 5000 | 265
Median | 10 | 19 | 884 | 2606 | 1748 | 2403 | 7641 | 5000 | 5000 | 2805 | 500
75% | 5 | 5 | 301 | 2916 | 1443 | 3564 | 8224 | 5000 | 5000 | 3217 | 1058
Max | 5 | 14 | 564 | 2560 | 2514 | 4482 | 10120 | 5000 | 5000 | 3349 | 265
If REGUP and RRS are not shown in the graph above, it means their price is at $5000/MWh for the full range of their ASDC

## Slide 14: Appendix

## Slide 15: Appendix – ASDC, all cases