## Slide 1
ERCOT Workshop
RTC+B: Modifications to RUC Capacity Short Calculations
Sai Moorty
Market Design
February 19, 2024

## Slide 2: Background: RUC Capacity Short Calculation
Under the RTC+B Project, the Reliability Unit Commitment (RUC) process is being modified to co-optimize energy and Ancillary Service (AS) procurements to meet the forecasted Load and AS requirements.
The binding outputs of the RUC process (including ERCOT Operator approval) are commitment instructions to Generation Resources (GRs). RUC committed GRs are eligible for Make-Whole payments.
A RUC committed GR is eligible to receive Make-Whole payment if the revenues (from energy and AS) is less than the approved costs (for details, please refer Section 5 of the Nodal Protocols).
Under the RTC+B Project, the Make-Whole payments made to RUC committed GRs (cost of “RUCing” a GR), are recovered through Make-Whole Charges applied to QSEs in the following sequence:
  First: QSEs that are short on energy or AS for the RUC committed hours
  Then: If the charges collected from QSEs that are insufficient, then the remainder is collected from all QSEs on a Load Ratio Share (LRS) basis
  If there are no RUC committed GRs for a particular hour, there is NO MAKE-WHOLE CHARGE to a QSE, even if that QSE is short on energy and/or AS for that hour. The QSE may receive energy and AS imbalance charges in Real-Time.

## Slide 3: Reasons for Modification to RUC Capacity Short Calcs
Currently approved RTC+B related protocols (NPRR1009, NPRR1014, NPRR1029, NPRR1032, and NPRR1139) has changes to incorporate QSE-level energy and AS shortage calculation.
After the RTC+B Project was restarted, the NPRRs approved while the project was on hold (e.g., NPRR1093) were reviewed to analyze any impacts to the RTC+B Project. In this process the following items came up that impacted the RUC Capacity Short calculation:
Certain limitations in the approved RTC+B protocol changes:
  AS subtypes were not originally considered. For example, a QSE with RRS-PFR position could cover it with UFR or FFR, which should not be allowed.
  Logic for Reg-Down had a deficiency where it could be possible for the same Resource capacity to be used for Reg-Down as well as any other Up AS types/subtypes (Reg-Up, RRS-FFR,RRS-UFR,RRS-PFR, ECRSS, NSPINS).
  Logic for an Energy Storage Resource (ESR) providing AS when charging.
The need to incorporate ESR SOC considerations based on NPRR 1204.
An NPRR to modify the RUC Capacity Short calculations will be developed after discussions at RTCBTF.

## Slide 4: Overview of Modification to RUC Capacity Short Calcs
The modifications are to address the issues described in the previous slide
The RUC Capacity Short calculation process, in basic terms, is just an accounting procedure. It determines, for a particular hour using information from a “RUC Snapshot” and information from an “end of the Adjustment Period Snapshot”, if the Resources in the QSE’s portfolio can cover the QSE’s energy and AS position for that particular hour.
In summary, the structure of this section remains the same. However, some of the bill determinant calculations change. The table below summarizes the changes to the grey box Section 5.7.4.1.1.
Section | Description of Proposed Change
5.7.4.1.1 (11) and (14) : Ancillary Service Shortfall: @RUC snapshot and, @ end of Adjustment Period. | These two sections describe how the Ancillary Service (AS) shortfall in MW for a QSE is calculated according to the RUC Snapshot and, again, at the end of the Adjustment Period. Changes to section 5.7.4.1.1 (11) and (14): RUCASFSNAP, RUCASFADJ: The procedure by which the AS shortfall is calculated at the RUC Snapshot and at the end of the Adjustment Period will be revamped and is described in later sections.
5.7.4.1.1 (10) and (13) : Overall Shortfall : @RUC snapshot and, @ end of Adjustment Period. | These two sections describe how the overall shortfall in MW for a QSE is calculated according to the RUC Snapshot and, again, at the end of the Adjustment Period. Changes to section 5.7.4.1.1 (10) and (13): RUCCAPSNAP, RUCCAPADJ, each has two new terms ESRASSNAP, ESRASADJ (QSE AS MW Position covered by ESRs) and ESRMWSNAP, ESRMWADJ (MW discharge/charge to support QSE AS MW Position coverage as well as respect COP SOC values) at the RUC Snapshot and at the end of the Adjustment Period. The terms ESRASSNAP and, ESRMWSNAP are described later. The terms ESRASADJ and ESRMWADJ are the same calculation but evaluated at the end of the Adjustment Period In RCAPSNAP and, RCAPADJ, the HSL of ESRs in the QSEs portfolio is removed. This is replaced by ESRMWSNAP and ESRMWADJ in RUCCAPSNAP and RUCCAPADJ, respectively.

## Slide 5: Process Flow : RUC Capacity Short Calculation
INPUTS: For each hour in the RUC Snapshot;
Day-Ahead posting of AS Deployment Factors
Resource Registered Qualified AS MW Amounts for each AS subtype
QSE’s RTAML
QSE DAM energy and AS awards & QSE submitted data (energy and Capacity Trades, AS Trades, QSE’s Resource COP data, QSE’s Resource AS Offers, and DC Tie Imports)
PROCESSING/CALCULATIONS: For each hour in the RUC Snapshot;
Calculate for each Resource, per hour, the AS MW Capability, by AS subtype (ASMWCAPABILITY)
Perform calculations (using optimization technique) to determine:
ASMWCAPUSED : Calculated amount of a Resource capacity used to cover its QSE AS position, per hour.
ESRMWSNAP: Calculated total MW discharge/charge, per QSE, per hour, required to support hourly AS position taking into account deployment factors and difference in consecutive hours HBSOC.
ESRASSNAP: Calculated QSE’s AS MW position covered by the QSE’s ESR portfolio
QSE AS MW shortage (RUCASFSNAP):
  RUCASFSNAP ruc, q,i =QSE total AS position –
QSE Overall shortage (RUCOSFSNAP)
  RUCOSFSNAP ruc, q,i = Max (0, (( RTAML q, p,i * 4) + ASONPOSSNAP ruc, q,i – RUCCAPSNAP ruc, q,I ))

## Slide 6: Example 1: QSE with NCLR has RRS-UFR Position
QSE Position for energy and AS, RTAML |  |  |  |  |  |  |  |  |  | 
Energy (MW) +ve Purchase -ve Sale | RU (MW) | RD (MW) | FFR (MW) | UFR (MW) | PFR (MW) | ECRSM (MW) | ECRSS (MW) | NSPINM (MW) | NSPINS (MW) | RTAML (MWh)
100 | 0 | 0 | 0 | 100 | 0 | 0 | 0 | 0 | 0 | 25
QSE Resources |  |  |  |  | 
Res. Type | HSL or MPC | LSL or LPC | Qual. UFR (MW) | ASMWCAPABILITY ruc,q,h,UFR,NCLR (MW) | ASMWCAPUSED ruc,q,h,UFR,NCLR (MW)
NCLR | 100 | 0 | 100 | 100 | 100
RUC Capacity Short Calc | RUC Capacity Short Calc |  |  |  |  |  |  | 
RUCASSFSNAP ruc,q,i | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h | RUCCAPSNAP ruc,q,i | ASONPOSSNAP ruc,q, i | RUCOSFSNAP ruc,q, i | RUCSFSNAP ruc,q, i
0 | 0 | 0 | 0 | 100 | 200 | 100 | 0 | 0
Summary:
a) QSE is NOT short.

## Slide 7: Example 2: QSE with NCLR has RRS-PFR Position
QSE Position for energy and AS, RTAML |  |  |  |  |  |  |  |  |  | 
Energy (MW) +ve Purchase -ve Sale | RU (MW) | RD (MW) | FFR (MW) | UFR (MW) | PFR (MW) | ECRSM (MW) | ECRSS (MW) | NSPINM (MW) | NSPINS (MW) | RTAML (MWh)
100 | 0 | 0 | 0 | 0 | 100 | 0 | 0 | 0 | 0 | 25
QSE Resources |  |  |  |  | 
Res. Type | HSL or MPC | LSL or LPC | Qual. UFR (MW) | ASMWCAPABILITY ruc,q,h,UFR,NCLR (MW) | ASMWCAPUSED ruc,q,h,UFR,NCLR (MW)
NCLR | 100 | 0 | 100 | 100 | 0
RUC Capacity Short Calc | RUC Capacity Short Calc |  |  |  |  |  |  | 
RUCASSFSNAP ruc,q,i | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h | RUCCAPSNAP ruc,q,i | ASONPOSSNAP ruc,q, i | RUCOSFSNAP ruc,q, i | RUCSFSNAP ruc,q, i
100 | 0 | 0 | 0 | 100 | 200 | 100 | 0 | 100
Summary:
a) QSE is short by 100 MW for RRS-PFR.
b) QSE can support 100 MW of RRS-UFR but has a position of 100 MW of RRS-PFR.

## Slide 8: Example 3: QSE with GR has RRS-UFR Position
QSE Position for energy and AS, RTAML |  |  |  |  |  |  |  |  |  | 
Energy (MW) +ve Purchase -ve Sale | RU (MW) | RD (MW) | FFR (MW) | UFR (MW) | PFR (MW) | ECRSM (MW) | ECRSS (MW) | NSPINM (MW) | NSPINS (MW) | RTAML (MWh)
0 | 0 | 0 | 0 | 100 | 0 | 0 | 0 | 0 | 0 | 0
QSE Resources |  |  |  |  | 
Res. Type | HSL or MPC | LSL or LPC | Qual. PFR (MW) | ASMWCAPABILITY ruc,q,h,PFR,NCLR (MW) | ASMWCAPUSED ruc,q,h,PFR,NCLR (MW)
GR | 300 | 200 | 100 | 100 | 100
RUC Capacity Short Calc | RUC Capacity Short Calc |  |  |  |  |  |  | 
RUCASSFSNAP ruc,q,i | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h | RUCCAPSNAP ruc,q,i | ASONPOSSNAP ruc,q, i | RUCOSFSNAP ruc,q, i | RUCSFSNAP ruc,q, i
0 | 100 | 0 | 0 | 0 | 300 | 100 | 0 | 0
Summary:
a) QSE is NOT short.
b) QSE capability of 100 MW of RRS-PFR is used to cover QSE position of 100 MW of RRS-UFR.

## Slide 9: Example 4: QSE with GR has Reg-Dn, & RRS-PFR Position
QSE Position for energy and AS, RTAML |  |  |  |  |  |  |  |  |  | 
Energy (MW) +ve Purchase -ve Sale | RU (MW) | RD (MW) | FFR (MW) | UFR (MW) | PFR (MW) | ECRSM (MW) | ECRSS (MW) | NSPINM (MW) | NSPINS (MW) | RTAML (MWh)
0 | 0 | 30 | 0 | 0 | 100 | 0 | 0 | 0 | 0 | 0
QSE Resources |  |  |  |  |  |  |  | 
Res. Type | HSL or MPC | LSL or LPC | Qual. RD (MW) | Qual. PFR (MW) | ASMWCAPABILITY ruc,q,h,RD,GR (MW) | ASMWCAPUSED ruc,q,h,RD,GR (MW) | ASMWCAPABILITY ruc,q,h,PFR,GR (MW) | ASMWCAPUSED ruc,q,h,PFR,GR (MW)
GR | 300 | 200 | 100 | 100 | 100 | 30 | 100 | 70
RUC Capacity Short Calc | RUC Capacity Short Calc |  |  |  |  |  |  | 
RUCASSFSNAP ruc,q,i | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h | RUCCAPSNAP ruc,q,i | ASONPOSSNAP ruc,q, i | RUCOSFSNAP ruc,q, i | RUCSFSNAP ruc,q, i
30 | 300 | 0 | 0 | 0 | 300 | 100 | 0 | 30
Summary:
a) QSE is short by 30.
b) QSE has capability of 100 MW of RD and 100 MW of RRS-PFR but the HSL-LSL is 100 MW and cannot cover the total AS MW position of 130 MW

## Slide 10: Example 5: QSE with ESR has RRS-PFR Position
QSE Position for energy and AS, RTAML |  |  |  |  |  |  |  |  |  | 
Energy (MW) +ve Purchase -ve Sale | RU (MW) | RD (MW) | FFR (MW) | UFR (MW) | PFR (MW) | ECRSM (MW) | ECRSS (MW) | NSPINM (MW) | NSPINS (MW) | RTAML (MWh)
0 | 0 | 0 | 0 | 0 | 100 | 0 | 0 | 0 | 0 | 0
QSE Resources |  |  |  |  |  |  |  |  | 
Res. Type | HSL or MPC | LSL or LPC | Qual. FFR (MW) | Qual. PFR (MW) | Qual. ECRS (MW) | HBSOC (h) (MWh) | HBSOC (h+1) (MWh) | ASMWCAPABILITY ruc,q,h,PFR,ESR (MW) | ASMWCAPUSED ruc,q,h,PFR,ESR (MW)
ESR | 100 | -100 | 200 | 200 | 100 | 0 | 100 | 200 | 100
Summary:
QSE is short by 100 MW charging. The 100 MW charging required is not backed by MW Energy Purchase
RUC Capacity Short Calc | RUC Capacity Short Calc |  |  |  |  |  |  | 
RUCASSFSNAP ruc,q,i | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h | RUCCAPSNAP ruc,q,i | ASONPOSSNAP ruc,q, i | RUCOSFSNAP ruc,q, i | RUCSFSNAP ruc,q, i
0 | 0 | 100 | -100 | 0 | 0 | 100 | 100 | 100
All AS Deployment Factors = 1 except PFR Deployment Factor=0
FFR Duration = 0.25 hour
Energy, RU, RD, RRS-PFR, ECRS, NSPIN Duration = 1 hour

## Slide 11: Example 6: QSE with ESR has RRS-FFR, RRS-PFR, ECRSS Position
QSE Position for energy and AS, RTAML |  |  |  |  |  |  |  |  |  | 
Energy (MW) +ve Purchase -ve Sale | RU (MW) | RD (MW) | FFR (MW) | UFR (MW) | PFR (MW) | ECRSM (MW) | ECRSS (MW) | NSPINM (MW) | NSPINS (MW) | RTAML (MWh)
0 | 0 | 0 | 30 | 0 | 20 | 0 | 10 | 0 | 0 | 0
QSE Resources |  |  |  |  |  |  |  |  |  |  | 
Res. Type | HSL or MPC | LSL or LPC | Qual. FFR (MW) | Qual. PFR (MW) | Qual. ECRS (MW) | HBSOC (h) (MWh) | HBSOC (h+1) (MWh) | ASMWCAPABILITY ruc,q,h,FFR,ESR (MW) | ASMWCAPUSED ruc,q,h,FFR,ESR (MW) | ASMWCAPABILITY ruc,q,h,PFR,ESR (MW) | ASMWCAPUSED ruc,q,h,PFR,ESR (MW)
ESR | 100 | -100 | 200 | 200 | 100 | 100 | 50 | 200 | 30 | 200 | 20
Summary:
QSE is NOT short.
ASMWCAPABILITY ruc,q,h,ecr,ESR (MW) | ASMWCAPUSED ruc,q,h,ecr,ESR (MW)
100 | 10
RUC Capacity Short Calc | RUC Capacity Short Calc |  |  |  |  |  |  | 
RUCASSFSNAP ruc,q,i | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h | RUCCAPSNAP ruc,q,i | ASONPOSSNAP ruc,q, i | RUCOSFSNAP ruc,q, i | RUCSFSNAP ruc,q, i
0 | 0 | 60 | 12.5 | 0 | 72.5 | 60 | 0 | 0
All AS Deployment Factors = 1
FFR Duration = 0.25 hour
Energy, RU, RD, RRS-PFR, ECRS, NSPIN Duration = 1 hour

## Slide 12: Example 7: QSE with ESR has RRS-FFR, RRS-PFR, ECRSS Position
QSE Position for energy and AS, RTAML |  |  |  |  |  |  |  |  |  | 
Energy (MW) +ve Purchase -ve Sale | RU (MW) | RD (MW) | FFR (MW) | UFR (MW) | PFR (MW) | ECRSM (MW) | ECRSS (MW) | NSPINM (MW) | NSPINS (MW) | RTAML (MWh)
0 | 0 | 0 | 30 | 0 | 20 | 0 | 10 | 0 | 0 | 0
QSE Resources |  |  |  |  |  |  |  |  |  |  | 
Res. Type | HSL or MPC | LSL or LPC | Qual. FFR (MW) | Qual. PFR (MW) | Qual. ECRS (MW) | HBSOC (h) (MWh) | HBSOC (h+1) (MWh) | ASMWCAPABILITY ruc,q,h,FFR,ESR (MW) | ASMWCAPUSED ruc,q,h,FFR,ESR (MW) | ASMWCAPABILITY ruc,q,h,PFR,ESR (MW) | ASMWCAPUSED ruc,q,h,PFR,ESR (MW)
ESR | 100 | -100 | 200 | 200 | 100 | 100 | 70 | 200 | 30 | 200 | 20
Summary:
a) QSE is short by 7.5 MW. The difference in HBSOC combined with AS Deployment Factors is not sufficient to support QSE AS position
ASMWCAPABILITY ruc,q,h,ecr,ESR (MW) | ASMWCAPUSED ruc,q,h,ecr,ESR (MW)
100 | 2.5
RUC Capacity Short Calc | RUC Capacity Short Calc |  |  |  |  |  |  | 
RUCASSFSNAP ruc,q,i | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h | RUCCAPSNAP ruc,q,i | ASONPOSSNAP ruc,q, i | RUCOSFSNAP ruc,q, i | RUCSFSNAP ruc,q, i
7.5 | 0 | 52.5 | 0 | 0 | 52.5 | 60 | 7.5 | 7.5
All AS Deployment Factors = 1
FFR Duration = 0.25 hour
RU, RD, RRS-PFR, ECRS, NSPIN Duration = 1 hour