## Slide 1
Mitigated Offer Cap for On-Line Hydro Resources
ERCOT
RTC+B Task Force
03/19/2024

## Slide 2: Background
Key Principle 1.3 (3):
  On-Line hydro Generation Resources not operating in Synchronous Condenser Fast-Response mode will be able to maintain RRS, Non-Spin, and ECRS on those Resources through modification of the Mitigated Offer Cap (MOC).
Additional Details in Key Principle Appendix (KP1.3 100419 Combined Comments):
  Under RTC, On-Line hydro Generation Resources not operating in ONRR mode must adhere to constraints imposed by governmental agencies or by treaty regarding the operations of those Resources. These Resources often have the opportunity to provide incremental energy in response to a deployment of AS and are therefore good candidates to provide AS, but cannot regularly exchange the AS capacity for an incremental energy deployment. The MOC for On-Line hydro Generation Resources shall be set equal to the submitted Energy Offer Curve.

## Slide 3: Protocol Language
Section 4.4.9.4.1 (1)(d):
  For On-line hydro Generation Resources not operating in Synchronous Condenser Fast-Response mode, the MOC shall be adjusted in accordance with Verifiable Cost Manual, Appendix 12, Calculation of the Variable O&M Value and Incremental Heat Rate used in Real Time Mitigation for On-Line Hydro Generation Resources not operating in Synchronous Condenser Fast-Response mode.

## Slide 4: Proposal
Given that Hydro Resources operating in synchronous condenser mode are not dispatched by SCED, ERCOT proposes setting the MOC for all Hydro Resources to SWCAP.
  For ONRR Resources, SCED Base Points mirror Resource output (i.e., the Resources are “price-takers”).
  Reduces the complexity of the change and accomplishes the exact outcome desired in the Key Principle and discussion on Protocol changes.
Accomplished by the following:
  Setting the O&M value in the MOC to SWCAP.
  Setting the heat rate to 0 MMBtu/MWh.

## Slide 5: Next Steps
File VCMRR with proposed changes.
Modify language in Section 4.4.9.4.1 (1)(d) with the clean up NPRR.