## Slide 1
ERCOT Workshop
RTC+B: Additional RUC Capacity Short Examples
Sai Moorty
Market Design
March 17, 2024

## Slide 2: Scenarios:
Scenario 1: “ESR QSE has up AS responsibility net position in hour 1 (the RUC hour) and a down AS responsibility in the second hour, so its HBSOC is lower in the second hour.”
Scenario 2: “ESR is on in hour 1, but off in hour2, so the HBSOC is set to a positive value that covers its position in the RUC hour but has an HBSOC of 0 in the second hour.”
Clarification Notes:
In scenario 1, some of the words have been crossed out and replaced with more appropriate language. RUC Capacity Short calculations performed by ERCOT considers AS position at the QSE portfolio level and not at an individual Resource level. The calculations, factors in individual Resource capability in the QSE’s portfolio and minimizes, if any, the RUC shortfall.
In scenario 1, the HBSOC+1 (second hour HBSOC) does not necessarily have to be less than the previous hour’s HBSOC. The HBSOC+1 value depends on the AS deployment factors (6am Day-Ahead posting for each hour) and how the QSE is planning to operate given its AS (and energy) positions (based on DAM awards and trades for AS and energy). This is because an ESR can provide RegUp (or other upward AS) while charging (by reducing charging amount) and can provide RegDn while discharging (by reducing discharging amount).
Under RTC+B, an ESR status is either ON or OUT (no OFF available status – i.e. RUC cannot commit an ESR to be on-line as there is no OFF available status to commit)
For the hours an ESR status is OUT, the HBSOC is not necessarily zero. HBSOC is how much energy is stored in the ESR. Analogy is when one drives a car back from work and turns the ignition off, the car’s gas tank is not necessarily empty.

## Slide 3: Scenarios:
Clarification Notes: Continued
RUC will not commit an ESR (there is no OFF status for an ESR). RUC will self schedule an ESR to its COP submitted State of Charge (HBSOC) considering AS deployment Factors and system conditions while respecting the COP submitted MinSOC and MaxSOC values.
QSE submits COP data for the Resources in its portfolio (GR, LR, ESR) depending on how it plans to meet its QSE portfolio level net forward energy and net AS positions:
  DAM awards for energy and AS,
  Trades (purchase and sales) for energy and AS trades.
As time progresses, the QSE can update its Resource COP data if conditions change.

## Slide 4: Scenario 1 Examples
For simplicity, assume QSE has only one Resource which is an ESR.
ESR: +-10MW, 10 MWh, ESR gets WSL treatment (charging energy does not show up in RTAML)
Example 8a) QSE has 10 MW RegUp position in Hour X and a 10 MW RegDn position in Hour X+1. ESR provides RegUp in Hour X by injecting energy (discharge) and RegDn in Hour X+1 by withdrawing energy (charge)
RegUp and RegDn AS deployment Factors for Hour X and Hour X+1 are 1. Assume RegUp and RegDn duration requirements are 1 hour each.
COP Data:
Hour | HSL (MW) | LSL (MW) | MinSOC (MWh) | MaxSOC (MWh) | HBSOC (MWh) | RegUp Capability (MW) | RegDn Capability (MW)
X | 10 | -10 | 0 | 10 | 10 | 20 | 20
X+1 | 10 | -10 | 0 | 10 | 0 | 20 | 20
X+2 | 10 | -10 | 0 | 10 | 10 | 20 | 20
RUC Capacity Short Calc – Example shows that QSE is NOT short (RUCSFSNAP=0 for Hour X and Hour X+1) |  |  |  |  |  |  |  |  | 
Settl. Int. (15min) | RUCASSFSNAP ruc,q,I (MW) | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h (MW) | RUCCAPSNAP ruc,q,I (MW) | ASONPOSSNAP ruc,q, I (MW) | RUCOSFSNAP ruc,q, I (MW) | RUCSFSNAP ruc,q, I (MW)
All SI in Hour X | 0 | 0 | 10 | 0 | 0 | 10 | 10 | 0 | 0
All SI in Hour X+1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 5: Scenario 1 Examples
Example 8b) QSE has 10 MW RegUp position in Hour X and a 10 MW RegDn position in Hour X+1. In addition, QSE has a net energy purchase of 4 MW for Hour X. ESR provides RegUp in Hour X and RegDn in Hour X+1, both, by withdrawing energy (charging)
RegUp and RegDn AS deployment Factors for Hour X and Hour X+1 are 1. Assume RegUp and RegDn duration requirements are 1 hour each.
COP Data:
Hour | HSL (MW) | LSL (MW) | MinSOC (MWh) | MaxSOC (MWh) | HBSOC (MWh) | RegUp Capability (MW) | RegDn Capability (MW)
X | 10 | -10 | 0 | 10 | 6 | 20 | 20
X+1 | 10 | -10 | 0 | 10 | 0 | 20 | 20
X+2 | 10 | -10 | 0 | 10 | 10 | 20 | 20
RUC Capacity Short Calc – Example shows that QSE is NOT short (RUCSFSNAP=0 for Hour X and Hour X+1) |  |  |  |  |  |  |  |  | 
Settl. Int. (15min) | RUCASSFSNAP ruc,q,i | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h | RUCCAPSNAP ruc,q,i | ASONPOSSNAP ruc,q, i | RUCOSFSNAP ruc,q, i | RUCSFSNAP ruc,q, i
All SI in Hour X | 0 | 0 | 10 | -4 | 0 | 10 | 10 | 0 | 0
All SI in Hour X+1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 6: Scenario 2 Examples
For simplicity, assume QSE has only one Resource which is an ESR.
ESR: +-10MW, 10 MWh, ESR gets WSL treatment (charging energy does not show up in RTAML)
Example 9a) QSE has 10 MW RegUp position in Hour X and ESR is OUT in Hour X+1. ESR provides RegUp in Hour X by injecting energy (discharge)
RegUp AS deployment Factors for Hour X is 1. Assume RegUp duration requirement is 1 hour.
COP Data:
Hour | HSL (MW) | LSL (MW) | MinSOC (MWh) | MaxSOC (MWh) | HBSOC (MWh) | RegUp Capability (MW) | RegDn Capability (MW)
X | 10 | -10 | 0 | 10 | 10 | 20 | 20
X+1 (OUT status) | 10 | -10 | 0 | 10 | 0 | 20 | 20
RUC Capacity Short Calc – Example shows that QSE is NOT short (RUCSFSNAP=0 for Hour X) |  |  |  |  |  |  |  |  | 
Settl. Int. (15min) | RUCASSFSNAP ruc,q,i | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h | RUCCAPSNAP ruc,q,i | ASONPOSSNAP ruc,q, i | RUCOSFSNAP ruc,q, i | RUCSFSNAP ruc,q, i
All SI in Hour X | 0 | 0 | 10 | 0 | 0 | 10 | 10 | 0 | 0

## Slide 7: Scenario 2 Examples
For simplicity, assume QSE has only one Resource which is an ESR.
ESR: +-10MW, 10 MWh, ESR gets WSL treatment (charging energy does not show up in RTAML)
Example 9b) QSE has 10 MW RegUp position in Hour X and ESR is OUT in Hour X+1. In addition, QSE has a net energy purchase of 4 MW for Hour X. ESR provides RegUp in Hour X by withdrawing energy (charging)
RegUp AS deployment Factors for Hour X is 1. Assume RegUp duration requirement is 1 hour.
COP Data:
Hour | HSL (MW) | LSL (MW) | MinSOC (MWh) | MaxSOC (MWh) | HBSOC (MWh) | RegUp Capability (MW) | RegDn Capability (MW)
X | 10 | -10 | 0 | 10 | 6 | 20 | 20
X+1 (OUT status) | 10 | -10 | 0 | 10 | 0 | 20 | 20
RUC Capacity Short Calc – Example shows that QSE is NOT short (RUCSFSNAP=0 for Hour X) |  |  |  |  |  |  |  |  | 
Settl. Int. (15min) | RUCASSFSNAP ruc,q,i | RCAPSNAP ruc,q,h (MW) | ESRASSNAP ruc,q,h (MW) | ESRMWSNAP ruc,q,h (MW) | ASOFRLRSNAP ruc,q,h | RUCCAPSNAP ruc,q,i | ASONPOSSNAP ruc,q, i | RUCOSFSNAP ruc,q, i | RUCSFSNAP ruc,q, i
All SI in Hour X | 0 | 0 | 10 | -4 | 0 | 10 | 10 | 0 | 0